KERMIT PROTOCOL MANUAL

                                 Sixth Edition



                                 Frank da Cruz

              Columbia University Center for Computing Activities
                           New York, New York 10027


                                   June 1986






                            Copyright (C) 1981,1986
            Trustees of Columbia University in the City of New York

       Permission is granted to any individual or institution to copy or
        use this document and the programs described in it, except for
                        explicitly commercial purposes.


                         PREFACE TO THE SIXTH EDITION

The sixth edition (June 1986) of the Kermit Protocol Manual is being issued for
two major reasons: to correct minor errors in the fifth edition, and to include
new  sections  on  two major protocol extensions: long packets and sliding win-
dows.  No attempt has been made to reorganize, rewrite,  or  otherwise  improve
the  protocol  manual.    The Kermit protocol has been presented in an entirely
different -- hopefully more thorough, organized, coherent, and useful  (if  not
more  formal)  --  manner  in  the book, "Kermit, A File Transfer Protocol," by
Frank da Cruz, Digital Press, Bedford MA (1987), ISBN 0-932376-88-6, DEC  order
number EY-6705E-DP.  If you have the book, you won't need this protocol manual.
On the other hand, if you don't have the book, this manual should still contain
all  the necessary information.  The Kermit Protocol Manual will continue to be
freely distributed in perpetuity.

The bare-bones C-language Kermit program that appeared as an appendix  in  pre-
vious editions has been removed.  It was not a particularly good example of how
to write a Kermit program, and made the manual unnecessarily thick.  For sample
Kermit  programs,  see  the  source  code for any of the hundreds of Kermit im-
plementations, or follow the program fragments in the book.


                         PREFACE TO THE FIFTH EDITION

The fifth edition (March 1984) attempts to clarify some fine  points  that  had
been  left  ambiguous in the 4th edition, particularly with respect to when and
how prefix encoding is done, and when it is not, and  about  switching  between
block  check  types.   A mechanism is suggested (in the Attributes section) for
file archiving, and several attributes have been  rearranged  and  some  others
added  (this should do no harm, since no one to date has attempted to implement
the attributes packet).  A more complete protocol state table  is  provided,  a
few minor additions are made to the collection of packet types.


                         PREFACE TO THE FOURTH EDITION

The  fourth  edition (November 1983) of the Kermit Protocol Manual incorporates
some new ideas that grew from our experience in attempting to implement some of
the features described in earlier editions, particularly user/server functions.
These include a mechanism to allow batch transfers to be interrupted gracefully
for  either the current file or the entire batch of files; a "capability mask";
a protocol extension for passing file attributes.  In addition, numbers are now
written  in  decimal  notation  rather  than octal, which was confusing to many
readers.  Also, several incompatible changes were made in minor areas where  no
attempts at an implementation had yet been made; these include:

   - The format and interpretation of the operands to the server commands.

   - Usurpation  of the reserved fields 10-11 of the Send-Init packet, and
     addition of new reserved fields.

Most of the remaining material has been rewritten and reorganized, and much new
material  added, including a section on the recommended vocabulary for documen-
tation and commands.

The previous edition of the Protocol Manual attempted to define "protocol  ver-
sion  3";  this  edition abandons that concept.  Since Kermit development is an
unorganized, disorderly, distributed enterprise, no requirement can be  imposed
on  Kermit  implementors  to include a certain set of capabilities in their im-
plementations.  Rather,  in  this  edition  we  attempt  to  define  the  basic
functionality of Kermit, and then describe various optional functions.

The  key  principle  is  that any implementation of Kermit should work with any
other, no matter how advanced the one or how primitive the other.  The capabily
mask and other Send-Init fields attempt to promote this principle.



                               ACKNOWLEDGEMENTS

Bill  Catchings and I designed the basic Kermit protocol at Columbia University
in 1981.  For ideas, we looked at some of the ANSI models (X3.57,  X3.66),  the
ISO OSI model, some real-world "asynchronous protocols" (including the Stanford
Dialnet and TTYFTP projects, the University of Utah Small FTP project), as well
as at file transfer on full-blown networks like DECnet and ARPAnet.

Bill  wrote  the  first  two  programs  to  implement the protocol, one for the
DEC-20, one for a CP/M-80 microcomputer, and in the process worked out most  of
the details and heuristics required for basic file transfer.  Meanwhile, Daphne
Tzoar and Vace Kundakci, also of Columbia, worked out  the  additional  details
necessary  for IBM mainframe communication, while writing IBM VM/CMS and PC-DOS
versions.

Much credit should also go to Bernie Eiben of Digital Equipment Corporation for
promoting  widespread  use  of  Kermit and for adding many insights into how it
should operate, to Nick Bush and Bob McQueen of Stevens Institute  of  Technol-
ogy,  for  many  contributions to the "advanced" parts of the protocol, and for
several major Kermit implementations, and to Leslie Spira and her group at  The
Source  Telecomputing  for  adding full-duplex sliding window capability to the
Kermit protocol.

Thanks to the many people all over the world who have  contributed  new  Kermit
implementations,  who have helped with Kermit distribution through various user
groups, and who have contributed to the quality of the protocol  and  its  many
implementations  by  reporting  or  fixing problems, criticizing the design, or
suggesting new features.  In particular, thanks to Ted Toal of Nevada City, CA,
for a detailed list of corrections to the fifth edition of this manual.

And  above  all,  thanks  to  Christine  Gianone for taking charge of Kermit at
Columbia; for keeping it alive, healthy, and strong; for promoting its develop-
ment  and  use  all  over  the  world;  for setting its tone and direction; for
fostering its spirit.  Without her guidance  and  perserverance,  Kermit  might
have faded from the scene years ago.

The  Kermit  protocol  was  named after Kermit the Frog, star of the television
series THE MUPPET SHOW.  The name is used by permission of  Henson  Associates,
Inc., New York City.


                                  DISCLAIMER

No  warranty of the software nor of the accuracy of the documentation surround-
ing it is expressed or implied, and neither the authors nor Columbia University
acknowledge any liability resulting from program or documentation errors.

1. Introduction

This manual describes the  Kermit  protocol.  It is assumed that you understand
the purpose and operation of the Kermit file transfer  facility,  described  in
the  Kermit  Users Guide, and basic terminology of data communications and com-
puter programming.


1.1. Background

The Kermit file transfer protocol is intended for use in an  environment  where
there  may  be  a  diverse  mixture of computers -- micros, personal computers,
workstations, laboratory computers, timesharing systems -- from  a  variety  of
manufacturers.    All  these systems need have in common is the ability to com-
municate in ASCII over ordinary serial telecommunication lines.

Kermit was originally designed at Columbia University to meet the need for file
transfer  between  our  DECSYSTEM-20  and IBM 370-series mainframes and various
microcomputers.  It turned out that the diverse characteristics of these  three
kinds of systems resulted in a design that was general enough to fit almost any
system.  The IBM mainframe, in  particular,  strains  most  common  assumptions
about how computers communicate.

1.2. Overview

The  Kermit  protocol is specifically designed for character-oriented transmis-
sion over serial telecommunication lines.  The design allows for  the  restric-
tions and peculiarities of the medium and the requirements of diverse operating
environments -- buffering, duplex, parity, character  set,  file  organization,
etc.   The protocol is carried out by Kermit programs on each end of the serial
connection sending "packets" back and forth; the sender sends file names,  file
contents,  and  control  information;  the receiver acknowledges (positively or
negatively) each packet.

The packets have a layered design, more or less in keeping with  the  ANSI  and
ISO  philosophies,  with  the  outermost  fields used by the data link layer to
verify data integrity, the next by the session layer to verify continuity,  and
the data itself at the application level.

Connections between systems are established by the ordinary user.  In a typical
case, the user runs Kermit on a microcomputer, enters terminal emulation,  con-
nects  to  a remote host computer (perhaps by dialing up), logs in, runs Kermit
on the remote host, and then issues commands to that Kermit  to  start  a  file
transfer,  "escapes"  back  to the micro, and issues commands to that Kermit to
start its side of the file transfer.  Files may be  transferred  singly  or  in
groups.

Basic  Kermit  provides only file transfer, and that is provided for sequential
files only, though the protocol attempts to allow for various types of  sequen-
tial  files.    Microcomputer  implementations  of  Kermit are also expected to
provide terminal emulation, to facilitate the initial connection.

More advanced implementations simplify the "user interface" somewhat by  allow-
ing  the  Kermit  on  the  remote host to run as a "server", which can transfer
files in either direction upon command from the local "user" Kermit.  The serv-
er  can  also  provide  additional functionality, such as file management, mes-
sages, mail, and so forth.  Other optional features  also  exist,  including  a
variety  of  block  check  types,  a mechanism for passing 8-bit data through a
7-bit communication link, a way to compressing a repeated sequence  of  charac-
ters, and so forth.

As  local area networks become more popular, inexpensive, and standardized, the
demand for Kermit and similar protocols may dwindle, but will never wither away
entirely.   Unlike hardwired networks, Kermit gives the ordinary user the power
to establish reliable error-free connections between any  two  computers;  this
may always be necessary for one-shot or long-haul connections.

1.3. General Terminology

TTY:  This  is the term commonly used for a device which is connected to a com-
puter over an EIA RS-232 serial telecommunication line.  This  device  is  most
commonly  an  ASCII  terminal,  but  it  may be a microcomputer or even a large
multi-user computer emulating  an  ASCII  terminal.    Most  computers  provide
hardware (RS-232 connectors and UARTs) and software (device drivers) to support
TTY connections; this is what makes TTY-oriented file transfer  protocols  like
Kermit possible on almost any system at little or no cost.

LOCAL:  When two machines are connected, the LOCAL machine is the one which you
interact with directly, and which is in control of the terminal.    The  "local
Kermit"  is the one that runs on the local machine.  A local Kermit always com-
municates over an external device (the micro's communication port, an  assigned
TTY line, etc).

REMOTE:  The REMOTE machine is the one on the far side of the connection, which
you must interact with "through" the local machine.  The "remote  Kermit"  runs
on the remote machine.  A remote Kermit usually communicates over its own "con-
sole", "controlling terminal", or "standard i/o" device.

HOST: Another word for "computer", usually meaning a computer that can  provide
a home for multiple users or applications.  This term should be avoided in Ker-
mit lore, unless preceded immediately by LOCAL or REMOTE, to denote which  host
is meant.

SERVER:  An  implementation of remote Kermit that can accept commands in packet
form from a local Kermit program, instead of directly from the user.

USER: In addition to its usual use to denote  the  person  using  a  system  or
program,  "user"  will also be used refer to the local Kermit program, when the
remote Kermit is a server.

1.4. Numbers

All numbers in the following text are expressed in decimal (base  10)  notation
unless otherwise specified.

Numbers  are  also  referred  to  in terms of their bit positions in a computer
word.  Since Kermit may be implemented on computers with various word sizes, we
start  numbering  the  bits from the "right" -- bit 0 is the least significant.
Bits 0-5 are the 6 least significant bits; if they were all  set  to  one,  the
value would be 63.

A  special  quirk  in  terminology,  however, refers to the high order bit of a
character as it is transmitted on the communication line,  as  the  "8th  bit".
More  properly, it is bit 7, since we start counting from 0.  References to the
"8th bit" generally are with regard to that bit which ASCII  transmission  sets
aside  for  use  as a parity bit.  Kermit concerns itself with whether this bit
can be usurped for the transmission of data, and  if  not,  it  may  resort  to
"8th-bit prefixing".

1.5. Character Set

All  characters  are in ASCII  (American national Standard Code for Information
Interchange) representation, ANSI standard X3.4-1968.  All  implementations  of
Kermit  transmit and receive characters only in ASCII.  The ASCII character set
is listed in Appendix III.

ASCII character mnemonics:

NUL     Null, idle, ASCII character 0.
SOH     Start-of-header, ASCII character 1 (Control-A).
SP      Space, blank, ASCII 32.
CR      Carriage return, ASCII 13 (Control-M).
LF      Linefeed, ASCII 10 (Control-J).
CRLF    A carriage-return linefeed sequence.
DEL     Delete, rubout, ASCII 127.

A control character is considered to be any byte whose low order 7 bits are  in
the  range 0 through 31, or equal to 127.  In this document, control characters
are written in several ways:

Control-A
        This  denotes  ASCII  character 1, commonly referred to as "Control-A".
        Control-B is ASCII character 2, and so forth.

CTRL-A  This is a common abbreviation for "Control-A".  A control character  is
        generally  typed  at a computer terminal by holding down the key marked
        CTRL and pressing the corresponding alphabetic character, in this  case
        "A".

^A      "Uparrow"  notation  for  CTRL-A.  Many computer systems "echo" control
        characters in this fashion.

A printable ASCII character is considered to be any character in the  range  32
(SP) through 126 (tilde).

1.6. Conversion Functions

Several  conversion functions are useful in the description of the protocol and
in the program example.  The machine that Kermit runs on need operate  only  on
integer data; these are functions that operate upon the numeric value of single
ASCII characters.

tochar(x) = x+32
    Transforms  the  integer  x,  which is assumed to lie in the range 0 to 94,
    into a printable ASCII character; 0 becomes SP, 1 becomes  "!",  3  becomes
    "#", etc.

unchar(x) = x-32
    Transforms the character x, which is assumed to be in the  printable  range
    (SP through tilde), into an integer in the range 0 to 94.

ctl(x) = x XOR 64
    Maps  between  control  characters  and  their  printable  representations,
    preserving the high-order bit.  If x is a control character, then

        x = ctl(ctl(x))

    that  is,  the same function is used to controllify and uncontrollify.  The
    argument is assumed to be a true control character (0 to 31,  or  127),  or
    the  result  of  applying  CTL to a true control character (i.e. 63 to 95).
    The transformation is a mnemonic one -- ^A becomes A and vice versa.

1.7. Protocol Jargon

A Packet is a clearly delimited string of  characters,  comprised  of  "control
fields" nested around data; the control fields allow a Kermit program to deter-
mine whether the data has been transmitted correctly and completely.  A  packet
is the unit of transmission in the Kermit protocol.

ACK  stands  for "Acknowledge".  An ACK is a packet that is sent to acknowledge
receipt of another packet.  Not to be confused with the ASCII character ACK.

NAK stands for "Negative Acknowledge".  A NAK is a packet sent to  say  that  a
corrupted  or incomplete packet was received, the wrong packet was received, or
an expected packet was not received.  Not to be confused with the ASCII charac-
ter NAK.

A  timeout is an event that can occur if expected data does not arrive within a
specified amount of time.  The program generating the input request can  set  a
"timer  interrupt"  to  break  it out of a nonresponsive read, so that recovery
procedures may be activated.


2. Environment

2.1. System Requirements

The Kermit protocol requires that:

   - The host can send and receive characters using 7- or 8-bit ASCII  en-
     coding  over  an  EIA RS-232 physical connection, either hardwired or
     dialup.

   - All printable ASCII characters are acceptable as input  to  the  host
     and  will  not  be  transformed  in any way[If they are translated to
     another character set, like EBCDIC, the Kermit program must  be  able
     to  reconstruct  the packet as it appeared on the communication line,
     before transformation.].  Similarly, any intervening network or  com-
     munications   equipment   ("smart  modems",  TELENET,  terminal  con-
     centrators, port selectors, etc) must not transform  or  swallow  any
     printable ASCII characters.

   - A  single  ASCII  control  character  can pass from one system to the
     other without transformation.  This  character  is  used  for  packet
     synchronization.  The character is normally Control-A (SOH, ASCII 1),
     but can be redefined.

   - If a host requires a line terminator for terminal  input,  that  ter-
     minator  must  be a single ASCII control character, such as CR or LF,
     distinct from the packet synchronization character.

   - When using a job's controlling terminal for file transfer, the system
     must  allow  the  Kermit  program to set the terminal to no echo, in-
     finite width (no "wraparound" or CRLF insertion by the operating sys-
     tem), and no "formatting" of incoming or outgoing characters (for in-
     stance, raising lowercase letters to uppercase, transforming  control
     characters to printable sequences, etc).  In short, the terminal must
     be put in "binary" or "raw" mode, and, hopefully, restored afterwards
     to normal operation.

   - The  host's terminal input processor should be capable of receiving a
     single burst of 40 to 100 characters at normal  transmission  speeds.
     This is the typical size of packet.

Note  that  most  of  these requirements rule out the use of Kermit through IBM
3270 / ASCII protocol converters, except those (like the Series/1 or 7171  run-
ning the Yale ASCII package) that can be put in "transparant mode."

Kermit does not require:

   - That the connection run at any particular baud rate.

   - That  the  system can do  XON/XOFF or any other kind of flow control.
     System- or hardware-level flow control can help, but it's not  neces-
     sary.  See section 3.7.

   - That  the system is capable of full duplex operation.  Any mixture of
     half and full duplex systems is supported.

   - That the system can transmit or receive 8-bit  bytes.    Kermit  will
     take advantage of 8-bit connections to send binary files; if an 8-bit
     connection is not possible, then binary files may be  sent  using  an
     optional prefix encoding.


2.2. Printable Text versus Binary Data

For  transmission  between  unlike systems, files must be assigned to either of
two catagories: printable text or binary.

A printable text file is one that can make sense on an unlike system -- a docu-
ment,  program  source,  textual data, etc.  A binary file is one that will not
(and probably can not) make sense on an unlike system -- an executable program,
numbers stored in internal format, etc.  On systems with 8-bit bytes, printable
ASCII files will have the high order bit of each byte  set  to  zero(There  are
some  exceptions,  such as systems that store text files in so-called "negative
ASCII", or text files produced by word processors that use the high  order  bit
to  indicate  underline or boldface attributes.)  (since ASCII is a 7-bit code)
whereas binary files will use the high order bit of  each  byte  for  data,  in
which case its value can vary from byte to byte.

Many  computers  have no way to distinguish a printable file from a binary file
-- especially one originating from an unlike system -- so the user may have  to
give  an explicit command to Kermit to tell it whether to perform these conver-
sions.

2.2.1. Printable Text Files

A primary goal of Kermit is for printable text files to be useful on the target
system after transfer.  This requires a standard representation for text during
transmission.  Kermit's standard is simple: 7-bit ASCII characters, with "logi-
cal  records"  (lines) delimited by CRLFs.  It is the responsibility of systems
that do not store printable files in this fashion to perform the necessary con-
versions  upon  input  and  output.    For instance, IBM mainframes might strip
trailing blanks on output and add them back on input; UNIX would prepend  a  CR
to its normal record terminator, LF, upon output and discard it upon input.  In
addition, IBM mainframes must do EBCDIC/ASCII translation for text files.

No other conversions (e.g. tab expansion) are performed upon text files.   This
representation  is  chosen  because  it  corresponds  to the way text files are
stored on most microcomputers and on many other systems.  In many common cases,
no transformations are necessary at all.

2.2.2. Binary Files

Binary files are transmitted as though they were a sequence of characters.  The
difference from printable files is that the status of the  "8th  bit"  must  be
preserved.  When binary files are transmitted to an unlike system, the main ob-
jective is that they can be brought back to the original system  (or  one  like
it)  intact;  no special conversions should be done during transmission, except
to make the data fit the transmission medium.

For binary files, eight bit character transmission is permissible  as  long  as
the  two  Kermit programs involved can control the value of the parity bit, and
no intervening communications equipment will change its value.  In  that  case,
the  8th  bit  of  a transmitted character will match that of the original data
byte, after any control-prefixing has been done.  When one or both sides cannot
control  the  parity  bit,  a  special  prefix  character  may  be inserted, as
described below.

Systems that do not store binary data in 8-bit bytes, or whose word size is not
a  multiple  of 8, may make special provisions for "image mode" transfer of bi-
nary files.  This may be done within the basic protocol by having the two sides
implicitly  agree  upon  a  scheme  for packing the data into 7- or 8-bit ASCII
characters, or else the more flexible (but optional)  file  attributes  feature
may  be  used.    The  former method is used on PDP-10 36-bit word machines, in
which text is stored five 7-bit bytes per word; the value of the "odd  bit"  is
sent as the parity bit of every 5th word.

3. File Transfer

The file transfer protocol takes place over a transaction.  A transaction is an
exchange of packets beginning with a Send-Init (S) packet, and  ending  with  a
Break  Transmission  (B)  or Error (E) packet(A transaction should also be con-
sidered terminated when one side or the other has stopped  without  sending  an
Error  packet.),  and may include the transfer of one or more files, all in the
same direction.  In order to minimize the unforseen, Kermit packets do not con-
tain  any control characters except one specially designated to mark the begin-
ning of a packet.  Except for the packet marker, only printable characters  are
transmitted.   The following sequence characterizes basic Kermit operation; the
sender is the machine that is  sending  files;  the  receiver  is  the  machine
receiving the files.

   1. The  sender  transmits  a  Send-Initiate  (S)  packet to specify its
      parameters (packet length, timeout, etc; these are explained below).

   2. The receiver sends an ACK (Y) packet, with its own parameters in the
      data field.

   3. The  sender  transmits  a File-Header (F) packet, which contains the
      file's name in the data field.  The receiver ACKs the F packet, with
      no data in the data field of the ACK (optionally, it may contain the
      name under which the receiver will store the file).

   4. The sender sends the contents of the file, in Data (D) packets.  Any
      data not in the printable range is prefixed and replaced by a print-
      able equivalent.  Each D packet is acknowledged before the next  one
      is sent.

   5. When  all  the  file data has been sent, the sender sends an End-Of-
      File (Z) packet.  The receiver ACKs it.

   6. If there is another file to send, the process is repeated  beginning
      at step 3.

   7. When  no  more files remain to be sent, the sender transmits an End-
      Of-Transmission (B) packet.  The receiver ACKs it.   This  ends  the
      transaction, and closes the logical connection (the physical connec-
      tion remains open).

Each packet has a sequence number, starting with 0 for the Send Init.  The ack-
nowledgment  (ACK or NAK) for a packet has the same packet number as the packet
being acknowledged.  Once an acknowledgment is successfully received the packet
number is increased by one, modulo 64.

If  the  sender  is remote, it waits for a certain amount of time (somewhere in
the 5-30 second range) before transmitting the Send-Init, to give the user time
to escape back to the local Kermit and tell it to receive files.

Each  transaction  starts fresh, as if no previous transaction had taken place.
For example, the sequence number is set back to zero, and parameters are  reset
to their default or user-selected values.

3.1. Conditioning the Terminal

Kermit is most commonly run with the user sitting at a microcomputer, connected
through a communications port to a remote timesharing system.  The remote  Ker-
mit is using its job's own "controlling terminal" for file transfer.  While the
microcomputer's port is an ordinary device,  a  timesharing  job's  controlling
terminal  is  a special one, and often performs many services that would inter-
fere with normal operation of Kermit.  Such services include echoing  (on  full
duplex systems), wrapping lines by inserting carriage return linefeed sequences
at the terminal width, pausing at the end of a screen or  page  full  of  text,
displaying  system  messages, alphabetic case conversion, control character in-
tepretation, and so forth.  Mainframe Kermit programs  should  be  prepared  to
disable  as  many  of  these  services  as possible before packet communication
begins, and to restore them to their original condition at the end of a  trans-
action.   Disabling these services is usually known as "putting the terminal in
binary mode."

Kermit's use  of  printable  control  character  equivalents,  variable  packet
lengths,  redefinable markers and prefixes, and allowance for any characters at
all to appear between packets with no adverse effects provide a great  deal  of
adaptability for those systems that do not allow certain (or any) of these fea-
tures to be disabled.

3.2. Timeouts, NAKs, and Retries

If a Kermit program is capable of setting a timer interrupt, or setting a  time
limit on an input request, it should do so whenever attempting to read a packet
from the communication line, whether sending or receiving files.  Having read a
packet, it should turn off the timer.

If the sender times out waiting for an acknowledgement, it should send the same
packet again, repeating the process a certain number of times  up  to  a  retry
limit,  or  until  an  acknowledgement  is received.  If the receiver times out
waiting for a packet, it can send either a NAK packet for the  expected  packet
or another ACK for the last packet it got.  The latter is preferred.

If  a  packet from the sender is garbled or lost in transmission (the latter is
detected by a timeout, the former by a bad checksum), the receiver sends a  NAK
for  the  garbled  or  missing packet.  If an ACK or a NAK from the receiver is
garbled or lost, the sender ignores it; in that case, one  side  or  the  other
will time out and retransmit.

A  retry  count  is  maintained,  and  there is a retry threshold, normally set
around 5.  Whenever a packet is resent -- because of a timeout, or  because  it
was  NAK'd  --  the counter is incremented.  When it reaches the threshold, the
transaction is terminated and the counter reset.

If neither side is capable of timing out, a facility  for  manual  intervention
must  be  available on the local Kermit.  Typically, this will work by sampling
the keyboard (console) periodically; if input, such as a CR, appears, then  the
same  action  is  taken as if a timeout had occurred.  The local Kermit keeps a
running display of the packet number or byte count on the screen to  allow  the
user  to  detect  when traffic has stopped.  At this point, manual intervention
should break the deadlock.

Shared systems which can become sluggish when heavily used should adjust  their
own  timeout intervals on a per-packet basis, based on the system load, so that
file transfers won't fail simply because the system was too slow.

Normally, only one side should be doing timeouts, preferably the side with  the
greatest  knowledge  of  the  "environment"  --  system load, baud rate, and so
forth, so as to optimally adjust the timeout interval for each packet.  If both
sides  are  timing  out, their intervals should differ sufficiently to minimize
collisions.

3.3. Errors

During file transfer, the sender may encounter an i/o error on the disk, or the
receiver  may  attempt  to write to a full or write-protected device.  Any con-
dition that will prevent successful transmission of the file is called a "fatal
error".    Fatal  errors  should be detected, and the transfer shut down grace-
fully, with the pertinent information provided to  the  user.    Error  packets
provide a mechanism to do this.

If  a fatal error takes place on either the sending or receiving side, the side
which encountered the error should send an Error (E) packet.  The E packet con-
tains  a  brief  textual  error message in the data field.  Both the sender and
receiver should be prepared to receive an Error packet at any time  during  the
transaction.   Both the sender and receiver of the Error packet should halt, or
go back into into user command mode (a server should return to  server  command
wait).  The side that is local should print the error message on the screen.

There  is no provision for sending nonfatal error messages, warnings, or infor-
mation messages during a transaction.  It would be possible to add such a  fea-
ture,  but  this  would require both sides agree to use it through setting of a
bit in the capability mask, since older Kermits that did not know about such  a
feature would encounter an unexpected packet type and would enter the fatal er-
ror state.  In any case, the utility of such a feature is  questionable,  since
there is no guarantee that the user will be present to see such messages at the
time they are sent; even if they are saved up for later perusal in  a  "message
box", their significance may be long past by the time the user reads them.  See
the section on Robustness, below.

3.4. Heuristics

During any transaction, several heuristics are useful:

   1. A NAK for the current packet is equivalent to an ACK  for  the  pre-
      vious  packet  (modulo  64).    This handles the common situation in
      which a packet is successfully received, and then ACK'd, but the ACK
      is lost.  The ACKing side then times out waiting for the next packet
      and NAKs it.  The side that receives a  NAK  for  packet  n+1  while
      waiting for an ACK for packet n simply sends packet n+1.

   2. If  packet  n  arrives more than once, simply ACK it and discard it.
      This can happen when the first ACK was lost.  Resending the  ACK  is
      necessary  and  sufficient -- don't write the packet out to the file
      again!

   3. When opening a connection, discard the contents of the line's  input
      buffer  before  reading  or sending the first packet.  This is espe-
      cially important if the other side is in receive mode (or acting  as
      a  server), in which case it may have been sending out periodic NAKs
      for your expected SEND-INIT or command packet.    If  you  don't  do
      this,  you  may  find  that there are sufficient NAKs to prevent the
      transfer -- you send a Send-Init, read the response, which is an old
      NAK,  so  you  send another Send-Init, read the next old NAK, and so
      forth, up to the retransmission limit, and give up before getting to
      the  ACKs  that are waiting in line behind all the old NAKs.  If the
      number of NAKs is below the cutoff, then each packet may  be  trans-
      mitted multiply.

   4. Similarly, before sending a packet, you should clear the input buff-
      er (after looking for any required handshake character).  Failure to
      clear  the buffer could result in propogation of the repetition of a
      packet caused by stacked-up NAKs.

   5. If an ACK arrives for a packet that has already been  ACK'd,  simply
      ignore  the redundant ACK and wait for the next ACK, which should be
      on its way.

3.5. File Names

The syntax for file names can vary widely from system  to  system.    To  avoid
problems,  it is suggested that filenames be represented in the File Header (F)
packet in a "normal form", by default (that is, there should be  an  option  to
override such conversions).

   1. Delete  all  pathnames  and  attributes from the file specification.
      The file header packet should not contain directory or device names;
      if  it  does, it may cause the recipient to try to store the file in
      an inaccessible or nonexistent area, or it  may  result  in  a  very
      strange filename.

   2. After  stripping  any  pathname,  convert  the remainder of the file
      specification to the form "name.type", with no restriction on length
      (except that it fit in the data field of the F packet), and:

         a. Include no more than one dot.
         b. Not begin or end with a dot.
         c. The name and type fields contain digits and uppercase letters.

Special  characters like "$", "_", "-", "&", and so forth should be disallowed,
since they're sure to cause problems on one system or another.

The recipient, of course, cannot depend upon the sender to follow this  conven-
tion,  and should still take precautions.  However, since most file systems em-
body the notion of a file name and a file  type,  this  convention  will  allow
these items to be expressed in a way that an unlike system can understand.  The
particular notation is chosen simply because it is the most common.

The recipient must worry about the length of the name and type  fields  of  the
file  name.    If  either  is  too long, they must be truncated.  If the result
(whether truncated or not) is the same as the name of a file that  already  ex-
ists  in the same area, the recipient should have the ability to take some spe-
cial action to avoid writing over the original file.

Kermit implementations that convert  file  specifications  to  normal  form  by
default  should  have  an  option to override this feature.  This would be most
useful when transferring files between like systems, perhaps used  in  conjunc-
tion with "image mode" file transfer.  This could allow, for instance, one UNIX
system to send an entire directory tree to another UNIX system.

3.6. Robustness

A major feature of the Kermit protocol is  the  ability  to  transfer  multiple
files.    Whether  a particular Kermit program can actually send multiple files
depends on the capabilities of the program and the host operating  system  (any
Kermit program can receive multiple files).

If  a  Kermit  program can send multiple files, it should make every attempt to
send the entire group specified.  If it fails to send  a  particular  file,  it
should  not  terminate the entire batch, but should go on the the next one, and
proceed until an attempt has been made to send each file in the group.

Operating in this robust manner, however, gives rise to  a  problem:  the  user
must  be  notified of a failure to send any particular file.  Unfortunately, it
is not sufficient to print a message to the screen since the user  may  not  be
physically  present.   A better solution would be to have the sender optionally
keep a log of the  transaction, giving the name of each file for which  an  at-
tempt was made, and stating whether the attempt was successful, and if not, the
reason.  Additional aids to robustness are described in the  Optional  Features
section, below.

3.7. Flow Control

On full duplex connections, XON/XOFF flow control can generally be used in con-
junction with Kermit file transfer with no ill effects.  This is because  XOFFs
are  sent  in the opposite direction of packet flow, so they will not interfere
with the packets themselves.  XON/XOFF, therefore, need not be  implemented  by
the  Kermit  program,  but  can  done  by  the host system.  If the host system
provides this capability, it should be  used  --  if  both  sides  can  respond
XON/XOFF  signals,  then  buffer  overruns  and  the  resulting  costly  packet
retransmissions can be avoided.

Beware, however, of the following situation: remote Kermit is sending  periodic
NAKs, local system is buffering them on the operating system level (because the
user has not started the local end of the file transfer yet); local line buffer
becomes  full, local systems sends XOFF, remote starts buffering them up on its
end, user finally starts file transfer  on  local  end,  clears  buffer,  local
operating  system  sends  XON, and then all the remotely buffered NAKs show up,
causing the packet echoing problem described above, despite the  buffer  clear-
ing.

Flow control via modem signals can also be used when available.

Note  that  flow  control should not be confused with "handshake" or "line tur-
naround" techniques that are  used  on  simplex  or  half-duplex  communication
lines.  In fact, the two techniques are mutually exclusive.

3.8. Basic Kermit Protocol State Table

The  Kermit  protocol  can be described as a set of states and transitions, and
rules for what to do when changing from one state to another.    State  changes
occur  based  on  the type of packets that are sent or received, or errors that
may occur.  Packets always go back and forth; the sender of a file always sends
data  packets of some kind (init, header, data) and the receiver always returns
ACK or NAK packets.

Upon entering a given state, a certain kind of packet is either being  sent  or
is expected to arrive -- this is shown on top of the description of that state.
As a result of the action, various responses may occur; these are shown in  the
EVENT column.  For each event, an appropriate ACTION is taken, and the protocol
enters a NEW STATE.

The following table specifies basic Kermit operation.  Timeouts and error  con-
ditions  have been omitted from the following table for simplicity, but the ac-
tion is as described above.  Server operation and some of the advanced features
are also omitted.  A full-blown state table is given subsequently.

    STATE   EVENT           ACTION                      NEW STATE

         -- SEND STATES --

    Send Send-Init Packet:
    S       Get NAK,bad ACK (None)                          S
            Get good ACK    Set remote's params, open file  SF
            (Other)         (None)                          A

    Send File-Header Packet
    SF      Get NAK,bad ACK (None)                          SF
            Get good ACK    Get bufferful of file data      SD
            (Other)         (None)                          A

    Send File-Data Packet
    SD      Get NAK,bad ACK (None)                          SD
            Get good ACK    Get bufferful of file data      SD
            (End of file)   (None)                          SZ
            (Other)         (None)                          A

    Send EOF Packet
    SZ      Get NAK,bad ACK (None)                          SZ
            Get good ACK    Get next file to send           SF
            (No more files) (None)                          SB
            (Other)         (None)                          A

    Send Break (EOT) Packet
    SB      Get NAK,bad ACK (None)                          SB
            Get good ACK    (None)                          C
            (Other)         (None)                          A


         -- RECEIVE STATES --

    Wait for Send-Init Packet
    R       Get Send-Init   ACK w/local params              RF
            (Other)         (None)                          A

    Wait for File-Header Packet
    RF      Get Send-Init   ACK w/local params
                             (previous ACK was lost)        RF
            Get Send-EOF    ACK (prev ACK lost)             RF
            Get Break       ACK                             C
            Get File-Header Open file, ACK                  RD
            (Other)         (None)                          A

    Wait for File-Data Packet
    RD      Get previous
             packet(D,F)    ACK it again                    RD
            Get EOF         ACK it, close the file          RF
            Get good data   Write to file, ACK              RD
            (Other)         (None)                          A


         -- STATES COMMON TO SENDING AND RECEIVING --

    C       (Send Complete)                                 start
    A       ("Abort")                                       start

4. Packet Format

4.1. Fields

The  Kermit  protocol is built around exchange of packets of the following for-
mat:

    +------+-------------+-------------+------+------------+-------+
    | MARK | tochar(LEN) | tochar(SEQ) | TYPE |    DATA    | CHECK |
    +------+-------------+-------------+------+------------+-------+

where all fields consist of ASCII characters.  The fields are:

MARK    The synchronization character that marks the beginning of  the  packet.
        This should normally be CTRL-A, but may be redefined.

LEN     The  number  of  ASCII  characters  within  the packet that follow this
        field, in other words the packet length minus two.  Since  this  number
        is  transformed to a single character via the tochar() function, packet
        character counts of 0 to 94 (decimal) are permitted, and  96  (decimal)
        is  the  maximum total packet length.  The length does not include end-
        of-line or padding characters, which are outside  the  packet  and  are
        strictly  for  the  benefit  of  the operating system or communications
        equipment, but it does include the block check characters.

SEQ     The packet sequence number, modulo 64, ranging from 0 to 63.   Sequence
        numbers "wrap around" to 0 after each group of 64 packets.

TYPE    The  packet type, a single ASCII character.  The following packet types
        are required:

        D   Data packet
        Y   Acknowledge (ACK)
        N   Negative acknowledge (NAK)
        S   Send initiate (exchange parameters)
        B   Break transmission (EOT)
        F   File header
        Z   End of file (EOF)
        E   Error
        Q   Reserved for internal use
        T   Reserved for internal use

The NAK packet is used only to  indicate  that  the  expected  packet  was  not
        received correctly, never to supply other kinds of information, such as
        refusal to perform a requested service.  The NAK packet always  has  an
        empty  data  field.    The T "packet" is used internally by many Kermit
        programs to indicate that a timeout occurred.

DATA    The "contents" of the packet, if any contents are required in the given
        type  of  packet,  interpreted  according  to the packet type.  Control
        characters (bytes whose low order 7 bits are in the ASCII control range
        0-31, or 127) are preceded by a special prefix character, normally "#",
        and "uncontrollified" via ctl().  A prefixed sequence may not be broken
        across  packets.  Logical records in printable files are delimited with
        CRLFs, suitably prefixed (e.g. "#M#J").  Logical records need not  cor-
        respond  to  packets.  Any prefix characters are included in the count.
        Optional encoding for 8-bit data and repeated characters  is  described
        later.   The data fields of all packets are subject to prefix encoding,
        except the S, I, and A packets and their acknowledgements,  which  must
        not be encoded.

CHECK   A  block check on the characters in the packet between, but not includ-
        ing, the mark and the block check itself.  The check for each packet is
        computed  by  both hosts, and must agree if a packet is to be accepted.
        A single-character arithmetic checksum is the normal and required block
        check.    Only  six  bits of the arithmetic sum are included.  In order
        that all the bits of each data character contribute to  this  quantity,
        bits  6  and  7  of the final value are added to the quantity formed by
        bits 0-5.  Thus if s is the arithmetic sum  of  the  ASCII  characters,
        then

            check = tochar((s + ((s AND 192)/64)) AND 63)

        This  is  the  default  block check, and all Kermits must be capable of
        performing it.  Other optional block check types are described later.

        The block check is based on the ASCII values of all the  characters  in
        the  packet, including control fields and prefix characters.  Non-ASCII
        systems must translate to ASCII before performing the block check  cal-
        culation.

4.2. Terminator

Any  line  terminator  that  is  required  by the system may be appended to the
packet; this is carriage return (ASCII 15) by default.   Line  terminators  are
not  considered part of the packet, and are not included in the count or check-
sum.  Terminators are not necessary to the protocol, and are invisible  to  it,
as  are  any  characters  that may appear between packets.  If a host cannot do
single character input from a TTY line, then a terminator will be required when
sending  to  that host.  The terminator can be specified in the initial connec-
tion exchange.

Some Kermit implementations also use  the  terminator  for  another  reason  --
speed.    Some  systems  are  not fast enough to take in a packet and decode it
character by character at high baud rates; by blindly reading and  storing  all
characters  between  the MARK and the EOL, they are able to absorb the incoming
characters at full speed and then process them at their own rate.

4.3. Other Interpacket Data

The space between packets may be used for any  desired  purpose.    Handshaking
characters  may  be necessary on certain connections, others may require screen
control or other sequences to keep the packets flowing.

4.4. Encoding, Prefixing, Block Check

MARK, LEN, SEQ, TYPE, and CHECK are control fields.  Control fields are  always
literal single-character fields, except that the CHECK field may be extended by
one or two additional check characters.   Each  control  field  is  encoded  by
tochar() or taken literally, but never prefixed.  The control fields never con-
tain 8-bit data.

The DATA field contains a string  of  data  characters  in  which  any  control
characters  are  encoded  printably  and preceded with the control prefix.  The
decision to prefix a character in this way depends upon whether its low order 7
bits  are in the ASCII control range, i.e. 0-31 or 127.  Prefix characters that
appear in the data must themselves be prefixed by the control prefix,  but  un-
like  control  characters, these retain their literal value in the packet.  The
character to be prefixed is considered a prefix character if  its  low-order  7
bits  corresponds  to  an  active  prefix  character,  such  as  #  (ASCII 35),
regardless of the setting of its high-order bit.

During decoding, any character that follows the control prefix, but is  not  in
the  control  range,  is  taken  literally.   Thus, it does no harm to prefix a
printable character, even if that character does not happen  to  be  an  active
prefix.

The treatment of the high order ("8th") bit of a data byte is as follows:

   - If  the  communication channel allows 8 data bits per character, then
     the original value of the 8th bit is retained in the prefixed charac-
     ter.  For instance, a data byte corresponding to a Control-A with the
     8th bit set would be send as a control prefix, normally "#",  without
     the 8th bit set, followed by ctl(^A) with the 8th bit set.  In binary
     notation, this would be

         00100011 11000001

     In this case, the 8th bit is figured into all  block  check  calcula-
     tions.

   - If  the  communication channel or one of the hosts requires parity on
     each character, and both sides are capable of 8th-bit prefixing, then
     the  8th bit will be used for parity, and must not be included in the
     block check.  8th bit prefixing is an  option  feature  described  in
     greater detail in Section 6, below.

   - If parity is being used but 8th-bit prefixing is not being done, then
     the value of the 8th bit of each data byte will be  lost  and  binary
     files will not be transmitted correctly.  Again, the 8th bit does not
     figure into the block check.

The data fields of all packets are subject to prefix encoding, except S, I, and
A packets, and the ACKs to those packets (see below).

5. Initial Connection

Initial connection occurs when the user has started up a Kermit program on both
ends of the physical connection.  One Kermit has been directed (in one  way  or
another) to send a file, and the other to receive it.

The  receiving  Kermit  waits for a "Send-Init" packet from the sending Kermit.
It doesn't matter whether the sending Kermit is started  before  or  after  the
receiving  Kermit  (if  before,  the  Send-Init  packet should be retransmitted
periodically until the receiving Kermit acknowledges it).  The  data  field  of
the  Send-Init  packet  is  optional;  trailing  fields can be omitted (or left
blank, i.e. contain a space) to accept or specify default values.

The Send-Init packet contains a string of configuration information in its data
field.   The receiver sends an ACK for the Send-Init, whose data field contains
its own configuration parameters.  The data field of the Send-Init and the  ACK
to  the  Send-Init  are literal, that is, there is no prefix encoding.  This is
because the two parties will not know how to do prefix encoding until after the
configuration data is exchanged.

It  is  important to note that newly invented fields are added at the right, so
that old Kermit programs that do not have code to handle the  new  fields  will
act  as  if  they  were  not there.  For this reason, the default value for any
field, indicated by blank, should result in the behavior that  occurred  before
the new field was defined or added.

   1      2      3      4      5      6      7      8      9      10...
  +------+------+------+------+------+------+------+------+------+-------
  | MAXL | TIME | NPAD | PADC | EOL  | QCTL | QBIN | CHKT | REPT | CAPAS
  +------+------+------+------+------+------+------+------+------+-------

The  fields  are as follows (the first and second person "I" and "you" are used
to distinguish the two sides).  Fields are encoded printably using the tochar()
function unless indicated otherwise.

1. MAXL   The  maximum  length  packet  I  want  to  receive, a number up to 94
          (decimal).  (This really means the biggest value I want to see  in  a
          LEN  field.)  You respond with the maximum you want me to send.  This
          allows systems to adjust to each other's buffer sizes, or to the con-
          dition of the transmission medium.

2. TIME   The  number  of  seconds  after which I want you to time me out while
          waiting for a packet from me.  You respond with the amount of time  I
          should  wait  for packets from you.  This allows the two sides to ac-
          commodate to different line speeds or other factors that could  cause
          timing  problems.    Only  one side needs to time out.  If both sides
          time out, then the timeout intervals should not be close together.

3. NPAD   The number of padding characters I  want  to  precede  each  incoming
          packet;  you  respond in kind.  Padding may be necessary when sending
          to a half duplex system that requires some time to change the  direc-
          tion  of  transmission,  although  in practice this situation is more
          commonly handled by a "handshake" mechanism.

4. PADC   The control character I need for  padding,  if  any,  transformed  by
          ctl()  (not  tochar())  to  make  it printable.  You respond in kind.
          Normally NUL (ASCII 0), some systems use DEL (ASCII 127).  This field
          is to be ignored if the value NPAD is zero.

5. EOL    The  character  I  need to terminate an incoming packet, if any.  You
          respond in kind.  Most systems that require  a  line  terminator  for
          terminal input accept carriage return for this purpose (note, because
          there is no way to specify that no EOL should be sent, it would  have
          been  better  to  use  ctl() for this field rather than tochar(), but
          it's too late now).

6. QCTL   (verbatim) The printable ASCII character I will use to quote  control
          characters,  normally  and  by default "#".  You respond with the one
          you will use.

The following fields relate to the use  of  OPTIONAL  features  of  the  Kermit
protocol, described in section 6.

7. QBIN   (verbatim)  The  printable  ASCII  character  I  want to use to quote
          characters which have the 8th bit set, for transmitting binary  files
          when  the  parity  bit  cannot  be used for data.  Since this kind of
          quoting increases both processor and  transmission  overhead,  it  is
          normally  to be avoided.  If used, the quote character must be in the
          range ASCII 33-62 ("!" through ">") or 96-126 ("`" through "~"),  but
          different  from  the control-quoting character.  This field is inter-
          preted as follows:

          Y   I agree to 8-bit quoting if you request it (I don't need it).
          N   I will not do 8-bit quoting (I don't know how).
          &   (or any other character in the range 33-62 or 96-126) I  need  to
              do  8-bit  quoting  using  this character (it will be done if the
              other Kermit puts a Y in this field, or responds  with  the  same
              prefix  character,  such  as &).  The recommended 8th-bit quoting
              prefix character is "&".
          Anything Else : 8-bit quoting will not be done.

Note that this scheme allows either side to initiate the request, and the order
          does  not  matter.  For instance, a micro capable of 8-bit communica-
          tion will normally put a "Y" in this field whereas a  mainframe  that
          uses  parity will always put an "&".  No matter who sends first, this
          combination will result in election of 8th-bit quoting.

8. CHKT   (Verbatim) Check Type, the method for  detecting  errors.    "1"  for
          single-character  checksum  (the normal and required method), "2" for
          two-character checksum (optional), "3" for three-character  CRC-CCITT
          (optional).    If your response agrees, the designated method will be
          used; otherwise the single-character checksum will be used.

9. REPT   The prefix character I will use to  indicate  a  repeated  character.
          This  can  be  any  printable  character  in the range ASCII 33-62 or
          96-126, but different from the control and 8th-bit prefixes.  SP (32)
          denotes no repeat count processing is to be done.  Tilde ("~") is the
          recommended and normal repeat prefix.  If  you  don't  respond  iden-
          tically,  repeat  counts will not be done.  Groups of at least 3 or 4
          identical characters may be  transmitted  more  efficiently  using  a
          repeat  count,  though an individual implementation may wish to set a
          different threshhold.

10-?. CAPAS
          A bit mask, in which each bit position corresponds to a capability of
          Kermit, and is set to 1 if that capability is present, or 0 if it  is
          not.     Each  character  contains  a  6-bit  field  (transformed  by
          tochar()), whose low order bit is set to 1 if another capability byte
          follows,  and  to  0  in  the last capability byte.  The capabilities
          defined so far are:

            #1  Reserved
            #2  Reserved
            #3  Ability to accept "A" packets (file attributes)
            #4  Ability to do full duplex sliding window protocol
            #5  Ability to transmit and receive extended-length packets

The capability byte as defined so far would then look like:

           bit5 bit4 bit3 bit2 bit1 bit0
          +----+----+----+----+----+----+
          | #1 | #2 | #3 | #4 | #5 |  0 |
          +----+----+----+----+----+----+

          If all these capabilities were "on", the value of the byte  would  be
          76  (octal).    When  capability 6 is added, the capability mask will
          look like this:

           bit5 bit4 bit3 bit2 bit1 bit0    bit5 bit4 bit3 bit2 bit1 bit0
          +----+----+----+----+----+----+   +----+----+----+----+----+----+
          | #1 | #2 | #3 | #4 | #5 |  1 |   | #6 | -- | -- | -- | -- |  0 |
          +----+----+----+----+----+----+   +----+----+----+----+----+----+

CAPAS+1. WINDO
          Window size (see section 7.2).

CAPAS+2. MAXLX1
          Extended packet length (see section 7.1).

CAPAS+3. MAXLX2
          Extended packet length (see section 7.1).

The  receiving  Kermit  responds with an ACK ("Y") packet in the same format to
indicate its own preferences, options, and parameters.  The ACK need  not  con-
tain  the same number of fields as the the Send-Init.  From that point, the two
Kermit programs are  "configured"  to  communicate  with  each  other  for  the
remainder  of  the  transaction.  In the case of 8th-bit quoting, one side must
specify the character to be used, and the other must agree with a  "Y"  in  the
same  field, but the order in which this occurs does not matter.  Similarly for
checksums -- if one side requests 2 character  checksums  and  the  other  side
responds  with  a  "1"  or with nothing at all, then single-character checksums
will be done, since not all implementations can be expected to  do  2-character
checksums or CRCs.  And for repeat counts; if the repeat field of the send-init
and the ACK do not agree, repeat processing will not be done.

All Send-Init fields are optional.  The data field may be left  totally  empty.
Similarly,  intervening fields may be defaulted by setting them to blank.  Ker-
mit implementations should know what to do in these  cases,  namely  apply  ap-
propriate defaults.  The defaults should be:

    MAXL:   80
    TIME:   5 seconds
    NPAD:   0, no padding
    PADC:   0 (NUL)
    EOL:    CR (carriage return)
    QCTL:   the character "#"
    QBIN:   space, can't do 8-bit quoting
    CHKT:   "1", single-character checksum
    REPT:   No repeat count processing
    CAPAS:  All zeros (no special capabilities)
    WINDO:  Blank (zero) - no sliding windows
    MAXLX1: Blank (zero) - no extended length packets
    MAXLX2: Blank (zero) - no extended length packets

There are no prolonged negotiations in the initial connection sequence -- there
is one Send-Init and one ACK in reply.  Everything must be settled in this  ex-
change.

The  very first Send-Init may not get through if the sending Kermit makes wrong
assumptions about the receiving host.  For instance, the receiving host may re-
quire  certain  parity,  some  padding,  handshaking,  or a special end of line
character in order to read the Send-Init packet.  For this reason, there should
be  a way for the user the user to specify whatever may be necessary to get the
first packet through.

A parity field is not provided in the Send-Init packet because it could not  be
of use.  If the sender requires a certain kind of parity, it will also be send-
ing it.  If the receiver does not know this in advance, i.e. before getting the
Send-Init, it will not be able to read the Send-Init packet.
6. Optional Features

The foregoing sections have discussed basic, required operations for any Kermit
implementation.  The following sections discuss optional and advanced features.


6.1. 8th-Bit and Repeat Count Prefixing

Prefix quoting of control characters is mandatory.  In addition, prefixing  may
also  be  used for 8-bit quantities or repeat counts, when both Kermit programs
agree to do so.  8th-bit prefixing can allow 8-bit  binary  data  pass  through
7-bit  physical  links.    Repeat count prefixing can improve the throughput of
certain kinds of files  dramatically;  binary  files  (particularly  executable
programs) and structured text (highly indented or columnar text) tend to be the
major beneficiaries.

When more than one type of prefixing is in effect, a single data character  can
be  preceded  by  more  than one prefix character.  Repeat count processing can
only be requested by the sender, and will only be used by  the  sender  if  the
receiver  agrees.   8th-bit prefixing is a special case because its use is nor-
mally not desirable, since it increases both processing and transmission  over-
head.   However, since it is the only straightforward mechanism for binary file
transfer available to those systems that usurp the parity bit, a receiver  must
be  able  to  request the sender to do 8th-bit quoting, since most senders will
not normally do it by default.

The repeat prefix is followed immediately by a single-character  repeat  count,
encoded  printably  via  tochar(),  followed  by  the character itself (perhaps
prefixed by control or 8th bit prefixes, as explained below).  The repeat count
may  express values from 0 to 94.  If a character appears more than 94 times in
a row, it must be "cut off" at 94, emitted with all appropriate  prefixes,  and
"restarted".    The following table should clarify Kermit's prefixing mechanism
(the final line shows how a sequence of 120 consecutive NULs would be encoded):

                 Prefixed           With
    Character    Representation     Repeat Count for 8
       A            A                ~(A   ["(" is ASCII 40 - 32 = 8]
       ^A           #A               ~(#A
       'A           &A               ~(&A
       '^A          &#A              ~(&#A
       #            ##               ~(##
       '#           &##              ~(&##
       &            #&               ~(#&
       '&           &#&              ~(&#&
       ~            #~               ~(#~
       '~           &#~              ~(&#~
       NUL          #@               ~~#@~:#@ [120 NULs]

A represents any printable character, ^A represents any control  character,  'x
represents  any  character  with  the 8th bit set.  The # character is used for
control-character prefixing, and the & character  for  8-bit  prefixing.    The
repeat  count must always precede any other prefix character.  The repeat count
is taken literally (after transformation by unchar(); for instance "#" and  "&"
immediately  following  a  "~"  denote repeat counts, not control characters or
8-bit characters.  The control prefix character "#" is most  closely  bound  to
the  data  character,  then  the  8-bit prefix, then the repeat count; in other
words, the order is: repeat prefix and count, 8-bit prefix, control prefix, and
the  data  character itself.  To illustrate, note that &#A is not equivalent to
#&A.

When the parity bit is available for data, then 8th-bit prefixing should not be
done, and the 8th bit of the prefixed character will have the same value as the
8th bit of the original data byte.  In that case, the table looks like this:

                 Prefixed           With
    Character    Representation     Repeat Count for 8
       'A           'A               ~('A
       '^A          #'A              ~(#'A
       '#           #'#              ~(#'#
       '&           '&               ~('&
       '~           #'~              ~(#'~

Note that since 8th bit prefixing is not being done, "&" is not being  used  as
an  8th  bit  prefix  character,  so  it does not need to be prefixed with "#".
Also, note that the 8th bit is set on the final  argument  of  the  repeat  se-
quence, no matter how long, and not on any of the prefix characters.

Finally, remember the following rules:

   - Prefixed sequences must not be broken across packets.

   - Control, 8th-bit, and repeat count prefixes must be distinct.

   - Data  fields  of  all  packets  must pass through the prefix encoding
     mechanism, except for S, I, and A packets, and ACKs to those packets,
     whose data fields must not be encoded.

In the first rule above, note that a prefixed sequence means a single character
and all its prefixes, like ~%&#X, not  a  sequence  like  #M#J,  which  is  two
prefixed sequences.


6.2. Server Operation

A  Kermit server is a Kermit program running remotely with no "user interface".
All commands to the server arrive in packets from the  local  Kermit.    SERVER
operation  is  much  more  convenient than basic operation, since the user need
never again interact directly with the remote Kermit program after once  start-
ing  it  up in server mode, and therefore need not issue complementary SEND and
RECEIVE commands on the two sides to get a file  transfer  started;  rather,  a
single command (such as SEND or GET) to the local Kermit suffices.  Kermit ser-
vers can also provide services beyond file transfer.

Between transactions, a Kermit server waits for packets containing server  com-
mands.  The packet sequence number is always set back to 0 after a transaction.
A Kermit server in command wait should be looking for  packet  0,  and  command
packets  sent to servers should also be packet 0.  Certain server commands will
result in the exchange of multiple packets.  Those operations  proceed  exactly
like file transfer.

A  Kermit  server program waiting for a command packet is said to be in "server
command wait".  Once put into server command  wait,  the  server  should  never
leave  it  until it gets a command packet telling it to do so.  This means that
after any transaction is terminated, either normally or by any kind  of  error,
the server must go back into command wait.  While in command wait, a server may
elect to send out periodic NAKs for packet  0,  the  expected  command  packet.
Since  the  user  may  be disconnected from the server for long periods of time
(hours), the interval between these NAKs should be  significantly  longer  than
the  normal timeout interval (say, 30-60 seconds, rather than 5-10).  The peri-
odic NAKs are useful for breaking the deadlock that  would  occur  if  a  local
program was unable to time out, and sent a command that was lost.  On the other
hand, they can cause problems for local Kermit programs that cannot clear their
input  buffers,  or  for  systems that do XON/XOFF blindly, causing the NAKs to
buffered in the server's host system output buffer, to be suddenly released  en
masse  when  an XON appears.  For this reason, servers should have an option to
set the command-wait wakeup interval, or to disable it altogher.

Server operation must be implemented in two places: in the server  itself,  and
in  any  Kermit  program  that will be communicating with a server.  The server
must have code to read the server commands from packets and  respond  to  them.
The  user Kermit must have code to parse the user's server-related commands, to
form the server command packets, and to handle the responses  to  those  server
commands.


6.2.1. Server Commands

Server  commands  are listed below.  Not all of them have been implemented, and
some may never be, but their use should  be  reserved.    Although  server-mode
operation  is optional, certain commands should be implemented in every server.
These include Send-Init (S), Receive-Init (R),  and  the  Generic  Logout  (GL)
and/or  Finish (GF) commands.  If the server receives a command it does not un-
derstand, or cannot execute, it should respond with an Error  (E)  packet  con-
taining a message like "Unimplemented Server Command" and both sides should set
the packet sequence number back to 0, and the server should  remain  in  server
command wait.  Only a GL or GF command should terminate server operation.

Server commands are as follows:

S   Send Initiate (exchange parameters, server waits for a file).
R   Receive Initiate (ask the server to send the specified files).
I   Initialize (exchange parameters).
X   Text header.  Allows transfer of text to the user's screen in response to a
    generic or host command.  This works just like file  transfer  except  that
    the  destination "device" is the screen rather than a file.  Data field may
    contain a filename, title, or other heading.
C   Host Command.  The data field contains a string to be executed as a command
    by the host system command processor.
K   Kermit  Command.   The data field contains a string in the interactive com-
    mand language of the Kermit server (normally a SET command) to be  executed
    as if it were typed in at command level.
G   Generic  Kermit Command.  Single character in data field (possibly followed
    by operands, shown in {braces}, optional fields  in  [brackets])  specifies
    the command:

    I   Login [{*user[*password[*account]]}]
    C   CWD, Change Working Directory [{*directory[*password]}]
    L   Logout, Bye
    F   Finish (Shut down the server, but don't logout).
    D   Directory [{*filespec}]
    U   Disk Usage Query [{*area}]
    E   Erase (delete) {*filespec}
    T   Type {*filespec}
    R   Rename {*oldname*newname}
    K   Copy {*source*destination}
    W   Who's logged in? (Finger) [{*user ID or network host[*options]}]
    M   Send a short Message {*destination*text}
    H   Help [{*topic}]
    Q   Server Status Query
    P   Program {*[program-filespec][*program-commands]}
    J   Journal {*command[*argument]}
    V   Variable {*command[*argument[*argument]]}

Asterisk  as  used  above ("*") represents a single-character length field, en-
    coded using tochar(), for the operand that follows it; thus lengths from  0
    to  94  may  be  specified.    This  allows multiple operands to be clearly
    delimited regardless of their contents.

Note that field length encoding is used within the data field  of  all  Generic
command  packets,  but not within the data fields of the other packets, such as
S, I, R, X, K, and C.

All server commands that send  arguments  in  their  data  fields  should  pass
through  the  prefix  encoding  mechanism.   Thus if a data character or length
field happens to correspond to an active prefix character, it  must  itself  be
prefixed.    The field length denotes the length of the field before prefix en-
coding and (hopefully) after prefix decoding.  For example, to send  a  generic
command  with  two  fields,  "ABC"  and  "ZZZZZZZZ",  first each field would be
prefixed by tochar() of its length,  in  this  case  tochar(3)  and  tochar(8),
giving  "#ABC(ZZZZZZZZ".   But "#" is the normal control prefix character so it
must be prefixed itself, and the eight Z's can be  condensed  to  3  characters
using a repeat prefix (if repeat counts are in effect), so the result after en-
coding would be "##ABC(~(Z" (assuming the repeat prefix is tilde  ("~").    The
recipient  would  decode this back into the original "#ABC(ZZZZZZZZ" before at-
tempting to extract the two fields.

Since a generic command must fit into a single packet, the program sending  the
command  should  ensure  that the command actually fits, and should not include
length fields that point beyond the end  of  the  packet.    Servers,  however,
should be defensive and not attempt to process any characters beyond the end of
the data field, even if the argument length field would lead them to do so.


6.2.2. Timing

Kermit does not provide a mechanism for  suspending  and  continuing  a  trans-
action.    This  means that text sent to the user's screen should not be frozen
for long periods (i.e. not longer than  the  timeout  period  times  the  retry
threshold).

Between  transactions,  when  the  server has no tasks pending, it may send out
periodic NAKs (always with type 1 checksums) to prevent a deadlock  in  case  a
command  was  sent  to  it  but  was lost.  These NAKs can pile up in the local
"user" Kermit's input buffer (if it has one), so  the  user  Kermit  should  be
prepared  to  clear  its  input  buffer  before  sending a command to a server.
Meanwhile, servers should recognize that some systems provide no function to do
this  (or  even  when they do, the process can be foiled by system flow control
firmware) and should therefore provide a way turn off or slow down the command-
wait NAKs.


6.2.3. The R Command

The  R  packet, generally sent by a local Kermit program whose user typed a GET
command, tells the server to send the files specified by the name in  the  data
field  of the R packet.  Since we can't assume that the two Kermits are running
on like systems, the local (user) Kermit must parse the file specification as a
character string, send it as-is (but encoded) to the server, and let the server
take care of validating its syntax and looking up the file.  If the server  can
open and read the specified file, it sends a Send-Init (S) packet -- not an ac-
knowledgement! -- to the user, and then completes the file-sending transaction,
as described above.

If  the server cannot send the file, it should respond with an error (E) packet
containing a reason, like "File not found" or "Read access required".

Thus, the only two valid responses to a successfully received R packet are an S
packet or an E packet.  The R packet is not ACK'd.


6.2.4. The K Command

The  K  packet  can contain a character string which the server interprets as a
command in its own interactive command language.  This facility is  useful  for
achieving  the  same effect as a direct command without having to shut down the
server, connect back to the remote system, continue it (or start  a  new  one),
and issue the desired commands.  The server responds with an ACK if the command
was executed successfully, or an error packet otherwise.  The most  likely  use
for the K packet might be for transmitting SET commands, e.g. for switching be-
tween text and binary file modes.


6.2.5. Short and Long Replies

Any request made of a server may be answered in either of  two  ways,  and  any
User  Kermit  that  makes  such a request should be prepared for either kind of
reply:

   - A short reply.  This consists of a single ACK packet, which may  con-
     tain  text  in  its  data field.  For instance, the user might send a
     disk space query to the server, and the server might ACK the  request
     with  a  short character string in the data field, such as "12K bytes
     free".  The user Kermit should display this text on the screen.

   - A long reply.  This proceeds exactly like a  file  transfer  (and  in
     some  cases  it  may  be a file transfer).  It begins with one of the
     following:

        * A File-Header (F) packet (optionally followed by one or more At-
          tributes packets; these are discussed later);

        * A Text-Header (X) packet.

        * A Send-Init (S) Packet, followed by an X or F packet.

     After  the  X or F packet comes an arbitrary number of Data (D) pack-
     ets, then an End-Of-File (Z) packet, and finally a Break-Transmission
     (B) packet, as for ordinary file transfer.

A  long reply should begin with an S packet unless an I-packet exchange has al-
ready taken place, and the type 1 (single-character) block check is being used.


6.2.6. Additional Server Commands

The following server commands request the server to perform  tasks  other  than
sending  or receiving files.  Almost any of these can have either short or long
replies.  For instance, the Generic Erase (GE) command may elicit a simple ACK,
or  a  stream  of  packets  containing the names of all the files it erased (or
didn't erase).  These commands are now described in more detail; arguments  are
as  provided in commands typed to the user Kermit (subject to prefix encoding);
no transformations to any kind of normal or canonic form are done --  filenames
and other operands are in the syntax of the server's host system.

I   Login.  For use when a Kermit server is kept perpetually running on a dedi-
    cated line.  This lets a new user obtain an identity on the  server's  host
    system.    If the data field is empty, this removes the user's identity, so
    that the next user does not get access to it.

L   Logout, Bye.  This shuts down the server entirely, causing the  server  it-
    self  to  log  out  its  own job.  This is for use when the server has been
    started up manually by the user, who then wishes to shut it down  remotely.
    For a perpetual, dedicated server, this command simply removes the server's
    access rights to the current user's files, and leaves  the  server  waiting
    for a new login command.

F   Finish.    This  is  to allow the user to shut down the server, putting its
    terminal back into normal (as opposed to binary or raw) mode,  and  putting
    the server's job back at system command level, still logged in, so that the
    user can connect back to the job.  For a perpetual, dedicated server,  this
    command behaves as the L (BYE) command.

C   CWD.    Change  Working Directory.  This sets the default directory or area
    for file transfer on the server's host.  With  no  operands,  this  command
    sets the default area to be the user's own default area.

D   Directory.    Send  a  directory listing to the user.  The user program can
    display it on the terminal or store it in a  file,  as  it  chooses.    The
    directory  listing  should contain file sizes and creation dates as well as
    file names, if possible.  A wildcard or other file-group designator may  be
    specified  to  ask  the  server  list  only  those files that match.  If no
    operand is given, all files in the current area should be shown.

U   Disk Usage Query.  The server responds with the amount of  space  used  and
    the  amount  left  free to use, in K bytes (or other units, which should be
    specified).

E   Erase (delete).  Delete the specified file or file group.

T   Type.  Send the specified file or file group, indicating (by starting  with
    an  X  packet rather than an F packet, or else by using the Type attribute)
    that the file is to be displayed on the screen, rather than stored.

R   Rename.  Change the name of the file or files as indicated.  The string in-
    dicating  the  new  name  may  contain other attributes, such as protection
    code, permitted in file specifications by the host.

K   Copy.  Produce a new copy of the file or file group, as indicated,  leaving
    the source file(s) unmodified.

W   Who's  logged  in? (Finger).  With no arguments, list all the users who are
    logged in on the server's host  system.    If  an  argument  is  specified,
    provide more detailed information on the specified user or network host.

M   Short  Message.    Send  the given short (single-packet) message to the in-
    dicated user's screen.

P   Program.  This command has two  arguments,  program  name  (filespec),  and
    command(s)  for  the program.  The first field is required, but may be left
    null (i.e. zero length).  If it is null, the currently  loaded  program  is
    "fed"  the specified command.  If not null, the specified program is loaded
    and started; if a program command is given it is fed to the program  as  an
    initial  command  (for instance, as a command line argument on systems that
    support that concept).  In any case, the output of the program is sent back
    in packets as either a long or short reply, as described above.

J   Journal.  This command controls server transaction logging.  The data field
    contains one of the following:

    +   Begin/resume logging transactions.  If a filename is given,  close  any
        currently  open transaction and then open the specified file as the new
        transaction log.  If no name given, but a log file  was  already  open,
        resume  logging  to that file.  If no filename was given and no log was
        open,  the  server  should  open  a  log  with  a  default  name,  like
        TRANSACTION.LOG.

    -   Stop  logging transactions, but don't close the current transaction log
        file.

    C   Stop logging and close the current log.

    S   Send the transaction log as a file.  If it was open, close it first.

Transaction logging is the recording of the progress of  file  transfers.    It
    should  contain entries showing the name of each file transferred, when the
    transfer began and ended, whether it completed successfully,  and  if  not,
    why.

V   Set  or Query a variable.  The command can be S or Q. The first argument is
    the variable name.  The second argument, if any, is the value.

    S   Set the specified variable to the specified value.   If  the  value  is
        null,  then  undefine  the  variable.   If the variable is null then do
        nothing.  If the variable did not exist before, create it.  The  server
        should respond with an ACK if successful, and Error packet otherwise.

    Q   Query  the  value  of  the named variable.  If no variable is supplied,
        display the value of all active variables.  The  server  responds  with
        either  a  short or long reply, as described above.  If a queried vari-
        able does not exist, a null value is returned.
Variables are named by character strings, and  have  character  string  values,
    which may be static or dynamic.  For instance, a server might have built-in
    variables like "system name" which never  changes,  or  others  like  "mail
    status"  which,  when queried, cause the server to check to see if the user
    has any new mail.


6.2.7. Host Commands

Host commands are conceptually simple, but may be hard  to  implement  on  some
systems.  The C packet contains a text string in its data field which is simply
fed to the server's host system command processor; any output from the  proces-
sor  is  sent  back  to  the  user in Kermit packets, as either a short or long
reply.

Implementation of this facility under UNIX, with its forking process  structure
and i/o redirection via pipes, is quite natural.  On other systems, it could be
virtually impossible.


6.2.8. Exchanging Parameters Before Server Commands

In basic Kermit, the Send-Init exchange is always sufficient to  configure  the
two  sides  to  each  other.   During server operation, on the other hand, some
transactions may not begin with a Send-Init packet.   For  instance,  when  the
user  sends  an  R  packet to ask the server to send a file, the server chooses
what block check option to use.  Or if the user requests a  directory  listing,
the server does not know what packet length to use.

The solution to this problem is the "I" (Init-Info) packet.  It is exactly like
a Send-Init packet, and the ACK works the same way too.  However, receipt of an
I  packet  does not cause transition to file-send state.  The I-packet exchange
simply allows the two sides to set their parameters,  in  preparation  for  the
next transaction.

Servers  should  be  able to receive and ACK "I" packets when in server command
wait.  User Kermits need not send "I" packets, however; in that case, the serv-
er  will  assume  all  the  defaults for the user listed on page 9, or whatever
parameters have been set by other means (e.g. SET commands typed to the  server
before it was put in server mode).

User  Kermits  which send I packets should be prepared to receive and ignore an
Error packet in response.  This could happen if the server has not  implemented
I packets.

The  I  packet,  together  with  its  ACK,  constitute  a complete transaction,
separate from the S-packet or other exchange that follows it.  The packet  num-
ber remains at zero after the I-packet exchange.


6.3. Alternate Block Check Types

There are two optional kinds of block checks:

Type 2
    A two-character checksum based on the low order 12 bits of  the  arithmetic
    sum  of  the  characters in the packet (from the LEN field through the last
    data character, inclusive) as follows:

                 1              2
        --------+----------------+---------------+
        ...data | tochar(b6-b11) | tochar(b0-b5) |
        --------+----------------+---------------+

    For instance, if the 16-bit result is 154321 (octal), then the 2  character
    block check would be "C1".

Type 3
    Three-character 16-bit CRC-CCITT. The CRC calculation treats  the  data  it
    operates  upon  as  a  string  of  bits with the low order bit of the first
    character first and the high order bit of the last character last.  The in-
    itial value of the CRC is taken as 0; the 16-bit CRC is the remainder after
                                                    16  12  5
    dividing the data bit string by the polynomial X  +X  +X +1 (this  calcula-
    tion  can  actually  be  done  a  character at a time, using a simple table
    lookup algorithm).  The result is represented as three printable characters
    at the end of the packet, as follows:

                 1               2              3
        --------+-----------------+----------------+---------------+
        ...data | tochar(b12-b15) | tochar(b6-b11) | tochar(b0-b5) |
        --------+-----------------+----------------+---------------+

    For  instance, if the 16-bit result is 154321 (octal), then the 3 character
    block check would be "-C1".  The CRC technique chosen here agrees with many
    hardware implementations (e.g. the VAX CRC instruction).

Here is an algorithm for Kermit's CRC-CCITT calculation:

      crc = 0                                   Start CRC off at 0
      i = <position of LEN field>               First byte to include

  A:  c = <byte at position i>                  Get current byte
      if (parity not NONE) then c = c AND 127;  Mask off any parity bit
      q = (crc XOR c) AND 15;                   Do low-order 4 bits
      crc = (crc / 16) XOR (q * 4225);
      q = (crc XOR (c / 16)) AND 015;           And high 4 bits
      crc = (crc / 16) XOR (q * 4225);
      i = i + 1                                 Position of next byte
      LEN = LEN - 1                             Decrement packet length
      if (LEN > 0) goto A                       Loop till done

  At this point, the crc variable contains the desired quantity.

Thanks to Andy Lowry of Columbia's CS department for this "tableless" CRC algo-
rithm (actually, it uses a table with one entry -- 4225).  AND is  the  bitwise
AND  operation,  XOR  the  bitwise exclusive OR, "*" is multiplication, and "/"
signifies integer division ("crc / 16" is equivalent to shifting the crc  quan-
tity 4 bits to the right).

The single-character checksum has proven quite adequate in practice.  The other
options can be used only if both sides agree to do so via Init packet (S or  I)
exchange.    The  2 and 3 character block checks should only be used under con-
ditions of severe line noise and packet corruption.

Since type 2 and 3 block checks are optional, not all Kermits can  be  expected
to  understand  them.  Therefore, during initial connection, communication must
begin using the type 1 block check.  If type 2 or 3 block checks are agreed  to
during  the  "I"  or  "S" packet exchange, the switch will occur only after the
Send-Init has been sent and ACK'd with a type 1 block check.  This  means  that
the  first  packet  with a type 2 or 3 block check must always be an "F" or "X"
packet.  Upon completion of a transaction, both sides must switch back to  type
1  (to  allow  for  the  fact that neither side has any way of knowing when the
other side has been stopped and restarted).  The transaction is  over  after  a
"B"  or  "E" packet has been sent and ACK'd, or after any error that terminates
the transaction prematurely or abnormally.

A consequence of the foregoing rule is that if a type 2 or 3 block check is  to
be  used,  a  long  reply  sent  by  the server must begin with a Send-Init (S)
packet, even if an I packet exchange had already occurred.   If  type  1  block
checks  are  being used, the S packet can be skipped and the transfer can start
with an X or F packet.

A server that has completed a transaction and is awaiting  a  new  command  may
send  out periodic NAKs for that command (packet 0).  Those NAKs must have type
1 block checks.

The use of alternate block check types can cause certain  complications.    For
instance, if the server gets a horrible error (so bad that it doesn't even send
an error packet) and reverts to command wait, sending NAKs for packet 0 using a
type  1  block  check,  while  a transfer using type 2 or 3 block checks was in
progress, neither side will be able to read the other's packets.  Communication
can  also  grind to a halt if A sends a Send-Init requesting, say, type 3 block
checks, B ACKs the request, switches to type 3 and waits for the X or F  packet
with a type 3 block check, but the ACK was lost, so A resends the S packet with
a type 1 block check.  Situations like this will ultimately resolve  themselves
after  the  two  sides retransmit up to their retry threshhold, but can be rec-
tified earlier by the use of two heuristics:

   - The packet reader can assume that if the  packet  type  is  "S",  the
     block check type is 1.

   - A  NAK  packet  never has anything in its data field.  Therefore, the
     block check type can always be deduced by the packet reader from  the
     length  field of a NAK.  In fact, it is the value of the length field
     minus 2.  A NAK can therefore be thought of as a kind  of  "universal
     synchronizer".

These  heuristics tend to violate the layered nature of the protocol, since the
packet reader should normally be  totally  unconcerned  with  the  packet  type
(which  is  of  interest  to  the  application  level  which invokes the packet
reader).  A better design would have had each packet include  an  indicator  of
the  type  of its own block check; this would have allowed the block check type
to be changed dynamically during a transaction to adapt to changing conditions.
But it's too late for that now...


6.4. Interrupting a File Transfer

This  section  describes  an  optional  feature of the Kermit protocol to allow
graceful interruption of file transfer.  This feature is  unrelated  to  server
operation.

To interrupt sending a file, send an EOF ("Z") packet in place of the next data
packet, including a "D" (for Discard) in the data field.   The  recipient  ACKs
the  Z  packet normally, but does not retain the file.  This does not interfere
with older Kermits on the receiving end; they will not inspect the  data  field
and  will close the file normally.  The mechanism can be triggered by typing an
interrupt character at the console  of  the  sending  Kermit  program.    If  a
(wildcard) file group is being sent, it is possible to skip to the next file or
to terminate the entire batch; the protocol is the same in either case, but the
desired action could be selected by different interrupt characters, e.g. CTRL-X
to skip the current file, CTRL-Z to skip the rest of the batch.

To interrupt receiving a file, put an "X" in the data field of  an  ACK  for  a
Data packet.  To interrupt receiving an entire file group, use a "Z".  The user
could trigger this mechanism by typing an interrupt character, say, CTRL-X  and
CTRL-Z,  respectively,  at  the  receiving Kermit's console.  A sender that was
aware of the new feature, upon  finding  one  of  these  codes,  would  act  as
described  above, i.e. send a "Z" packet with a "D" code; a sender that did not
implement this feature would simply ignore the codes and continue sending.   In
this  case, and if the user wanted the whole batch to be cancelled (or only one
file was being sent), the receiving Kermit program, after determining that  the
sender  had ignored the "X" or "Z" code, could send an Error (E) packet to stop
the transfer.

The sender may also choose to send a Z packet containing the  D  code  when  it
detects  that the file it is sending cannot be sent correctly and completely --
for instance, after sending some packets correctly, it gets an i/o error  read-
ing the file.  Or, it notices that the "8th bit" of a file byte is set when the
file is being sent as a text file and no provision has been made for  transmit-
ting the 8th bit.


6.5. Transmitting File Attributes

The  optional  Attributes  (A)  packet provides a mechanism for the sender of a
file to provide additional information about it.  This packet can  be  sent  if
the  receiver has indicated its ability to process it by setting the Attributes
bit in the capability mask.    If  both  sides  set  this  bit  in  the  Kermit
capability  mask, then the sender, after sending the filename in the "F" packet
and receiving an acknowledgement, may (but does not have to) send an "A" packet
to provide file attribute information.

Setting the Attributes bit in the capability mask does not indicate support for
any particular attributes, only that the receiver is prepared to accept the "A"
packet.

The  attributes  are given in the data field of the "A" packet.  The data field
consists of 0 or more subfields, which may occur in any order.   Each  subfield
is of the following form:

    +-----------+----------------+------+
    | ATTRIBUTE | tochar(LENGTH) | DATA |
    +-----------+----------------+------+

where

ATTRIBUTE is a single printable character other than space,

LENGTH    is  the  length  of  the  data characters (0 to 94), with 32 added to
          produce a single printable character, and

DATA      is length characters worth of data, all printable characters.

No quoting or prefixing is done on any of this data.

More than one attribute packet may be sent.  The only requirement is  that  all
the A packets for a file must immediately follow its File header (or X) packet,
and precede the first Data packet.

There may be 93 different attributes, one for each of the  93  printable  ASCII
characters other than space.  These are assigned in ASCII order.

! (ASCII 33)
          Length.  The data field gives the length in  K  (1024)  bytes,  as  a
          printable decimal number, e.g. "!#109".  This will allow the receiver
          to determine in advance whether there  is  sufficient  room  for  the
          file, and/or how long the transfer will take.

" (ASCII 34)
          Type.  The data field can contain some indicator of the nature of the
          file.     Operands  are  enclosed  in  {braces},  optional  items  in
          [brackets].  The braces and brackets do not actually  appear  in  the
          packet.

          A[{xx}] ASCII  text,  containing no 8-bit quantities, logical records
                  (lines) delimited by the (quoted) control character  sequence
                  {xx},  represented  here  by  its printable counterpart (MJ =
                  CRLF, J = LF, etc).  For instance  AMJ  means  that  the  ap-
                  pearance  of  #M#J  (the  normal prefixed CRLF sequence) in a
                  file data packet indicates the end of a record, assuming  the
                  current  control  prefix is "#".  If {xx} is omitted, MJ will
                  be assumed.

          B[{xx}] Binary.  {xx} indicates in what manner the file is binary:

                  8   (default) The file is a sequence of  8-bit  bytes,  which
                      must  be saved as is.  The 8th bit may be sent "bare", or
                      prefixed according to  the  Send-Init  negotiation  about
                      8th-bit prefixing.

                  36  The  file  is  a PDP-10 format binary file, in which five
                      7-bit bytes are fit into one 36-bit word, with the  final
                      bit of each word being represented as the "parity bit" of
                      every 5th character (perhaps prefixed).

          D{x}    Moved from here to FORMAT attribute

          F{x}    Moved from here to FORMAT attribute

          I[{x}]  Image.  The file is being sent exactly as it  is  represented
                  on  the  system  of  origin.    For use between like systems.
                  There are {x} usable bits per  character,  before  prefixing.
                  For  instance,  to  send binary data from a system with 9-bit
                  bytes, it might be convenient to send three 6-bit  characters
                  for every two 9-bit bytes.  Default {x} is 8.

# (ASCII 35)
          Creation Date, expressed as "[yy]yymmdd[ hh:mm[:ss]]"  (ISO  standard
          date  format), e.g. 831009 23:59.  The time is optional; if given, it
          should be in 24-hour format, and the seconds may be  omitted,  and  a
          single space should separate the time from the date.

$ (ASCII 36)
          Creator's ID, expressed as a character string of the given length.

% (ASCII 37)
          Account to charge the file to, character string.

& (ASCII 38)
          Area in which to store the file, character string.

' (ASCII 39)
          Password for above, character string.

( (ASCII 40)
          Block Size.  The file has, or is to be stored with, the  given  block
          size.

) (ASCII 41)
          Access:

          N   New, the normal case -- create a new file of the given name.
          S   Supersede (overwrite) any file of the same name.
          A   Append to file of the given name.

* (ASCII 42)
          Encoding:

          A   ASCII, normal ASCII encoding with any necessary prefixing, etc.
          H   Hexadecimal "nibble" encoding.
          E   EBCDIC (sent as if it were a binary file).
          X   Encrypted.
          Q{x}
              Huffman Encoded for compression.  First x bytes of the  file  are
              the key.

+ (ASCII 43)
          Disposition (operands are specified in the syntax of  the  receiver's
          host system):

          M{user(s)}      Send the file as Mail to the specified user(s).

          O{destination}  Send  the  file  as  a  lOng  terminal message to the
                          specified destination (terminal, job, or user).

          S[{options}]    Submit the file as a batch job,  with  any  specified
                          options.

          P[{options}]    Print   the  file  on  a  system  printer,  with  any
                          specified options, which  may  specify  a  particular
                          printer, forms, etc.

          T               Type the file on the screen.

          L[{aaa}]        Load  the  file  into memory at the given address, if
                          any.

          X[{aaa}]        Load the file into memory at the  given  address  and
                          eXecute it.

          A               Archive the file; save the file together with the at-
                          tribute packets that preceded it, so that it  can  be
                          sent  back  to  the system of origin with all its at-
                          tributes intact.  A file stored in this way should be
                          specially  marked  so  that  the Kermit that sends it
                          back will recognize the attribute information as dis-
                          tinct from the file data.

, (ASCII 44)
          Protection.  Protection code for the  file,  in  the  syntax  of  the
          receiver's host file system.  With no operand, store according to the
          system's default protection for the destination area.

- (ASCII 45)
          Protection.    Protection  code  for  the  file  with  respect to the
          "public" or "world", expressed generically in a 6-bit quantity  (made
          printable by tochar()), in which the bits have the following meaning:

          b0: Read Access
          b1: Write Access
          b2: Execute Access
          b3: Append Access
          b4: Delete Access
          b5: Directory Listing

A  one in the bit position means allow the corresponding type of access, a zero
          means prohibit it.  For example, the letter "E" in this  field  would
          allow  read,  execute,  and  directory  listing access (unchar("E") =
          69-32 = 37 = 100101 binary).

. (ASCII 46)
          Machine  and  operating system of origin.  This is useful in conjunc-
          tion with the archive disposition attribute.  It allows a file,  once
          archived, to be transferred among different types of systems, retain-
          ing its archive status, until it finds its way to a machine with  the
          right  characteristics  to de-archive it.  The systems are denoted by
          codes; the first character is the major system designator, the second
          designates the specific model or operating system.  A third character
          may be added to make further  distinctions,  for  instance  operating
          system version.  The systems below do not form a complete collection;
          many more can and probably will be added.

          A   Apple microcomputers

              1   Apple II, DOS
              2   Apple III
              3   Macintosh
              4   Lisa
          B   Sperry (Univac) mainframes

              1   1100 series, EXEC
              2   9080, VS9

          C   CDC mainframes

              1   Cyber series, NOS
              2   Cyber series, NOS-BE
              3   Cyber series, NOS-VE
              4   Cyber series, SCOPE

          D   DEC Systems

              1   DECsystem-10/20, TOPS-10
              2   DECsystem-10/20, TOPS-20
              3   DECsystem-10/20, TENEX
              4   DECsystem-10/20, ITS
              5   DECsystem-10/20, WAITS
              6   DECsystem-10/20, MAXC
              7   VAX-11, VMS
              8   PDP-11, RSX-11
              9   PDP-11, IAS
              A   PDP-11, RSTS/E
              B   PDP-11, RT-11
              C   Professional-300, P/OS
              D   Word Processor (WPS or DECmate), WPS

          E   Honeywell mainframes

              1   MULTICS systems
              2   DPS series, running CP-6
              3   DPS series, GCOS
              4   DTSS

          F   Data General machines

              1   RDOS
              2   AOS
              3   AOS/VS

          G   PR1ME machines, PRIMOS

          H   Hewlett-Packard machines

              1   HP-1000, RTE
              2   HP-3000, MPE

          I   IBM 370-series and compatible mainframes

              1   VM/CMS
              2   MVS/TSO
              3   DOS
              4   MUSIC
              5   GUTS
              6   MTS

          J   Tandy microcomputers, TRSDOS

          K   Atari computers

              1   Home computers, DOS
              2   ST series

          L   Commodore micros

              1   Pet
              2   64
              3   Amiga

          M   Miscellaneous mainframes and  minis  with  proprietary  operation
              systems:

              1   Gould/SEL minis, MPX
              2   Harris, VOS
              3   Perkin-Elmer minis, OS/32
              4   Prime, Primos
              5   Tandem, Nonstop
              6   Cray, CTSS
              7   Burroughs (subtypes may be necessary here)
              8   GEC 4000, OS4000
              9   ICL machines
              A   Norsk Data, Sintran III
              B   Nixdorf machines

          N   Miscellaneous micros and workstations:

              1   Acorn BBC Micro
              2   Alpha Micro
              3   Apollo Aegis
              4   Convergent, Burroughs, and similar systems with CTOS, BTOS
              5   Corvus, CCOS
              6   Cromemco, CDOS
              7   Intel x86/3x0, iRMX-x86
              8   Intel MDS, ISIS
              9   Luxor ABC-800, ABCDOS
              A   Perq
              B   Motorola, Versados

          O-T Reserved

          U   Portable Operating or File Systems

              1   UNIX
              2   Software Tools
              3   CP/M-80
              4   CP/M-86
              5   CP/M-68K
              6   MP/M
              7   Concurrent CP/M
              8   MS-DOS
              9   UCSD p-System
              A   MUMPS
              B   LISP
              C   FORTH
              D   OS-9

/ (ASCII 47)
          Format of the data within the packets.

          A{xx}           Variable length delimited records, terminated by  the
                          character  sequence {xx}, where xx is a string of one
                          or more control characters, represented here by their
                          unprefixed  printable  equivalents,  e.g. MJ for ^M^J
                          (CRLF).

          D{x}            Variable length undelimited records.    Each  logical
                          record  begins  with  an  {x}-character ASCII decimal
                          length field (similar to ANSI tape format "D").   For
                          example,  "D$"  would indicate 4-digit length fields,
                          like "0132".

          F{xxxx}         Fixed-length  undelimited  records.    Each   logical
                          record is {xxxx} bytes long.

          R{x}            For record-oriented transfers, to be used in combina-
                          tion with one of  the  formats  given  above.    Each
                          record  begins  (in  the  case of D format, after the
                          length field) with an x-character long position field
                          indicating the byte position within the file at which
                          this record is to be stored.

          M{x}            For record-oriented transfers, to be used in combina-
                          tion  with  one  of the formats given above.  Maximum
                          record length for a variable-length record.

0 (ASCII 48)
          Special  system-dependent parameters for storing the file on the sys-
          tem of origin, for specification of exotic attributes not covered ex-
          plicitly by any of the Kermit attribute descriptors.  These are given
          as a character string in the system's own  language,  for  example  a
          list of DCB parameters in IBM Job Control Language.

1-@ (ASCII 49)
          Exact byte count of the file as it is stored on the sender's  system,
          before any conversions (e.g. to canonic form).  Of limited usefulness
          when transferring text files  between  systems  that  represent  text
          boundaries differently.

2-@ (ASCII 50-64)
          Reserved

Other attributes can be imagined, and can be added later if needed.    However,
two important points should be noted:

   - The  receiver may have absolutely no way of honoring, or even record-
     ing, a given attribute.  For instance, CP/M-80 has no slot for  crea-
     tion  date  or  creator's ID in its FCB; the DEC-20 has no concept of
     block size, etc.

   - The sender may have no way of determining the correct values  of  any
     of  the  attributes.  This is particularly true when sending files of
     foreign origin.

The "A" packet mechanism only provides a way to send certain information  about
a  file to the receiver, with no provision or guarantee about what the receiver
may do with it.  That information may be  obtained  directly  from  the  file's
directory entry (FCB, FDB, ...), or specified via user command.

The  ACK  to  the  "A"  packet  may in turn have information in its data field.
However, no complicated negotiations about file attributes may take  place,  so
the  net  result  is that the receiver may either refuse the file or accept it.
The receiver may reply to the "A" packet with any of the following codes in the
data field of the ACK packet:

<null>  (empty data field) I accept the file, go ahead and send it.

N[{xxx}]
        I refuse the file as specified, don't send it; {xxx}  is  a  string  of
        zero  or more of the attribute characters listed above, to specify what
        attributes I object to (e.g. "!" means it's too long, "&" means I don't
        have write access to the specified area, etc).

Y[{xxx}]
        I agree to receive the file, but I cannot honor attributes {xxx}, so  I
        will store the file according to my own defaults.

Y       (degenerate case of Y{xxx}, equivalent to <null>, above)

How  the  receiver  actually  replies  is an implementation decision.  A NAK in
response to the "A" packet means, of course, that the receiver did not  receive
the "A" correctly, not that it refuses to receive the file.


6.6. Advanced Kermit Protocol State Table

The  simple  table  presented  previously  is sufficient for a basic Kermit im-
plementation.  The following is a state table for the full Kermit protocol, in-
cluding  both server mode and sending commands to a server Kermit.  It does not
include handling of the file attributes packet (A).   Note  that  states  whose
names  start  with "Send" always send a packet each time they are entered (even
when the previous state was the same).  States whose name  starts  with  "Rec",
always  wait for a packet to be received (up to the timeout value), and process
the received packet.  States whose names do not include either send or  receive
do  not  process  packets  directly.  These are states which perform some local
operation and then change to another state.

The initial state is determined by the user's  command.    A  "server"  command
enters  at Rec_Server_Idle.  A "send" command enters at Send_Init.  A "receive"
command (the old non-server version, not a "get" command) enters  at  Rec_Init.
Any  generic command, the "get" command, and the "host" command enter at either
Send_Server_Init or Send_Gen_Cmd, depending upon the expected response.

Under "Rec'd Msg", the packet type of the incoming message is  shown,  followed
by the packet number in parentheses; (n) means the current packet number, (n-1)
and (n+1) mean the previous and next packet  numbers  (modulo  64),  (0)  means
packet  number zero. Following the packet number may be slash and a letter, in-
dicating some special signal in the data field.  For instance Z(n)/D  indicates
a Z (EOF) packet, sequence number n, with a "D" in the data field.

Under  "Action",  "r+"  means  that the retry count is incremented and compared
with a threshhold; if the threshhold is exceeded, an Error packet is  sent  and
the  state  changes  to  "Abort".    "n+"  means  that the packet number is in-
cremented, modulo 64, and the retry count, r, is set back to zero.

State   Rec'd Msg       Action                  Next state

Rec_Server_Idle -- Server idle, waiting for a message

    Set n and r to 0

        I(0)            Send ACK                Rec_Server_Idle
        S(0)            Process params,
                         ACK with params, n+    Rec_File
        R(0)            Save file name          Send_Init

        K, C or G(0)    Short reply:
                         ACK(0)/reply           Rec_Server_Idle
                        Long reply:
                         init needed            Send_Init
                         init not needed, n+    Open_File

        Timeout         Send NAK(0)             Rec_Server_Idle
        Other           Send E                  Rec_Server_Idle

Rec_Init -- Entry point for non-server RECEIVE command

    Set n and r to 0

        S(0)            Process params, send
                         ACK with params, n+    Rec_File
        Timeout         Send NAK(0), r+         Rec_Init
        Other           Send E                  Abort

Rec_File -- Look for a file header or EOT message

        F(n)            Open file, ACK, n+      Rec_Data
        X(n)            Prepare to type on
                         screen, ACK, n+        Rec_Data
        B(n)            ACK                     Complete
        S(n-1)          ACK with params, r+     Rec_File
        Z(n-1)          ACK, r+                 Rec_File
        Timeout         Resend ACK(n), r+       Rec_File
        Other           Send E                  Abort

Rec_Data -- Receive data up to end of file

        D(n)            Store data, ACK, n+;
                         If interruption wanted
                         include X or Z in ACK  Rec_Data
        D(n-1)          Send ACK, r+            Rec-Data
        Z(n)            Close file, ACK, n+     Rec_File
        Z(n)/D          Discard file, ACK, n+   Rec_File
        F(n-1)          Send ACK, r+            Rec_Data
        X(n-1)          Send ACK, r+            Rec_Data
        Timeout         Send ACK(n-1), r+       Rec_Data
        Other           Send E                  Abort


Send_Init -- Also entry for SEND command

    Set n and r to 0, send S(0) with parameters

        Y(0)            Process params, n+      Open_File
        N, Timeout      r+                      Send_Init
        Other           r+                      Send_Init

Open_File -- Open file or set up text to send

                                                Send_File

Send_File -- Send file or text header

    Send F or X(n)

        Y(n), N(n+1)    Get first buffer of     Send_Data or Send_Eof if
                         data, n+                empty file or text
        N, Timeout      r+                      Send_File
        Other                                   Abort

Send_Data -- Send contents of file or textual information

    Send D(n) with current buffer

        Y(n), N(n+1)    n+, Get next buffer     Send_Data or Send_Eof if
                                                 at end of file or text
        Y(n)/X or Z     n+                      Send_Eof
        N, Timeout      r+                      Send_Data
        Other                                   Abort

Send_Eof -- Send end of file indicator

    Send Z(n); if interrupting send Z(n)/D

        Y(n), N(n+1)    Open next file, n+      Send_File if more, or
                                                Send_Break if no more
                                                 or if interrupt "Z".
        N, Timeout      r+                      Send_Eof
        Other                                   Abort

Send_Break -- End of Transaction

    Send B(n)

        Y(n), N(0)                              Complete
        N(n), Timeout                           Send_Break
        Other                                   Abort

Send_Server_Init - Entry for Server commands which expect large response.

    Send I(0) with parameters

        Y(0)            Process params          Send_Gen_Cmd
        N, Timeout      r+                      Send_Server_Init
        E               Use default params      Send_Gen_Cmd
        Other                                   Abort

Send_Gen_Cmd - Entry for Server commands which expect short response (ACK)

    Send G, R or C(0)

        S(0)            Process params,
                         ACK with params, n+    Rec_File
        X(1)            Setup to type on
                         terminal, n+           Rec_Data
        Y(0)            Type data on TTY        Complete
        N, Timeout      r+                      Send_Gen_Cmd
        Other                                   Abort

Complete -- Successful Completion of Transaction

        Set n and r to 0;
        If server, reset params, enter Rec_Server_Idle
        otherwise exit

Abort -- Premature Termination of Transaction

    Reset any open file, set n and r to 0

        If server, reset params, enter Rec_Server_Idle
        otherwise exit

Exit, Logout states
        Exit or Logout

Note that the generic commands determine the next state as follows:

   1. If the command is not supported, an error packet  is  sent  and  the
      next state is "Abort".

   2. If  the  command generates a response which can be fit into the data
      portion of an ACK, an ACK is sent with the text  (quoted  as  neces-
      sary) in the data portion.

   3. If the command generates a large response or must send a file, noth-
      ing is sent from the Rec_Server_Idle state, and the  next  state  is
      either  Send_Init  (if either no I message was received or if alter-
      nate block check types are to be used), or Open_File (if an  I  mes-
      sage  was  received  and  the  single character block check is to be
      used).

   4. If the command is Logout, an ACK  is  sent  and  the  new  state  is
      Logout.

   5. If the command is Exit, an ACK is sent and the new state is Exit.
7. Performance Extensions

The  material in this chapter was added in 1985-86 to address the inherent per-
formance problems of a stop-and-wait protocol like Kermit.


7.1. Long Packets

A method is provided to allow the formation of long Kermit packets.   Questions
as  to  the  desirability  or  appropriateness  of this extension to the Kermit
protocol are not addressed.  All numbers are in decimal (base 10) notation, all
arithmetic is integer arithmetic.

In  order  for  long  packets  to be exchanged, the sender must set the bit for
Capability #5 (the LONGP bit) in the CAPAS field of  the  Send-Init  (S  or  I)
packet,

     bit5 bit4 bit3 bit2 bit1 bit0
    +----+----+----+----+----+----+
    | #1 | #2 | #3 | #4 | #5 |  0 |
    +----+----+----+----+----+----+
                           ^
                           |
                         LONGP

and  also  furnish  the  MAXLX1 and MAXLX2 (extended length 1 and 2) fields, as
follows:

        10              CAPAS+1  CAPAS+2  CAPAS+3
    ---+-------+-     -+--------+--------+--------+
       | CAPAS |  ...  | WINDO  | MAXLX1 | MAXLX2 |
    ---+-------+-     -+--------+--------+--------+
                        ^
                        |
                      (currently field 11, because CAPAS is still 1 byte)

where WINDO is the window size (a  separate  Kermit  protocol  extension),  and
MAXLX1  and MAXLX2 are each a printable ASCII character in the range SP (space,
ASCII 32) to ~ (tilde, ASCII 126), formed as follows:

    MAXLX1 = tochar(m / 95)
    MAXLX2 = tochar(m MOD 95)

(where m is the intended maximum length, / signifies integer division, and  MOD
is  the  modulus  operator),  to indicate the longest extended-length packet it
will accept as input.  The receiver responds with an ACK packet having the same
bit  also  set in the CAPAS field, and with the MAXLX1 and MAXLX2 fields set to
indicate the maximum length packet it will accept.

The maximum length expressible by this construct is 95 x 94 + 94, or 9024.

Since the sender can not know in advance whether the receiver is capable of ex-
tended  headers, the Send-Init MAXL field must also be set in the normal manner
for compatibility.

If the receiver responds favorably to an extended-length packet bid  (that  is,
if  its  ACK has the LONGP bit set in the CAPAS field), then the combined value
of its MAXLX1,MAXLX2 fields is  used.    If  the  LONGP  bit  is  set  but  the
MAXLX1,MAXLX2 pair is missing, then the value 500 will be used by default.

If  the  response  is  unfavorable  (the LONGP bit is not set in the receiver's
CAPAS field), then extended headers will not be used and the  MAXL  field  will
supply the maximum packet length.

After  the Send-Init has been sent and acknowledged with agreement to allow ex-
tended headers, all packets up to and including the B or E  packet  which  ter-
minates  the  transaction  (and its acknowledgement) are allowed -- but not re-
quired -- to have extended headers; extended and normal packets may  be  freely
mixed by both Kermits.

The  normal  Kermit  packet length field (LEN) specifies the number of bytes to
follow, up to and including the block check.  Since at least 3 bytes must  fol-
low  (SEQ,  TYPE, and CHECK), a value of 0, 1, or 2 is never encountered in the
LEN field of a valid unextended Kermit packet.  When extended packets have been
negotiated,  the LEN field is treated as follows for the duration of the trans-
action:

   - If unchar(LEN) > 2 then the packet is a normal, unextended packet.
   - If unchar(LEN) = 0 then the packet has a "Type 0" extended header.
   - If unchar(LEN) = 1 or 2, the packet is invalid and  should  cause  an
     Error.

"Lengths"  of  1  and  2  are  reserved for future use in Type 1 and 2 extended
headers, yet to be specified.

A Type 0 extended packet has the following layout:

+------+-----+-----+------+-------+-------+--------+----       ----+-------+
| MARK |     | SEQ | TYPE | LENX1 | LENX2 | HCHECK |  DATA ....    | CHECK |
+------+-----+-----+------+-------+-------+--------+----       ----+-------+
                          | Extended Header        |

The blank length field (SP = tochar(0)) indicates that the  first  3  bytes  of
what  is  normally the data field is now an extended header of Type 0, in which
the number of bytes remaining in the packet, up  to  and  including  the  block
check, is

    extended-length = (95 x unchar(LENX1)) + unchar(LENX2)

and  HCHECK  is  a  header  checksum, formed exactly like a Type-1 Kermit block
check, but from the sum of the ASCII values of the SEQ, TYPE, LENX1, and  LENX2
fields:

     s = LEN + SEQ + TYPE + LENX1 + LENX2

     HCHECK = tochar((s + ((s & 192)/64)) & 63)

where & is the bitwise AND operator.

Since  the value of the extended length field must be known accurately in order
to locate the end of the packet and the packet block check, it  is  vital  that
this  information  not  be  corrupted  before  it is used.  The header checksum
prevents this.

The extended header, like the normal  header  itself,  is  not  prefix-encoded.
This  is  because  it  is  used at datalink level, before decoding takes place.
Therefore the entity responsible for building packets must leave  3  spaces  at
the  beginning  of  the  data field, and the datalink function (spack) fills in
LENX1, LENX2, and HCHECK based upon the data actually entered into the  packet,
after encoding.  The packet receiving datalink function (rpack) behaves accord-
ingly.

The packet block check is formed in the usual manner, based on all packet bytes
beginning  with  LEN and ending with the last character in the data field.  The
block check may be Type 1, 2, or 3, depending upon  what  was  negotiated,  but
longer  packets  are  more  likely to be corrupted than shorter ones and should
therefore have higher-order block checks if possible.  This proposal  does  not
change the way block check type is negotiated, and does not require that Type 2
or 3 block check be implemented.

With long packets, the possibility  exists  that  the  arithmetic  sum  of  the
characters  in  a  packet will exceed 2^15, and will overflow a 16-bit word, or
become negative.  The checksum function would have  to  be  modified  to  guard
against  this,  for instance by always setting the high four bits of the sum to
zero before adding in the next byte.

Implementation can be a bit tricky.  The Kermit program should be set up to use
normal,  untextended  packets  by  default -- that is, to mimic the behavior of
original, "classic" Kermit.  Even  when  the  program  believes  itself  to  be
capable  of  sending  and  receiving  long packets, it has no knowledge of what
devices may lie along the communication path, whose buffers might not  be  long
enough  to  accommodate  bursts  of  data  of the desired length.  Long packets
should be elected when the user has explicitly elected them with a SET command.
The current SET SEND PACKET-LENGTH <n> command will do; if the number is larger
than 94, then the program will -- transparently to the user -- try to negotiate
long  packets.    A finer degree of control can be accomplished by included SET
commands to explicitly enable or disable the use of long packets.

Once long packets are successfully negotiated, the program should  be  prepared
to  back  off  when errors occur, since the very size of the packets may be the
cause of the errors.  Upon timeout or receipt of a NAK (or extra copies of  the
previous  packet),  the  sender  should  be prepared to reconstruct the current
packet at, say,  half  its  size,  down  to  some  reasonable  minimum,  before
retransmission.    Even  when  the  size  itself is not the problem, this makes
retransmission less painful under noisy conditions.

Long packets and sliding windows may be used  at  the  same  time,  though  the
benefits from doing so may not be worth the trouble of coding the dynamic buff-
er allocation required (for n buffers of size m, negotiated at Send-Init time).
It's  also  worth  noting  that the benefit/cost ratio of long packets declines
after a length of about 1000, at which point the benefit of  additional  length
is less than 1%, and the cost of retransmission is very high.


7.2. Sliding Windows

The sliding window extension to Kermit was proposed and developed by a group at
The Source Telecomputing in McLean, Virginia, led by Leslie Spira and including
Hugh  Matlock  and John Mulligan, who wrote the following material.  Like other
extensions, this one is designed for "upward compatibility" with  Kermits  that
do not support this extension.

The  windowing  protocol  as  defined  for the Kermit file transfer protocol is
based on the main premise of continuously sending data packets up to the number
defined by a set window size.  These data packets are continuously acknowledged
by the receive side and the ideal transfer occurs as long as  they  are  trans-
mitted  with good checksums, they are transmitted in sequential order and there
are no lost data packets or acknowledgements.   The  various  error  conditions
define  the  details  of the windowing protocol and are best examined on a case
basis.

There are five stages that describe the overall sequence of events in the  Ker-
mit  protocol.  Three of these stages deviate from the original protocol in or-
der to add the windowing feature.  Stages 1 through 5 are briefly described  on
the  following  page.    The  three  stages (1, 3 and 4) which deviate from the
original protocol are then described in greater detail in the pages  that  fol-
low.


7.2.1. Overall Sequence of Events

STAGE 1 - Propose and Accept Windowing
    The send side requests windowing in the transmission of  the  Send-Initiate
    (S)  packet.  The receive side accepts windowing by sending an acknowledge-
    ment (ACK packet) for the Send-Initiate packet.

STAGE 2 - Send and Accept File-Header Packet
    The  send  side  transmits  the  File-Header  (F)  packet and waits for the
    receive side to acknowledge it prior to transmitting any data.

STAGE 3 - Transfer Data
    The  sending  routine  transmits Data (D) packets one after the other until
    the protocol window is closed.  The receiving side ACKs good  data,  stores
    data to disk as necessary and NAKs bad data.

    When  the  sender  receives  an ACK, the window may be rotated and the next
    packet sent.  If the sender receives a NAK, the data  packet  concerned  is
    retransmitted.

STAGE 4 - Send and Accept End_of_File Packet
    As the sender is reading the file for data  to  send,  it  will  eventually
    reach  the end of the file.  It then waits until all outstanding data pack-
    ets have been acknowledged, and then sends an End-of_File (Z) packet.

    When the receive side gets the End-of-File packet it stores the rest of the
    data to disk, closes the file, and ACKs the End-of_File packet.

    The protocol then returns to Stage 2, sending and acknowledging any further
    File-Header (F) packets.

STAGE 5 - End of Transmission
    Once the End-of-File packet has been sent and acknowledged and there are no
    more files to send, the sender transmits the End-of-Transmission (B) packet
    in  order  to  end  the  ongoing  transaction.  Once the receiver ACKs this
    packet, the transaction is ended and the logical connection closed.


Stage 1 - Propose and Accept Windowing

The initial connection as currently defined for the Kermit protocol  will  need
to  change  only  in  terms  of  the contents of the Send-Initiate packet.  The
receiving Kermit waits for the sending Kermit to transmit the Send-Initiate (S)
packet and the sending packet does not proceed with any additional transmission
until the ACK has been returned by the receiver.

The contents of the Send-Init packet, however, will be slightly revised.    The
data  field of the Send-Init packet currently contains all of the configuration
parameters.  The first six fields of the Send-Init packet are fixed as follows:

   1        2        3        4        5        6
  +--------+--------+--------+--------+--------+--------+
  | MAXL   | TIME   | NPAD   | PADC   | EOL    | QCTL   |
  +--------+--------+--------+--------+--------+--------+

Fields 7 through 10 are optional features of Kermit and fields 7 through 9 will
also remain unchanged as defined for the existing protocol:

   7        8        9        10
  +--------+--------+--------+--------+
  | QBIN   | CHKT   | REPT   | CAPAS  |
  +--------+--------+--------+--------+

The  windowing capability constitutes a fourth capability and the fourth bit of
the capability field will be set to 1 if the Kermit implementation  can  handle
windowing:

     bit5 bit4 bit3 bit2 bit1 bit0
    +----+----+----+----+----+----+
    | #1 | #2 | #3 | #4 | #5 |  0 |
    +----+----+----+----+----+----+
                      ^
                      |
                     SWC (sliding window capability)

The remaining fields of the Send-Init packet are either reserved for future use
by the standard Kermit protocol or reserved  for  local  site  implementations.
The  four  fields  following the capability field are reserved for the standard
Kermit protocol.  The field following the capability mask is  used  to  specify
the "Window Size":

        10              CAPAS+1  CAPAS+2  CAPAS+3
    ---+-------+-     -+--------+--------+--------+
       | CAPAS |  ...  | WINDO  | MAXLX1 | MAXLX2 |
    ---+-------+-     -+--------+--------+--------+
                        ^
                        |
                      (currently field 11, because CAPAS is still 1 byte)

WINDO is the window size to be used, encoded printably using the tochar() func-
tion.  The window size may range from 1 to 31 inclusive.

The sender will specify the window size it wishes to use and the receiver  will
reply  (in  the  ACK packet) with the window size it wishes to use.  The window
size actually used will be the minimum of the two.   If  the  receiver  replies
with a window size of 0 then no windowing will be done.


Stage 3 - Transfer Data

The  sequence  of events required for the transmission of data packets and con-
firmation of receipts constitute the main functions of the windowing  protocol.
There are four main functions which can be identified within this stage.  These
are:

   - the sender's processing of the data packets,
   - the receiver's handling of incoming packets,
   - the sender's handling of the confirmations,
   - the error handling on both sides.

The following discussion details the specific  actions  required  for  each  of
these  functions.  Refer to the state table at the end of this document for the
specific action taken on a "received message" basis for the full protocol.

The Sender's Processing of Data Packets

The sender instigates the transmission by sending the  first  data  packet  and
then  operating  in a cyclical mode of sending data until the defined window is
closed.

Data to be sent must be read from  the  file,  encoded  into  the  Kermit  Data
packet,  and  saved  in  a Send-Table.  A Send-Table entry consists of the data
packet itself (which makes convenient the re-send of a  NAK'd  packet),  a  bit
which  keeps  track of whether the packet has been ACK'd (the ACK'd bit), and a
retry counter.  The table is large enough to  hold  all  the  packets  for  the
protocol window.

Before  each  transmission, the input buffer is checked and input is processed,
as described below.  Transmission is stopped if the protocol  window  "closes",
that is, if the Send-Table is full.

The Receiver's Handling of Incoming Packets

The  receiver  keeps  its own table as it receives incoming data packets.  This
allows the receiver to receive subsequent packets while it  is  waiting  for  a
re-send  of  an erroneous or lost packet.  In other words, the incoming packets
do not have to be received in sequential order and can still be written to disk
in order.

A  Receive-Table  entry consists of the data packet, a bit which keeps track of
whether a good version of the packet has been received (the ACK'd bit),  and  a
retry  counter  for  the NAKs we send to request retransmissions of the packet.
The table is large enough to hold all the packets for the protocol window.

The different possibilities for a received packet are:

   1. A new packet, the next sequential one (the usual case)
   2. A new packet, not the next sequential one (some were lost)
   3. An old packet, retransmitted
   4. An unexpected data packet
   5. Any packet with a bad checksum

These are now discussed separately:

   1. The next new packet has sequence number <one past the  latest  table
      entry>.    The packet is ACK'd, and the Receive-Table is checked for
      space.  If it is full (already contains  window_size  entries)  then
      the  oldest  entry  is written to disk.  (This entry should have the
      ACK'd bit set.  If not, the receiver aborts the file transfer.)  The
      received  packet is then stored in the Receive-Table, with the ACK'd
      bit set.

   2. If the packet received has sequence number in the  range  <two  past
      the latest table entry> to <window_size past the latest table entry>
      then it is a new packet, but some have been lost.  (The upper  limit
      here  represents the highest packet the sender could send within its
      protocol window.  Note that the requirement to test for this case is
      what limits the maximum window_size to half of the range of possible
      sequence numbers) We ACK the packet, and NAK all packets  that  were
      skipped.    (The skipped packets are those from <one past the latest
      table entry> to <one before the received packet>) The  Receive-Table
      is then checked.  The table may have to be rotated to accomodate the
      packet, as with case 1.  (This time, several table entries may  have
      to  be written to disk.  As before, if any do not have the ACK'd bit
      set, they will trigger an abort.)  The packet is then stored in  the
      table, and the ACK'd bit set.

   3. A  retransmitted  packet will have sequence number in the range <the
      oldest table entry> to <the latest table  entry>.    The  packet  is
      ACK'd, then placed in the table, setting the ACK'd bit.

   4. A  packet with sequence number outside of the range from <the oldest
      table entry> to <window_size past the latest  table  entry>  is  ig-
      nored.

   5. If the packet received has a bad checksum, we must decide whether to
      generate a NAK, and if so, with what sequence number.  The best  ac-
      tion  may  depend  on the configuration and channel error rate.  For
      now, we adopt the following heuristic:  If there are unACK'd entries
      in  our  Receive-Table, we send a NAK for the oldest one.  Otherwise
      we ignore the packet.  (Notice that this  will  occur  in  a  common
      case:    when  things  have  been going smoothly and one packet gets
      garbled.  In this case, when we later receive  the  next  packet  we
      will NAK for this one as described under Case 2 above.)

The Sender's Handling of Confirmations

The  sender's  receipt of confirmations controls the rotation of the Send-Table
and normally returns the sender to  a  sending  state.    The  sender's  action
depends  on  the  packet  checksum,  the type of confirmation (ACK or NAK), and
whether the  confirmation  is  within  the  high  and  low  boundaries  of  the
Send-Table.

If the checksum is bad the packet is ignored.

When  the  sender receives an ACK, the sequence number is examined.  If the se-
quence number is outside of the current table boundaries, then the ACK is  also
ignored.  If the sequence number is inside of the current table boundaries then
the ACK'd bit for that packet is marked.  If the entry is at the low  boundary,
this  enables  a  "rotation"  of the table.  The low boundary is changed to the
next sequential entry for which the ACK'd bit is not set.  This frees space  in
the table to allow further transmissions.

When  the  sender receives a NAK, the table boundaries are checked.  A NAK out-
side of the table boundary is ignored and a NAK inside the table  boundary  in-
dicates  that  the  sender must re-send the packet.  The sender first tests the
packet's retry counter against the retry threshold.  If the threshold has  been
reached,  then  the  transfer is stopped (by going to the Abort state).  Other-
wise, the retry counter is incremented and the packet re-sent.

Error Handling for Both Sides

Three situations are discussed here:  Sender timeout, Receiver timeout, and in-
valid packets.

If  certain  packets are lost, each side may "hang", waiting for the other.  To
get things moving when this happens  each  may  have  a  "timeout  limit",  the
longest they will wait for something from the other side.

If  the  sender's  timeout condition is triggered, then it will send the oldest
unACK'd packet.  This will be the first one in the Send-Table.

If the receiver's timeout condition is triggered, then it will send a  NAK  for
the  "most  desired  packet".    This  is  defined as either the oldest unACK'd
packet, or if none are unACK'd, then the next packet to be  received  (sequence
number  <latest  table  entry  plus  one>).   The packet retry count is not in-
cremented by this NAK; instead we depend on the timeout retry count,  discussed
next.

For  either the sender or receiver, the timeout retry count is incremented each
time a timeout occurs.  If the timeout retry limit is exceeded  then  the  side
aborts  the  file  transfer.  Each side resets the retry count to zero whenever
they receive a packet.

In addition, as with the existing Kermit, any invalid packet types received  by
either side will cause an Error packet and stop the file transfer.


Stage 4 - Send and Accept End of File Packet

There  are several ways to end the file transfer.  The first is the normal way,
when the sender encounters an end-of-file condition when reading  the  file  to
get a packet for transmission.  The second is because of a sender side user in-
terrupt.  The third is because of a receiver side  user  interrupt.    Both  of
these  cause  the  received  file to be discarded.  In addition either side may
stop the transfer with an Error packet if an  unrecoverable  error  is  encoun-
tered.

Normal End of File Handling

When  the  sender  reaches the end of file, it must wait until all data packets
have been acknowledged before sending the End-of-File (Z) packet.  To  do  this
it must be able to check the end-of-file status when it processes ACKs.  If the
ACK causes the Send-Table to be emptied and the end-of-file has  been  reached,
then  a  transition  is  made to the Send_Eof state which sends the End_of_File
packet.

When the receiver gets the End_of_File packet, it writes the  contents  of  the
Receive-Table  to  the  file  (suitably  decoded) and closes the file.  (If any
entries do not have the ACK'd bit set, or if errors occur in writing the  file,
the  receiver  aborts  the file transfer.)  If the operation is successful, the
receiver sends an ACK.  It then sets its sequence  number  to  the  End_of_File
packet sequence number and goes to Rcv_File state.


File Transfer Interruptions

Sender User Interrupt
    Whenever the sender checks for input from the data communications line,  it
    should also check for user input.  If that indicates that the file transfer
    should be stopped, the sender goes directly to the Send_Eof state and sends
    an  End_of_File  packet  with  the Discard indication.  It will not have to
    wait for outstanding packets to be ACK'd.

    When the receiver gets the End_of_File packet with the  Discard  indication
    it  discards  the  file, sets its sequence number to the End_of_File packet
    sequence number, and goes to RcvFile state.

Receiver User Interrupt
    Whenever  the  receiver checks for input from the data communications line,
    it also should check for user input.   If  that  indicates  that  the  file
    transfer  should be stopped, the receiver sets an "interrupt indication" of
    X (for "stop this file transfer") or of Z (for  "stop  the  batch  of  file
    transfers").   When the receiver later sends an ACK, it places an X or Z in
    the data field.

    When the sender gets this ACK, it goes to the Send_Eof state and sends  the
    End_of_File packet with the Discard indication, as above.

    When  the receiver gets the End_of_File packet with the Discard indication,
    it discards the file, sets its sequence number to  the  End_of_File  packet
    sequence number, and goes to RcvFile state.


Low Level Protocol Requirements

The windowing protocol makes certain assumptions about the underlying transmis-
sion and reception mechanism.

First, it must provide a full-duplex channel so that messages may be  sent  and
received simultaneously.

Second,  it  will prove advantageous to be able to buffer several received mes-
sages at the low level before processing them at the Kermit level.  This is for
two  reasons.  The first is that the Kermit windowing level of the protocol may
take a while to process one input, and meanwhile  several  others  may  arrive.
The  second  reason is to support XON/XOFF flow control.  If Kermit receives an
XOFF from the data communications line, it must wait for an XON before  sending
its  packet.  While it is waiting, the low level receive must be able to accept
input.  Otherwise a deadlock situation could arise with  each  side  flow  con-
trolled, waiting for the other.


Kermit Windowing Protocol State Table

The  following  table shows the inputs expected, the actions performed, and the
succeeding states for the Send_Data_Windowing and Rcv_Data_Windowing states.

If both sides agree on windowing in the Send Init  exchange,  then  instead  of
entering  the  old  Send_Data or Rcv_Data states from Send_File or Rcv_File, we
enter the new Send_Data_Windowing or Rcv_Data_Windowing.

SEND_DATA_WINDOWING (SDW)

Rec'd Msg                Action                          Next State

No input/Window closed  (1) Wait for input                   SDW
No input/Window open    (2) Read file, encode packet,        SDW
                            Place in table, mark unACK'd,
                            Send packet

ACK/ X or Z             (3) set interrupt indicator (X/Z)  Send_Eof
ACK/outside table        -ignore-                            SDW
ACK/inside table        (4) mark pkt ACK'd,         SDW or Send_Eof
                            if low rotate table,
                            if file eof & table empty
                               then goto Send_Eof

NAK/outside table        -ignore-                            SDW
NAK/inside table        (5) test retry limit,                SDW
                            re-send DATA packet

Bad checksum            -ignore-                             SDW

Timeout                 (6) re-send oldest unACK'd pkt       SDW

User interrupt          (7) set interrupt indicator (X/Z)  Send_Eof

Other                   (8) send Error                      Quit

RCV_DATA_WINDOWING (RDW)

Rec'd Msg                Action                          Next State

DATA/new                (1) send ACK                         RDW
                            if table full: file & rotate
                            store new pkt in table
DATA/old                (2) send ACK, store in table         RDW
DATA/unexpected         -ignore-                             RDW

Z/discard               (3) discard file                   Rcv_File
Z/                      (4) write table to file & close    Rcv_File
                            if OK send ACK, else Error     or Quit

Bad checksum            (5) send NAK for oldest unACK'd      RDW

Timeout                 (6) send NAK for most desired pkt    RDW

User Interrupt          (7) Set interrupt indicator X or Z   RDW

Other                   (8) send Error pkt                  Quit


7.2.2. Questions and Answers about Sliding Windows

Q.  What is the purpose of the "windowing" extension?

A.  The object is to speed up file transfers using Kermit.  The  increase  will
    be  especially  noticeable over the data networks (such as Telenet and Tym-
    net) and over connections using satellite links.  This is because there are
    long communications delays over these connections.

Q.  How does it work?

A.  Basically,  it  allows you to send several packets out in a row before get-
    ting the first acknowledgment back.  The number of packets that can be sent
    out is set by the "window size", hence the name windowing.

Q.  Could you explain in more detail?

A.  Right  now, a system sending a file transmits one packet of data, then does
    nothing more until it gets back an acknowledgment that the packet has  been
    received.    Once  it  gets  an acknowledgment, it sends the next packet of
    data.  Over standard direct-dial land-based phone lines,  the  transmission
    delays  are  relatively small.  However, the public data networks or satel-
    lite links can introduce delays of up to several seconds round trip.  As  a
    result, the sending system ends up spending much more time waiting than ac-
    tually sending data.

    With the new windowing enhancement, the sending system will be able to keep
    sending data continuously, getting the acknowledgments back later.  It only
    has to stop sending data if it reaches the  end  of  the  current  "window"
    without getting an acknowledgment for the first packet in the current "win-
    dow".

Q.  What size is the "window"?

A.  The window size can vary depending on what the two ends of  the  connection
    agree  on.  The suggested standard window size will be 8 packets.  The max-
    imum is 31 packets.

    The Kermit sequence numbering is modulo 64 (it "wraps" back to the 1st  se-
    quence  number after the 64th sequence number).  It is helpful to limit the
    maximum window size to 31 to avoid problems  (ambiguous  sequence  numbers)
    under certain error conditions.

Q.  Is windowing in effect throughout a Kermit session?

A.  No,  it  is  only  in effect during the actual data transfer (data packets)
    portion of a file transfer.  Windowing begins with the first data packet (D
    packet type), and stops when you get an End-of-File packet (Z packet type).

Q.  Why does it stop when you get to the End-of-File packet?

A.  This is done primarily to avoid having more than one file open at once.

Q.  Why  will  windowing  be  especially helpful at higher baud rates over com-
    munications paths that have delays?

A.  As you increase the baud rate, the  transmission  speed  of  the  data  in-
    creases, but you do not change the delay caused by the communications path.
    As a result, the delay becomes more and more significant.

    Assume, for example, that your communications path introduces a delay of  1
    second  each  way  for  packets, for a total delay of 2 seconds round trip.
    Assume also that your packets have 900 bits in  them  so  it  takes  you  3
    seconds to send a packet at 300 baud (this is roughly equivalent to a typi-
    cal Kermit packet).

    WITHOUT windowing, here is what happens:

    If at 300 baud you transmitted data for 3 seconds (sending 900 bits),  then
    waited  2 seconds for each acknowledgment, your throughput would be roughly
    180 baud.  (Total time for each transmission = 5 seconds.  900/5 = 180).

    However, if you went to 2400 baud, you would transmit data for 3/8  second,
    then  wait 2 seconds for an acknowledgment.  (Total time for each transmis-
    sion = 2 and 3/8 seconds).  The throughput would increase only to about 378
    baud. (900 / 2.375 = 378).

    The delay becomes the limiting factor; in this case, with this packet size,
    the delay sets an outside limit of 450 baud (900 / 2 second delay  =  450),
    no matter how fast the modem speed.

    WITH  windowing,  the throughput should be close to the actual transmission
    speed.  It should be possible to send data nearly continuously.  The  exact
    speed  will  depend  on the window size, length of transmission delays, and
    error rate.

Q.  Are there any new packet types introduced by this extension?

A.  No, the only change is to the contents of the Send-Init packet, to  arrange
    for  windowing if both sides can do it.  If either side cannot, Kermit will
    work as it does now.  Adding an extension such as this was provided for  in
    the  original Kermit definition.  See section 3 of the windowing definition
    for details.

Q.  On the receive side, in section 4.2, why does the definition say that writ-
    ing to disk is done when the Receive-Table becomes full rather than as soon
    as you get a good packet?

A.  The definition was phrased this way because  it  makes  the  logic  of  the
    receive side clearer and simpler to implement.

    Actually,  you  could  also write a packet to disk when it is a good packet
    and it is the earliest entry in the receive table.  This approach  has  the
    disadvantage that you don't know at this point that the sender has received
    your ACK, so you have to be prepared to handle the same packet later on  if
    the  sender never gets the ACK, times out, and sends the same packet again.
    Thus you have to be prepared to deal with packets previous to  the  current
    window; you will have to ACK such a packet if it has been received properly
    before.

    By writing packets to disk only when the receive table becomes  full,  (the
    oldest  packet)  you  know that the sender has received your ACK (otherwise
    the sender could not have rotated the window to the n+1  position  to  send
    the  current  packet, where n is the window size).  This makes it very easy
    to stay in synch with the sender.  The disadvantage  of  this  approach  is
    that  when you receive the End-of-File packet, you have to take the time to
    write all the remaining packets in the Receive-Table to disk.

Q.  Could you briefly explain what happens if a single packet gets corrupted?

A.  In essence, the receiver will ignore the bad packet.  When it gets the next
    good  packet,  it  will  realize (because packets are numbered) that one or
    more packets were lost, and NAK those packets.  The receiver  continues  to
    accept good data.

    As  long as the sender's window does not become "blocked", the only loss of
    throughput will be the time it takes to transmit the NAK'd packets.

Q.  There are currently two proposals for Kermit extensions: the Windowing  ex-
    tension  and a proposal for extended packet lengths.  What are the relative
    advantages  and  disadvantages  of  sliding  windows  and  extended  packet
    lengths?

A.  What is best depends on the exact conditions and systems involved in a par-
    ticular file transfer.  There are some general rules however.

    Windowing helps more and more as the communications path delays get longer.

    Windowing is also more and more helpful as the baud rate goes up.

    Increased packet length is most helpful on circuits with low  error  rates.
    If the error rate is high, it is difficult for a long packet to get through
    uncorrupted.  Also, it then  takes  longer  to  re-transmit  the  corrupted
    packet.

    On  some  machines, the CPU time to process a packet is relatively constant
    no matter what the packet length, so longer packets can reduce CPU time.

Q.  Are extended packet lengths and sliding windows mutually exlusive?

A.  No, there is no real reason that they would have to be.    As  a  practical
    matter,  it  is slightly easier to implement windowing if you know the max-
    imum packet size ahead of time, since you can then just  use  an  array  to
    store  your  data.    In standard Kermit, you know automactically that your
    maximum packet length is 94, so you can just go ahead and dimension an  ar-
    ray at 94 by Window-size.

    If you are going to use both extended packet length and windowing, you need
    to select the maximum packet length and window-size so that the combination
    does not exceed the available memory for each side of the transfer.

    In  addition, it is possible to see the desired relationship between packet
    size and windowing for various baud rates and communications delays.    For
    the  common  case  of  an error corrected by one retransmission of the cor-
    rupted packet, the minimum window size  needed  for  continuous  throughput
    (the window never gets "blocked") can be calculated by:

                    4 x delay x baud rate
      WS  >   1 +  ------------------------
                       packet-size x 10          (this is the # of bits)

    Windowing  always  helps  (the minimal continuous throughput window size is
    always greater than 1).

    In the above equation, the "4" derives  from  the  fact  that  a  corrupted
    packet has 4 transit times involved:

       - Original (bad checksum) packet
       - NAK for the packet
       - Retransmission of packet
       - ACK for retransmission.

    All of this must happen before the window becomes blocked.

    The  "delay"  is  the  effective maximum one-way communications path delay,
    which includes any CPU delays.

    Strictly speaking, the "packet-size" should have  the  length  of  the  ACK
    packets added to it.

    As an example, if you assume a 2-second (one-way) delay, at 1200 baud, with
    a packet size of 94, the minimum  window  size  for  continuous  throughput
    would be:

              4 x 2 x 1200
       WS  >  ------------    =   10.2
                94 x 10

    Under  these  circumstances, a window size of at least 11 should be chosen,
    if possible.


7.2.3. More Q-and-A About Windows

While reading the following questions and answers, keep in mind that the Kermit
windowing  definiton was developed to handle a common situation of long circuit
delays with possible moderate error rates.  Kermit does not need this  type  of
extension  for  clean  lines  with  insignificant delays - Kermit could be left
alone, or use Extended Packet Lengths, in such environments.

Long delays with significant error rates will occur under two obvious and  com-
mon conditions:

   1. Local  phone  line  (of  uncertain  quality) to Public Data Networks
      (such as Telenet).

   2. Satellite phone links.  These  often  occur  with  the  lower-priced
      phone  services,  which often also have noisier lines.  In addition,
      satellite links will increase as more people need to  transfer  data
      overseas.

The  above  conditions  will  become more common, as well increased baud rates,
which make the delays more significant.

As an aside, note that the benefit of Extended Packet Lengths over  the  Public
Data  Networks  is  limited  by the number of outstanding bytes the PDN allows.
(Internally, the PDNs require end-to-end acknowledgement.  They use  their  own
windowing  system within the network.)  I don't currently know the exact impact
of this.

Now on to the questions...

Q.  Can sliding windows be done on half-duplex channels?  Are any modifications
    to the proposal required?

A.  An underlying assumption in the development of windowing was that there was
    a full-duplex channel.

    The intent of windowing is to try to keep the sender  continuously  sending
    data.   Obviously, this is not possible on a half-duplex channel.  A better
    solution for half-duplex channels  would  be  to  use  an  extended  packet
    length.

    An  attempt  to  use windowing on half-duplex really is just a way of doing
    extended packet lengths.  The sender would send out  a  group  of  packets,
    then wait and get a group of ACKS.  It would be better to simply send out a
    large packet, which would have less overhead.

Q.  Is the cost in complexity for sliding windows worth the increase in perfor-
    mance?

A.  Under  the conditions described above (long delays and possibly significant
    error rates) windowing can increase performance by a factor  of  2,  3,  or
    more,  especially at higher baud rates.  This increase is necessary to make
    Kermit viable under some conditions.  With classic Kermit over  the  Public
    Data  Networks,  I  have  had througput as low as 250 baud over a 1200 baud
    circuit (with a negligible error rate).  Windowing should allow  throughput
    close to the maximum baud rate.

    Windowing is most helpful when the delay is significant in relation to data
    sending time.  Any delay becomes more significant as users move  to  higher
    baud rates (2400 baud and beyond).

    The  complexity  of  implementing  windowing has yet to be fully evaluated.
    The first implementation (for the IBM  PC  using  C-Kermit)  proved  to  be
    fairly  manageable.  It appears that the windowing logic can be implemented
    so that Kermit Classic uses the same code, but with a  window  size  of  1,
    which should avoid having to keep separate sections of code.

    The  windowing  definiton was developed with the idea of keeping changes to
    Kermit to a minimum.  No new packet types were  developed,  ACKs  and  NAKS
    were  kept  the  same,  and  windowing is in effect only during actual data
    transfer (D packets).  We tried to define the protocol  so  that  a  window
    size of 1 was the same as the current classic Kermit.

    These  factors should help reduce the complexity of implementing windowing.
    We currently have a working implementation of Kermit for the IBM  PC  going
    through testing.

    It's fun to see the modem "Send" light stay on constantly!

Q.  Why doesn't the Windowing proposal use a "bulk ACK"?

A.  There  are a couple of possibilities for ways to use some sort of "bulk" or
    combined ACK.  We looked at them when developing the Windowing  definition.
    We did not see any advantages that outweighed the disadvantages.

    Here are two possible ways of changing how ACKs would work:

       1. An  ACK for any packet would also ACK all previous packets.  The
          concept that an ACK would also ACK all  previous  packets  seems
          attractive  at  first, since it would appear to reduce overhead.
          However, it has a major drawback in that you then must  re-synch
          when  you  get errors.  This is because, once you have an error,
          you have to send a NAK, then stop and wait for a re-transmission
          of the NAK'd packet, before you send out any more ACKs.  (If you
          sent out an ACK for a later packet, it would imply that you  had
          received  the  NAK'd  packet.    Not  until  you  safely get the
          re-transmission can you go ahead.)  This would negate one of the
          nicest  parts  of  windowing as it is defined now, which is that
          the sender can transmit  continuously,  including  during  error
          recovery,  as  long  as  the window does not become blocked.  It
          does not appear to us that the reduction in the number  of  ACKs
          sent  is  worth  this penalty.  In addition, this is a departure
          from the way ACKs in Kermit work now.  It seemed best to make as
          few  changes  to Kermit as possible.  If this facility turns out
          to be useful, it would be better to introduce a new packet  type
          (or  other  means  of  distinguishing  regular  ACKs  from "Bulk
          ACKS").

       2. A new "Bulk ACK" packet type could be developed.  This  did  not
          seem  to  us to be a good idea, since it required defining a new
          packet type.  We were trying to fit windowing  in  with  as  few
          changes  to  Kermit  as  possible.    A "Bulk ACK", in which one
          packet could contain a whole string of ACKs and NAKs, also seems
          like  a  good  idea at first.  The penalty here is a little more
          subtle.  First, if you lose a "Bulk ACK" packet, you  lose  more
          information  and  it takes longer to get things flowing smoothly
          again.  Second, and probably more importantly, efficient window-
          ing  depends  on  the window never becoming "blocked" (i.e., the
          sender can always keep sending).  A "Bulk ACK"  interferes  with
          this to some extent, because if you have a long delay, the "Bulk
          ACK" with its multiple individual ACKs may not get back  to  the
          sender  in  time  to  prevent  the window from becoming blocked.
          With the current definition of windowing, returning an  ACK  for
          each  packet  gets  the  ACKs (or NAKs) to the sender as soon as
          possible.  This provides the best chance for keeping the  window
          open  so  that the sender can transmit continually.  Once again,
          remember the conditions under which windowing  is  most  useful:
          long  delays  with  significant  error  rates.  Under these con-
          ditions, individual ACKs have advantages.  If  these  conditions
          don't apply, it may not be necessary to use windowing, or it may
          be better to use extended packet lengths.
8. Kermit Commands

The following list of Kermit commands and terms is suggested.  It  is  not  in-
tended  to  recommend  a particular style of command parsing, only to promote a
consistent vocabulary, both in documentation and in choosing the names for com-
mands.


8.1. Basic Commands

SEND    This verb tells a Kermit program to send one or more files from its own
        file structure.

RECEIVE This verb should tell a Kermit program to expect one or more  files  to
        arrive.

GET     This  verb  should  tell a user Kermit to send one or more files.  Some
        Kermit implementations have separate RECEIVE and GET  commands;  others
        use RECEIVE for both purposes, which creates confusion.

Since  it  can be useful, even necessary, to specify different names for source
and destination files, these commands should take operands as follows (optional
operands in [brackets]):

SEND local-source-filespec [remote-destination-filespec]
        If the destination file specification is included, this will go in  the
        file header packet, instead of the file's local name.

RECEIVE [local-destination-filespec]
        If the destination filespec is given, the incoming file will be  stored
        under that name, rather than the one in the file header pakcet.

GET remote-source-filespec [local-destination-filespec]
        If the destination filespec is given, the incoming file will be  stored
        under that name, rather than the one in the file header packet.

If  a file group is being sent or received, alternate names should not be used.
It may be necessary to adopt  a  multi-line  syntax  for  these  commands  when
filespecs may contain characters that are also valid command field delimiters.


8.2. Program Management Commands

EXIT    Leave  the  Kermit  program, doing whatever cleaning up must be done --
        deassigning of devices, closing of files, etc.

QUIT    Leave the Kermit program without cleaning up, in such a  manner  as  to
        allow further manipulation of the files and devices.

PUSH    Preserve  the  current  Kermit environment and enter the system command
        processor.

TAKE    Read and execute Kermit program commands from a local file.

LOG     Specify a log for file transfer transactions, or for  terminal  session
        logging.


8.3. Terminal Emulation Commands

CONNECT This  verb,  valid  only  for a local Kermit, means to go into terminal
        emulation mode; present the illusion of being directly connected  as  a
        terminal  to the remote system.  Provide an "escape character" to allow
        the user to "get back" to the local system.  The escape character, when
        typed,  should take a single-character argument; the following are sug-
        gested:

            0   (zero) Transmit a NUL
            B   Transmit a BREAK
            C   Close the connection, return to local Kermit command level
            P   Push to system command processor
            Q   Quit logging (if logging is being done)
            R   Resume logging
            S   Show status of connection
            ?   Show the available arguments to the escape character
            (a second copy  of  the  escape  character):  Transmit  the  escape
                character itself

Lower  case  equivalents should be accepted.  If any invalid argument is typed,
        issue a beep.

Also see the SET command.


8.4. Special User-Mode Commands

These commands are used only by Users of Servers.

BYE     This command sends a message to the remote server to  log  itself  out,
        and upon successful completion, terminate the local Kermit program.

FINISH  This  command  causes  the remote server to shut itself down gracefully
        without logging out its job, leaving the local Kermit at Kermit command
        level, allowing the user to re-CONNECT to the remote job.


8.5. Commands Whose Object Should Be Specified

Some  Kermit implementations include various local file management services and
commands to invoke them.  For instance, an implementation might  have  commands
to  let  you  get  directory  listings, delete files, switch disks, and inquire
about free disk space without having to exit and restart the program.   In  ad-
dition,  remote  servers may also provide such services.  A user Kermit must be
able to distinguish between commands aimed at its own system and those aimed at
the remote one.  When any confusion is possible, such a command may be prefixed
by one of the following "object prefixes":

REMOTE  Ask the remote Kermit server to provide this service.

LOCAL   Perform the service locally.

If the "object prefix" is omitted, the command should be executed locally.  The
services include:

LOGIN   This  should  be  used  in its timesharing sense, to create an identity
        ("job", "session", "access", "account") on the system.

LOGOUT  To terminate a session that was initiated by LOGIN.

COPY    Make a new copy of the specified file with the specified name.

CWD     Change Working Directory.  This is ugly, but more  natural  verbs  like
        CONNECT and ATTACH are too imprecise.  CWD is the ARPAnet file transfer
        standard command to invoke this function.

DIRECTORY
        Provide  a  list  of  the  names, and possibly other attributes, of the
        files in the current working directory (or the specified directory).

DELETE  Delete the specified files.

ERASE   This could be a synomym for DELETE, since its meaning is clear.

            (It doesn't seem wise to include UNDELETE  or  UNERASE  in  the
            standard  list; most systems don't support such a function, and
            users' expectations should not be toyed with...)

KERMIT  Send a command to the remote Kermit server in its own interactive  com-
        mand syntax.

RENAME  Change the name of the specified file.

TYPE    Display the contents of the specified file(s) at the terminal.

SPACE   Tell how much space is used and available for storing files in the cur-
        rent working directory (or the specified directory).

SUBMIT  Submit the specified file(s) for background (batch) processing.

PRINT   Print the specified file(s) on a printer.

MOUNT   Request a mount of the specified tape, disk, or other removable storage
        medium.

WHO     Show  who  is  logged in (e.g. to a timesharing system), or give infor-
        mation about a specified user or network host.

MAIL    Send electronic mail to the specified user(s).

MESSAGE Send a terminal message (on a network or timesharing system).

HELP    Give brief information about how to use Kermit.

SET     Set various parameters relating to debugging, transmission, file  mode,
        and so forth.

SHOW    Display settings of SET parameters, capabilities in force, etc.

STATISTICS
        Give information about the performance of the most recent file transfer
        -- elapsed time, effective baud rate, various counts, etc.

HOST    Pass  the  given command string to the specified (i.e. remote or local)
        host for execution in its own command language.

LOGGING Open or close a transaction or debugging log.


8.6. The SET Command

A SET command should be provided to allow the user to tailor  a  connection  to
the  peculiarities  of the communication path, the local or remote file system,
etc.  Here are some parameters that should be SET-able:

BLOCK-CHECK
        Specify  the type of block check to be used: single character checksum,
        two-character checksum, 3-character CRC.

DEBUGGING
        Display  or  log  the  packet  traffic,  packet numbers, and/or program
        states.  Useful for debugging new versions of  Kermit,  novel  combina-
        tions of Kermit programs, etc.

DELAY   How  many seconds a remote (non-server) Kermit should wait before send-
        ing the Send-Init packet, to give the user time to escape back  to  the
        local Kermit and type a RECEIVE command.

DISPLAY Style of file transfer display (NONE, SERIAL, SCREEN, etc).

DUPLEX  For terminal emulation, specify FULL or HALF duplex echoing.

END-OF-LINE
        Specify any line terminator that must be used after a packet.

ESCAPE  Specify the escape character for terminal emulation.

FILE attributes
        Almost  any  of  the  attributes listed above in the Attributes section
        (6.5).  The most common need is to tell the Kermit program  whether  an
        incoming or outbound file is text or binary.

FLOW-CONTROL
        Specify the flow control mechanism for  the  line,  such  as  XON/XOFF,
        ENQ/ACK,  DTR/CTS,  etc.  Allow flow control to be turned off (NONE) as
        well as on.  Flow control is done only on full-duplex connections.

HANDSHAKE
        Specify  any  line-access  negotiation  that  must be used or simulated
        during file transfer.  For instance, a half duplex  system  will  often
        need to "turn the line around" after sending a packet, in order to give
        you permission to reply.  A common handshake is XON (^Q);  the  current
        user of the line transmits an XON when done transmitting data.

LINE    Specify  the line or device designator for the connection.  This is for
        use in a Kermit program that can run in either remote  or  local  mode;
        the  default  line  is the controlling terminal (for remote operation).
        If an external device is used, local operation is presumed.

LOG     Specify a local file in which to keep a log of the transaction.   There
        may  be logs for debugging purposes (packet traffic, state transitions,
        etc) and for auditing purposes (to record the name and  disposition  of
        each file transferred).

MARKER  Change  the  start-of-packet marker from the default of SOH (CTRL-A) to
        some other control character, in case one or both systems has  problems
        using CTRL-A for this purpose.

PACKET-LENGTH
        The maximum length for a packet.  This should normally be no less  than
        30  or  40, and can be greater than 94 only if the long-packet protocol
        extension is available, in which case it can be a much  larger  number,
        up  to  the maximum size allowed for the particular Kermit program (but
        never greater than 9024).  Short packets can be an advantage  on  noisy
        lines;  they  reduce  the  probabily  of a particular packet being cor-
        rupted, as well as the retransmission overhead when corruption does oc-
        cur.  Long packets boost performance on clean lines.

PADDING The  number  of  padding  characters  that  should  be sent before each
        packet, and what the padding character should be.  Rarely necessary.

PARITY  Specify the parity (ODD, EVEN, MARK, SPACE, NONE) of the physical  con-
        nection.   If other than none, the "8th bit" cannot be used to transmit
        data and must not be used by either side in block check computation.

PAUSE   How many seconds to pause after receiving a packet before  sending  the
        next  packet.  Normally 0, but when a system communication processor or
        front end has trouble keeping up with the traffic, a  short  pause  be-
        tween  packets  may  allow it to recover its wits; hopefully, something
        under a second will suffice.

PREFIX  Change the default prefix for control characters, 8-bit characters,  or
        repeated quantities.

PROMPT  Change  the  program's  prompt.  This is useful when running Kermit be-
        tween two systems whose prompt is  the  same,  to  eliminate  confusion
        about which Kermit you are talking to.

REPEAT-COUNT-PROCESSING
        Change the default for repeat count processing.  Normally, it  will  be
        done if both Kermit programs agree to do it.

RETRY   The  maximum number of times to attempt to send or receive a packet be-
        fore giving up.  The normal number is about 5, but the user  should  be
        able  to  adjust it according to the condition of the line, the load on
        the systems, etc.

TIMEOUT Specify the length of the timer to set when waiting for a packet to ar-
        rive.

WINDOW-SIZE
        Maximum number of unacknowledged packets outstanding, when the  sliding
        window option is available, usually between 4 and 31.


8.7. Macros, the DEFINE Command

In  addition  to the individual set commands, a "macro" facility is recommended
to allow users to combine the characteristics of specific systems into a single
SET option.  For example:

    DEFINE IBM = PARITY ODD, DUPLEX HALF, HANDSHAKE XON
    DEFINE UNIX = PARITY NONE, DUPLEX FULL
    DEFINE TELENET = PARITY MARK

This  could  be done by providing a fancy runtime parser for commands like this
(which could be automatically TAKEn from the user's Kermit initialization  file
upon program startup), or simply hardwired into the SET command table.

With  these  definitions  in  place, the user would simply type "SET IBM", "SET
UNIX", and so forth, to set up the program to communication to the remote  sys-
tem.
9. Kermit Programs


9.1. Terminal emulation

The local system must be able to act as a terminal so that the user can connect
to the remote system, log in, and start up the remote Kermit.

Terminal emulation should be provided by any Kermit program that runs  locally,
so that the user need not exit and restart the local Kermit program in order to
switch between terminal and protocol operation.  On smaller  systems,  this  is
particularly important for various reasons -- restarting the program and typing
in all the necessary SET commands is too inconvenient  and  time-consuming;  in
some  micros,  switching  in and out of terminal emulation may cause carrier to
drop, etc.

Only bare-bones terminal emulation need be supplied by Kermit; there is no need
to  emulate  any  particular  kind of "smart" terminal.  Simple "dumb" terminal
emulation is sufficient to do the job.  Emulation of fancier terminals is  nice
to  have, however, to take advantage of the remote system's editing and display
capabilities.  In some cases, microcomputer firmware will take  care  of  this.
To build emulation for a particular type of terminal into the program, you must
interpret and act upon escape sequences as they arrive at the port.

No error checking is done during  terminal  emulation.    It  is  "outside  the
protocol"; characters go back and forth "bare".  In this sense, terminal emula-
tion through Kermit is no better than actually using a real terminal.

Some Kermit implementations may allow logging of the terminal emulation session
to  a  local  file.  Such a facility allows "capture" of remote typescripts and
files, again with no error checking or  correction.    When  this  facility  is
provided,  it is also desirable to have a convenient way of "toggling" the log-
ging on and off.

If the local system does not provide system- or  firmware-level  flow  control,
like  XON/XOFF,  the  terminal emulation program should attempt to simulate it,
especially if logging is being done.

The terminal emulation facility should be able to handle either remote or local
echoing (full or half duplex), any required handshake, and it should be able to
transmit any parity required by the remote side or the communication medium.

A terminal emulator works by continuously sampling both console input from  the
local  terminal and input from the communication line.  Simple input and output
functions will not suffice, however, since if you ask for input from a  certain
device  and  there is none available, you will generally block until input does
become available, during which time you will be missing input  from  the  other
device.    Thus  you  must  have  a  way to bounce back and forth regardless of
whether input is available.  Several mechanisms are commonly used:

   - Continuously jump back and forth between the port status register and
     the  console  status  register,  checking  the  status bits for input
     available.  This is only  practical  on  single-user,  single-process
     systems, where the CPU has nothing else to do.

   - Issue an ordinary blocking input request for the port, but enable in-
     terrupts on console input, or vice versa.

   - Handle port input in one process and console input in another, paral-
     lel process.  The UNIX Kermit program listed in this manual uses this
     method.

Any input at the port should be displayed immediately on the screen.  Any input
from the console should be output immediately to the port.  In addition, if the
connection is half duplex, console input should also be sent immediately to the
screen.

The  terminal  emulation  code must examine each console character to determine
whether it is the "escape character".  If so, it should take the next character
as  a  special command, which it executes.  These commands are described above,
in section 8.3.

The terminal emulator should be able to send every ASCII character, NUL through
DEL,  and  it  should  also  be able to transmit a BREAK signal (BREAK is not a
character, but an "escape" from ASCII transmission in which a 0 is put  on  the
line  for  about  a  quarter  of a second, regardless of the baud rate, with no
framing bits).  BREAK is important when  communicating  with  various  systems,
such as IBM mainframes.

Finally, it is sometimes necessary to perform certain transformations on the CR
character that is normally typed to end a line of input.  Some systems use  LF,
EOT, or other characters for this function.  To complicate matters, intervening
communications equipment (particularly the public packet-switched networks) may
have  their  own independent requirements.  Thus if using Kermit to communicate
over, say, TRANSPAC with a system that uses  LF  for  end-of-line,  it  may  be
necessary to transform CR into LFCR (linefeed first -- the CR tells the network
to send the packet, which will contain the LF, and the host  uses  the  LF  for
termination).  The user should be provided with a mechanism for specifying this
transformation, a command like "SET CR sequence".


9.2. Writing a Kermit Program

Before writing a new implementation of Kermit or modifying an old one, first be
sure  to  contact the Kermit Distribution center at Columbia University to make
sure that you're not duplicating someone else's effort, and that you  have  all
the  latest material to work from.  If you do write or significantly modify (or
document) a Kermit program, please send it back to Columbia so that it  can  be
included  in  the  standard Kermit distribution and others can benifit from it.
It is only through this kind of sharing that Kermit has grown from  its  modest
beginnings to its present scale.

The following sections provide some hints on Kermit programming.


9.2.1. Program Organization

A  basic  Kermit  implementation  can  usually be written as a relatively small
program, self-contained in a single source file.  However, it is often the case
that  a  program  written  to run on one system will be adapted to run on other
systems as well.  In that case, it is best to avoid  having  totally  divergent
sources,  because when new features are added to (or bugs fixed in) the system-
independent parts of the program -- i.e. to the protocol itself -- only one im-
plementation will reap the benefits initially, and the other will require pain-
ful, error-prone "retrofitting" to bring it up to the same level.

Thus, if there is any chance that a Kermit program will run on  more  than  one
machine, or under more than one operating system, or support more than one kind
of port or modem, etc, it is desirable to isolate the system-dependent parts in
a way that makes the common parts usable by the various implementations.  There
are several approaches:

   1. Runtime support.  If possible, the program can inspect the  hardware
      or  inquire  of  the system about relevant parameters, and configure
      itself dynamically at startup time.  This is hardly ever possible.

   2. Conditional compilation (or assembly).  If the number of systems  or
      options  to  be supported is small, the system dependent code can be
      enclosed in conditional compilation brackets (like IF IBMPC .... EN-
      DIF).  However, as the number of system dependencies to be supported
      grows, this method becomes unwieldy and  error-prone  --  installing
      support  for  system  X  tends to break the pre-existing support for
      system Y.

   3. Modular composition.  When there is a potentially  large  number  of
      options  a  program  should  support,  it  should  be broken up into
      separate modules (source  files),  with  clearly  specified,  simple
      calling conventions.  This allows people with new options to provide
      their own support for them in an easy way, without  endangering  any
      existing support.  Suggested modules for a Kermit program are:

   4.

         - System-Indendent  protocol  handling:  state  switching, packet
           formation, encoding (prefixing) and decoding, etc.

         - User Interface: the command parser.  Putting this in a separate
           module  allows  plug-in  of  command parsers to suit the user's
           taste, to mimic the style of the host system command parser  or
           some popular application, etc.

         - Screen i/o: This module would contain the screen control codes,
           cursor positioning routines, etc.

         - Port i/o: Allows support of various port hardware.  This module
           can  define the port status register location, the status bits,
           and so forth, and can implement the functions to read and write
           characters at the port.

         - Modem  control:  This  module would support any kind of "intel-
           ligent" modem, which is not simply a transparent  extension  of
           the  communications  port.  Such modems may accept special com-
           mands to perform functions like dialing out, redialing a recent
           number,  hanging  up, etc., and may need special initialization
           (for instance, setting modem signals like DTR).

         - Console input: This module would supply  the  function  to  get
           characters  from  the  console;  it would know about the status
           register  locations  and  bits,  interrupt  structure,  key-to-
           character   mappings,   etc.,  and  could  also  implement  key
           redefinitions, keystroke macros,  programmable  function  keys,
           expanded control and meta functions, etc.

         - Terminal  Emulation:  This  module  would  interpret escape se-
           quences in the incoming character  stream  (obtained  from  the
           port i/o module) for the particular type of terminal being emu-
           lated and interpret them by making appropriate  calls  the  the
           screen i/o module, and it would send user typein (obtained from
           the console input module) out the serial port (again using  the
           port  i/o module).  Ideally, this module could be replacable by
           other modules to emulate different  kinds  of  terminals  (e.g.
           ANSI, VT52, ADM3A, etc).

         - File i/o: This module contains all the knowledge about the host
           system's file structure; how to open and close  files,  perform
           "get next file" operations, read and write files, determine and
           set their attributes, detect the end of a file, and  so  forth,
           and  provides  the  functions,  including  buffering,  to get a
           character from a file and put a character  to  a  file.    This
           module  may  also  provide  file  management services for local
           files -- directory listings, deleting, renaming,  copying,  and
           so forth.

         - Definitions  and  Data: Separate modules might also be kept for
           compile-time parameter definitions and for global runtime data.
9.2.2. Programming Language

The language to be used in writing a Kermit program is more than  a  matter  of
taste.    The  primary consideration is that the language provide the necessary
functionality and speed.  For instance, a microcomputer implementation of BASIC
may  not  allow  the  kind of low-level access to device registers needed to do
terminal emulation, or to detect console input during file transfer, or even if
it  can  do  these things, it might not be able to run fast enough do drive the
communication line at the desired baud rate.

The second consideration in choosing a language is portability.  This  is  used
in  two  senses:  (1)  whether the language is in the public domain (or, equiv-
alently, provided "free" as part of the basic system), and (2)  whether  it  is
well  standardized and in wide use on a variety of systems.  A language that is
portable in both senses is to be preferred.

Whatever programming language is selected, it is important that  all  lines  in
the  program source be kept to 80 characters or less (after expansion of tabs).
This is because Kermit material must often be shipped over RJE and other  card-
format communication links.

In  addition,  it is important that the names of all files used in creating and
supporting a particular Kermit implementation be (possibly  a  subset)  of  the
form NAME.TYPE, where NAME is limited to six characters, and TYPE is limited to
three, and where the NAME of each file begin with a common  2  or  3  character
prefix.    This is so that all related files will be grouped together in an al-
phabetic directory listing, and so when all of the hundreds of  Kermit  related
files  are  placed together on a tape, all names will be both legal and unique,
especially on systems (like PDP-11 operating  systems)  with  restrictive  file
naming conventions.


9.2.3. Documentation

A  new  Kermit program should be thoroughly documented; one of the hallmarks of
Kermit is its documentation.  The documentation should  be  at  both  the  user
level  (how  to  use  the  program,  what the commands are, etc, similar to the
documentation presently found in the Kermit Users  Guide),  and  the  implemen-
tation  level  (describe system dependencies, give pointers for adapting to new
systems, and so forth).    In  addition,  programs  themselves  should  contain
copious  commentary.   Like program source, documentation should be kept within
80-character lines.

If possible, a section for the implementation should be written for the  Kermit
User  Guide using the UNILOGIC Scribe formatting language (subsets of which are
also to be found in some microcomputer text processing software such as Perfect
Writer  or  Final  Word),  using  the  same general conventions as the existing
Scribe-format implementation sections.

Kermit programs should also contain a revision history, in which each change is
briefly  explained,  assigned an "edit number", and the programmer and site are
identified.  The lines or sections comprising the edit should  be  marked  with
the corresponding edit number, and the Kermit program, upon startup, should an-
nounce its version and edit numbers, so that when users complain of problems we
will know what version of the program is in question.

The version number changes when the functionality has been changed sufficiently
to require major revisions of user documentation.  The edit number  should  in-
crease  (monotonically,  irrespective  of  version number) whenever a change is
made to the program.  The edit numbers are very important for  program  manage-
ment;  after  shipping  out a version of, say, CP/M Kermit-80, we often receive
many copies of it, each containing its own set of changes, which we must recon-
cile in some manner.  Edit numbers help a great deal here.


9.2.4. Bootstrapping

Finally,  a  bootstrap  procedure should be provided.  Kermit is generally dis-
tributed on magnetic tape to large central sites; the users at those sites need
ways of "downloading" the various implementations to their micros and other lo-
cal systems.  A simple bootstrap procedure would consist  of  precise  instruc-
tions  on  how  to accomplish an "unguarded" capture of the program.  Perhaps a
simple, short program can be written for each each end that will  do  the  job;
listings and instructions can be provided for the user to type in and run these
programs.
I. Packet Format and Types

Basic Kermit Packet Layout


       |<------Included in CHECK------>|
       |                               |
+------+-----+-----+------+------ - - -+-------+
| MARK | LEN | SEQ | TYPE | DATA       | CHECK |<terminator>
+------+-----+-----+------+------ - - -+-------+
             |                                 |
             |<--------LEN-32 characters------>|

 MARK   A real control character, usually CTRL-A.
  LEN   One character, length of remainder of packet + 32, max 95
  SEQ   One character, packet sequence number + 32, modulo 64
 TYPE   One character, an uppercase letter
CHECK   One, two, or three characters, as negotiated.

<terminator>  Any control character required for reading the packet.

Kermit Extended Packet Layout

       |<-------------------------Included in CHECK------------->|
       |                                                         |
       |<-------Included in HCHECK------->|                      |
       |                                  |                      |
+------+-----+-----+------+-------+-------+--------+----- - - - -+-------+
| MARK |     | SEQ | TYPE | LENX1 | LENX2 | HCHECK | DATA        | CHECK |
+------+-----+-----+------+-------+-------+--------+----- - - - -+-------+
        blank                                      |                     |
                                                   |<------------------->|
                    LX1=LENX1-32, LX2=LX2-32         95 x LX1 + LX2 chars

HCHECK is a single-character type 1 checksum

Initialization String

 1       2       3       4       5       6       7       8       9       10
+-------+-------+-------+-------+-------+-------+-------+-------+-------+- -
| MAXL  | TIME  | NPAD  | PADC  | EOL   | QCTL  | QBIN  | CHKT  | REPT  |
+-------+-------+-------+-------+-------+-------+-------+-------+-------+- -

     10              CAPAS+1  CAPAS+2  CAPAS+3
- --+-------+-     -+--------+--------+--------+- -
    | CAPAS    ... 0| WINDO  | MAXLX1 | MAXLX1 |
- --+-------+-     -+--------+--------+--------+- -

MAXL    Maximum length (0-94) +32
TIME    Timeout, seconds (0-94) +32
NPAD    Number of pad characters (0-94) +32
EOL     Packet terminator (0-63) +32
QCTL    Control prefix, literal
QBIN    8th bit prefix, literal
CHKT    Block check type {1,2,3}, literal
REPT    Repeat count prefix, literal
CAPAS   Extendable capabilities mask, ends when value-32 is even
WINDO   Window size (0-31) +32
MAXLX1  High part of extended packet maximum length (int(max/95)+32)
MAXLX2  Low part of extended packet maximum length (mod(max,95)+32)

Packet Types

Y   Acknowledgment (ACK).  Data according to what kind of packet is  being  ac-
    knowledged.
N   Negative Acknowledgment (NAK).  Data field always empty.
S   Send  Initiation.    Data  field  contains unencoded initialization string.
    Tells receiver to expect files.  ACK to this packet also contains unencoded
    initialization string.
I   Initialize.   Data field contains unencoded initialization string.  Sent to
    server to set parameters prior to a command.  ACK to this packet also  con-
    tains unencoded initialization string.
F   File  Header.    Indicates  file data about to arrive for named file.  Data
    field contains encoded file name.  ACK to this packet may  contain  encoded
    name receiver will store file under.
X   Text  Header.   Indicates screen data about to arrive.  Data field contains
    encoded heading for display.
A   File Attributes.  Data field contains unencoded attributes.  ACK  may  con-
    tain unencoded corresponding agreement or refusal, per attribute.
D   Data  Packet.    Data  field contains encoded file or screen data.  ACK may
    contain X to interrupt sending this file,  Z  to  interrupt  entire  trans-
    action.
Z   End of file.  Data field may contain D for Discard.
B   Break transmission.
E   Error.  Data field contains encoded error message.
R   Receive Initiate.  Data field contains encoded file name.
C   Host  Command.    Data  field  contains  encoded command for host's command
    processor.
K   Kermit Command.  Data field contains encoded  command  for  Kermit  command
    processor.
T   Timeout psuedopacket, for internal use.
Q   Block check error psuedopacket, for internal use.
G   Generic Kermit Command.  Data field contains a single character subcommand,
    followed by zero or more length-encoded operands, encoded after formation:

    I   Login [<%user[%password[%account]]>]
    C   CWD, Change Working Directory [<%directory[%password]>]
    L   Logout, Bye
    F   Finish (Shut down the server, but don't logout).
    D   Directory [<%filespec>]
    U   Disk Usage Query [<%area>]
    E   Erase (delete) <%filespec>
    T   Type <%filespec>
    R   Rename <%oldname%newname>
    K   Copy <%source%destination>
    W   Who's logged in? [<%user ID or network host[%options]>]
    M   Send a short Message <%destination%text>
    H   Help [<%topic>]
    Q   Server Status Query
    P   Program <%[program-filespec][%program-commands]>
    J   Journal <%command[%argument]>
    V   Variable <%command[%argument[%argument]]>
II. List of Features

There's no true linear scale along which to rate  Kermit  implementations.    A
basic,  minimal  implementation provides file transfer in both directions, and,
for microcomputers (PC's, workstations, other single  user  systems),  terminal
emulation.  Even within this framework, there can be variations.  For instance,
can the program send a file group in a single command, or  must  a  command  be
issued for each file?  Can it time out?  Here is a list of features that may be
present; for any Kermit implementation, the documentation should  show  whether
these features exist, and how to invoke them.

   - File  groups.    Can  it send a group of files with a single command,
     using "wildcard", pattern, or list notation?    Can  it  successfully
     send or receive a group of files of mixed types?  Can it recover from
     an error on a particular file and go on to the next one?  Can it keep
     a log of the files involved showing the disposition of each?

   - Filenames.  Can it take action to avoid overwriting a local file when
     a new file of the same name arrives?  Can it convert filenames to and
     from legal or "normal form"?

   - File types.  Can binary as well as text files be transmitted?

   - 8th-Bit  prefixing.    Can  it  send and receive 8-bit data through a
     7-bit channel using the prefixing mechanism?

   - Repeat-Count processing.  Can it send and receive data with  repeated
     characters replaced by a prefix sequence?

   - Terminal  Emulation.    Does  it  have a terminal emulation facility?
     Does it emulate a particular terminal?  To  what  extent?    Does  it
     provide  various  communication  options, such as duplex, parity, and
     handshake selection?  Can it transmit all ASCII characters?   Can  it
     transmit BREAK?  Can it log the remote session locally?

   - Communications Options.  Can duplex, parity, handshake, and line ter-
     minator be specified for file transfer?

   - Block Check Options.   In  addition  to  the  basic  single-character
     checksum,  can the two-character checksum and the three-character CRC
     be selected?

   - Basic Server.  Can it run in server mode, accepting commands to  send
     or receive files, and to shut itself down?

   - Advanced  Server.    Can  it  accept server commands to delete files,
     provide directory listings, send messages, and forth?

   - Issue Commands to Server.  Can it send  commands  to  a  server,  and
     handle all possible responses?

   - Host  Commands.  Can it parse and send remote "host commands"?  If it
     is a server, can it pass these commands to the  host  system  command
     processor and return the results to the local user Kermit?

   - Interrupt  File  Transfers.   Can it interrupt sending or receiving a
     file?  Can it respond to interrupt requests from the other side?

   - Local File Management Services.  Are  there  commands  to  get  local
     directory listings, delete local files, and so forth?

   - File  Attributes.  Can it send file attribute information about local
     files, and can deal with incoming file attribute  information?    Can
     alternate dispositions be specified.  Can files be archived?

   - Long Packets.  Is the long packet protocol extension implemented?

   - Sliding  Windows.    Is  the  sliding  window  protocol extension im-
     plemented?

   - Debugging Capability.    Can  packet  traffic  be  logged,  examined,
     single-stepped?

   - Frills.    Does  it have login scripts?  Raw download/upload?  A DIAL
     command and modem control?  Phone directories?
III. The ASCII Character Set

ASCII Code (ANSI X3.4-1968)

There are 128 characters in the ASCII (American national Standard Code for  In-
formation Interchange) "alphabet".  The characters are listed in order of ASCII
value; the columns are labeled as follows:

Bit             Even parity bit for ASCII character.
ASCII Dec       Decimal (base 10) representation.
ASCII Oct       Octal (base 8) representation.
ASCII Hex       Hexadecimal (base 16) representation.
EBCDIC Hex      EBCDIC hexadecimal equivalent for Kermit translate tables.
Char            Name or graphical representation of character.
Remark          Description of character.

The first group consists of nonprintable 'control' characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   000   000   00   00    NUL   ^@, Null, Idle
 1   001   001   01   01    SOH   ^A, Start of heading
 1   002   002   02   02    STX   ^B, Start of text
 0   003   003   03   03    ETX   ^C, End of text
 1   004   004   04   37    EOT   ^D, End of transmission
 0   005   005   05   2D    ENQ   ^E, Enquiry
 0   006   006   06   2E    ACK   ^F, Acknowledge
 1   007   007   07   2F    BEL   ^G, Bell, beep, or fleep
 1   008   010   08   16    BS    ^H, Backspace
 0   009   011   09   05    HT    ^I, Horizontal tab
 0   010   012   0A   25    LF    ^J, Line feed
 1   011   013   0B   0B    VT    ^K, Vertical tab
 0   012   014   0C   0C    FF    ^L, Form feed (top of page)
 1   013   015   0D   0D    CR    ^M, Carriage return
 1   014   016   0E   0E    SO    ^N, Shift out
 0   015   017   0F   0F    SI    ^O, Shift in
 1   016   020   10   10    DLE   ^P, Data link escape
 0   017   021   11   11    DC1   ^Q, Device control 1, XON
 0   018   022   12   12    DC2   ^R, Device control 2
 1   019   023   13   13    DC3   ^S, Device control 3, XOFF
 0   020   024   14   3C    DC4   ^T, Device control 4
 1   021   025   15   3D    NAK   ^U, Negative acknowledge
 1   022   026   16   32    SYN   ^V, Synchronous idle
 0   023   027   17   26    ETB   ^W, End of transmission block
 0   024   030   18   18    CAN   ^X, Cancel
 1   025   031   19   19    EM    ^Y, End of medium
 1   026   032   1A   3F    SUB   ^Z, Substitute
 0   027   033   1B   27    ESC   ^[, Escape, prefix, altmode
 1   028   034   1C   1C    FS    ^\, File separator
 0   029   035   1D   1D    GS    ^], Group separator
 0   030   036   1E   1E    RS    ^^, Record separator
 1   031   037   1F   1F    US    ^_, Unit separator
The last four are usually associated with the  control  version  of  backslash,
right  square  bracket,  uparrow (or circumflex), and underscore, respectively,
but some terminals do not transmit these control characters.
The following characters are printable:
First, some punctuation characters.

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 1   032   040   20   40    SP    Space, blank
 0   033   041   21   5A    !     Exclamation mark
 0   034   042   22   7F    "     Doublequote
 1   035   043   23   7B    #     Number sign, pound sign
 0   036   044   24   5B    $     Dollar sign
 1   037   045   25   6C    %     Percent sign
 1   038   046   26   50    &     Ampersand
 0   039   047   27   7D    '     Apostrophe, accent acute
 0   040   050   28   4D    (     Left parenthesis
 1   041   051   29   5D    )     Right parenthesis
 1   042   052   2A   5C    *     Asterisk, star
 0   043   053   2B   4E    +     Plus sign
 1   044   054   2C   6B    ,     Comma
 0   045   055   2D   60    -     Dash, hyphen, minus sign
 0   046   056   2E   4B    .     Period, dot
 1   047   057   2F   61    /     Slash
Numeric characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   048   060   30   F0    0     Zero
 1   049   061   31   F1    1     One
 1   050   062   32   F2    2     Two
 0   051   063   33   F3    3     Three
 1   052   064   34   F4    4     Four
 0   053   065   35   F5    5     Five
 0   054   066   36   F6    6     Six
 1   055   067   37   F7    7     Seven
 1   056   070   38   F8    8     Eight
 0   057   071   39   F9    9     Nine
More punctuation characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   058   072   3A   7A    :     Colon
 1   059   073   3B   5E    ;     Semicolon
 0   060   074   3C   4C    <     Left angle bracket
 1   061   075   3D   7E    =     Equal sign
 1   062   076   3E   6E    >     Right angle bracket
 0   063   077   3F   6F    ?     Question mark
 1   064   100   40   7C    @     "At" sign
Upper-case alphabetic characters (letters):

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   065   101   41   C1    A
 0   066   102   42   C2    B
 1   067   103   43   C3    C
 0   068   104   44   C4    D
 1   069   105   45   C5    E
 1   070   106   46   C6    F
 0   071   107   47   C7    G
 0   072   110   48   C8    H
 1   073   111   49   C9    I
 1   074   112   4A   D1    J
 0   075   113   4B   D2    K
 1   076   114   4C   D3    L
 0   077   115   4D   D4    M
 0   078   116   4E   D5    N
 1   079   117   4F   D6    O
 0   080   120   50   D7    P
 1   081   121   51   D8    Q
 1   082   122   52   D9    R
 0   083   123   53   E2    S
 1   084   124   54   E3    T
 0   085   125   55   E4    U
 0   086   126   56   E5    V
 1   087   127   57   E6    W
 1   088   130   58   E7    X
 0   089   131   59   E8    Y
 0   090   132   5A   E9    Z
More punctuation characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 1   091   133   5B   AD    [     Left square bracket
 0   092   134   5C   E0    \     Backslash
 1   093   135   5D   BD    ]     Right square bracket
 1   094   136   5E   5F    ^     Circumflex, up arrow
 0   095   137   5F   6D    _     Underscore, left arrow
 0   096   140   60   79    `     Accent grave
Lower-case alphabetic characters (letters):

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 1   097   141   61   81    a
 1   098   142   62   82    b
 0   099   143   63   83    c
 1   100   144   64   84    d
 0   101   145   65   85    e
 0   102   146   66   86    f
 1   103   147   67   87    g
 1   104   150   68   88    h
 0   105   151   69   89    i
 0   106   152   6A   91    j
 1   107   153   6B   92    k
 0   108   154   6C   93    l
 1   109   155   6D   94    m
 1   110   156   6E   95    n
 0   111   157   6F   96    o
 1   112   160   70   97    p
 0   113   161   71   98    q
 0   114   162   72   99    r
 1   115   163   73   A2    s
 0   116   164   74   A3    t
 1   117   165   75   A4    u
 1   118   166   76   A5    v
 0   119   167   77   A6    w
 0   120   170   78   A7    x
 1   121   171   79   A8    y
 1   122   172   7A   A9    z
More punctuation characters:

     .....ASCII.... EBCDIC
Bit  Dec   Oct  Hex  Hex    Char  Remarks
 0   123   173   7B   C0     {    Left brace (curly bracket)
 1   124   174   7C   4F     |    Vertical bar
 0   125   175   7D   D0     }    Right brace (curly bracket)
 0   126   176   7E   A1     ~    Tilde

Finally, one more nonprintable character:

 0    127   177  7F   07    DEL   Delete, rubout