HH     HH  PPPPPPPP    8888888    6666666
                   HH     HH  PP     PP  88     88  66
                   HH     HH  PP     PP  88     88  66
                   HHHHHHHHH  PPPPPPPP    8888888   66666666
                   HH     HH  PP         88     88  66     66
                   HH     HH  PP         88     88  66     66
                   HH     HH  PP          8888888    6666666



        KK    KKK  EEEEEEEE  RRRRRRRR    MMM     MMM  IIIIII  TTTTTTTTTT
        KK   KKK   EE        RR     RR   MMMM   MMMM    II        TT
        KK  KKK    EE        RR     RR   MM MM MM MM    II        TT
        KKKKK      EEEEEEE   RRRRRRRR    MM  MMM  MM    II        TT
        KKKKKK     EE        RR RRR      MM   M   MM    II        TT
        KK  KKK    EE        RR   RRR    MM       MM    II        TT
        KK    KKK  EEEEEEEE  RR     RRR  MM       MM  IIIIII      TT



















                                     - 1 -










                            ======================
                            HP86 KERMIT USER GUIDE
                            ======================
                                Edition 1.00

                      This Manual applies to version 1.00

                                   CONTENTS
                                   --------

      1. Introduction.

      2. What is Kermit.

      3. Running Kermit on the HP86.
         3.1 Starting the HP86 Kermit.
         3.2 Entering Kermit commands.
         3.3 HP86 Kermit commands.
         3.4 Using Kermit.
         3.5 Finishing Kermit.

      4. Communicating with another computer.
         4.1 Setting the RS232.
         4.2 Using the HP86 as a terminal.
             4.2.1 The CONNECT command.
             4.2.2 Differences between command mode and terminal mode.
             4.2.3 Sending a break.
             4.2.4 Returning to the HP86 Kermit.

      5. Transferring files using Kermit.
         5.1 The basic method.
         5.2 File types.
             5.2.1 The file type problem.
             5.2.2 The data type problem.
         5.3 HP86 to remote file transfer - The SEND command.
         5.4 Remote to HP86 file transfer - The RECEIVE command.
         5.5 Transfer problems.
         5.6 File name conversion.
             5.6.1 HP86 to standard conversion.
             5.6.2 Standard to HP86 conversion.
             5.6.3 File renaming.

      6. Changing Kermit attributes.
         6.1 The SET command.
         6.2 The SHOW command.
         6.3 Settable attributes.

      Appendix A - HP86 Kermit capabilities.

      Appendix B - HP86 Kermit error messages.

      Appendix C - Converting numeric variables.


                                     - 2 -










      1. INTRODUCTION
      ===============

      Program:       Martin Rootes, Sheffield City Polytechnic, U.K.
      Language:      HP86 Basic.
      Documentation: Martin Rootes.
      Version:       1.00
      Date:          April 1986

        This manual describes the Kermit program for the HP86 microcomputer
     produced  by  the  Computer  Services  Department  of  Sheffield  City
     Polytechnic.       The   implementation   described   is   HP86 Kermit
     version 1.00. The purpose of this manual is to supply  the  user  with
     the information necessary to enable them to transfer files from a HP86
     microcomputer to another Kermit.  As transfer will almost always be to
     a  different  system the user will also have to read the corresponding
     guide for the other Kermit.

       This manual has been divided into  various  chapters,  dealing  with
     various  aspects of the HP86 Kermit. For users new to Kermit Chapter 2
     describes what Kermit is, the way it works, and why it is better  than
     some  other  methods  of  file  transfer.    Chapter 3 details the way
     HP86 Kermit is run, how to enter commands, brief descriptions  of  the
     commands,  and  how  they are used.   Chapter 4 deals with setting the
     HP86 Kermit up to communicate with another computer, and how to use it
     as a  terminal  for  a  mainframe.    Chapter  5  gives  comprehensive
     information on how to transfer files, and the problems associated with
     transfer.    Following these are various chapters giving more detailed
     information on commands and some hints and tips.


       The HP86 Kermit version 1.00 is written in HP86 BASIC and needs  the
     binary  program UTIL/1 to be loaded to provide various extra commands,
     this program is provided with the HP86 microcomputer on the demo disk.

       HP86 Kermit version 1.00 was developed, written  and  tested  on  an
     Hewlett  Packard  HP86 microcomputer with a HP 82939A Serial interface
     and the I/O programming ROM installed. Due to being written  in  BASIC
     it  will  very probably work with the HP87 as long as the same I/O ROM
     and interface are fitted, however this has not as yet been tested.














                                     - 3 -










      2. WHAT IS KERMIT
      ==================

       Kermit is a data transfer system devised by the Center for Computing
     Activities at the University of  Columbia,  New  York  (CUCCA).    The
     copyright  on Kermit is retained by CUCCA, however they have published
     full information on it and permit anyone  to  implement  it  on  their
     machines, as long as this is not for commercial purposes.  Due to this
     policy  Kermit  is now available for a large range of computers: There
     are  implementations  for  nearly  all  mainframes  and  most  popular
     microcomputers.

         The  basic idea behind Kermit is to allow the transfer of any data
     between different systems, in a uniform manner, and producing a usable
     file on the receiving system. There are other methods of data transfer
     that could be used, most notably 'dumb capture',  however  Kermit  has
     several advantages over this method.

         Most  simple  terminal emulator programs will allow some degree of
     data transfer in the form of 'dumb capture'.  This is a method whereby
     as characters are received from the mainframe they  are  placed  in  a
     file, as well as being displayed on screen.  The reverse process being
     to  take  characters  from a file on the microcomputer, instead of the
     keyboard, and transmit them to the mainframe.

       The dumb capture method, although fast and easy  to  implement,  has
     many  problems  associated  with  it.  These  are  due  to  the  RS232
     communications system used to link the computers, and  the  manner  in
     which it is used.

       The first problem is caused by parity, as many mainframe systems use
     one bit of a byte for error checking, the 'parity' bit, only the lower
     7  bits  of  a byte can be used to transmit data, thus only characters
     with codes between 0 and 127 will be able to be sent.

       Secondly communications systems commonly use certain  characters  as
     control  characters,  these  can  therefore not be sent as part of the
     data without causing problems, control codes lie in the range 0 to  31
     and sometimes include 127.

         Thirdly  in  a dumb capture system no error checking is performed,
     this means that the file received may not necessarily be the  same  as
     the  file  sent,  due  to  transmission  faults  as  well as the above
     problems.










                                     - 4 -










        Kermit  overcomes  these  problems  by  encoding  the  data  to  be
     transferred  using a standard set of rules, the Kermit 'protocol'. The
     rules have been designed  to  allow  transmission  of  any  character,
     regardless  of  any  parity  or  control  codes,  with  adequate error
     checking to ensure that the file received is  the  same  as  the  file
     sent.

       The full Kermit protocol is beyond the scope of this manual, however
     the basic method will be described here to aid in the comprehension of
     following  discussions,  if more detail is required consult the Kermit
     protocol manual (5th edition).

       Kermit transfers data by dividing data up into  individual  packets,
     each  packet  containing  the  data  itself  plus  some  extra control
     information.  This information is used by the receiving Kermit to give
     the start of packet, the sequence number of the packet, the length  of
     packet,  the  type  of  packet  and  finally  a check byte. Using this
     information the receiving Kermit can verify the  data  and  check  for
     missing packets.

         If  a  character needs to be sent whose code falls into one of the
     problem areas as mentioned above (0-32, 128-255), Kermit will  convert
     it  into  a  sequence of two 'legal' characters using prefix encoding.
     This is achieved in the following manner, if  for  example  a  control
     code  needs  to be sent as data it is first converted into a printable
     character, corresponding with the  standard  representation  of  these
     codes,  for  instance ASCII 13, usually called control M, is converted
     to the letter M. This is  then  prefixed  with  the  prefix  character
     (default - #), thus ASCII 13 will be sent as '#M'. A similar method is
     used  to  encode  data  with  the 8th bit set using the 8th bit prefix
     (default - &).

        After sending a packet Kermit will  wait  for  a  packet  from  the
     receiving  Kermit  to  confirm  that the packet has arrived correctly,
     this is called the acknowledge packet (ACK). If  for  any  reason  the
     packet is not received correctly the receiving Kermit sends a negative
     acknowledge  (NAK),  this  causes  the  sender  to retransmit the last
     packet. Thus if transmission errors occur Kermit will not only  detect
     the error it will try to remedy the situation by repeating the data.

       Although ensuring safe transmission of data this method can, without
     adequate  safeguards, cause the system to become 'hung', however there
     two mechanisms employed to stop this, timeouts and the retry limit.

       The purpose of the timeout is to avoid the situation where  the  two
     Kermits  are  each waiting for a packet from the other, this can occur
     when a packet is lost in transmission. A timeout is basically  a  time
     limit  on  the  receiving  of packets, if after the limit has passed a
     packet has still not been received the Kermit  will  assume  that  the
     last one it had sent was lost and will retransmit it.




                                     - 5 -










         The  retry limit is, as its name implies, a limit on the number of
     times that Kermit will try to retransmit a  particular  packet  before
     giving  up.  This  is to prevent the Kermit from endlessly sending the
     same packet to a Kermit that is either  not  replying,  or  is  having
     severe transmission problems.

       The result of using the Kermit protocol is a simple, highly reliable
     system  of  data transfer, that can be, and has been, implemented on a
     wide variety of machines ranging from  microcomputers  to  mainframes.
     The  only  requirements  needed  to  transfer  data  from the HP86 and
     another computer are two Kermit programs, one for the HP86 and one for
     the target computer, and the existence of  a  RS232  serial  interface
     port  on  both  machines.  The  great  advantage  of  Kermit over data
     transfer  programs  written  for  specific  machines   is   its   wide
     availability,  making  it  possible to transfer data to many different
     machines using the same program.






































                                     - 6 -










      3. RUNNING KERMIT ON THE HP86
      =============================

       This section describes the general operation of the HP86 Kermit, how
     to start it and how to enter commands.


      3.1 STARTING THE HP86 KERMIT
      ----------------------------

       To run Kermit on the HP86 the disk containing the Kermit program and
     the utility programs should be inserted in the  disk  drive  (if  your
     HP86  has  more  than one disk drive insert in drive 0). The following
     procedure should now be taken:-

       LOAD "Kermit"      <--- Load the Kermit program.
       LOADBIN "UTIL/1"   <--- Load the utility program.
       <INIT>             <--- Press the INIT button.
       <RUN>              <--- Press the RUN button.

      After about 80 secs the program will display the following prompt:-

       Kermit-HP86 > Enter command ?

      If this does not happen the RUN button should be pressed again.


      3.2 ENTERING KERMIT COMMANDS
      ----------------------------

       To control the HP86 Kermit commands have to be issued to it, this is
     done by entering the desired  command  in  the  space  underneath  the
     Kermit  prompt (note: on most implementations of Kermit the command is
     entered next to the prompt).  Commands can be entered in either  upper
     or  lower  case,  and  may  be abbreviated to a minimum of 1 character
     (depending on command).

       Some of the commands will require parameters to be entered as  well,
     these  should be typed after the command and should be separated by at
     least one space, except for filenames which must be enclosed by quotes
     (").  The parameters can be of various types, a filename, a character,
     a numeric value, or an item from a  list.  In  the  case  of  the  SET
     command  two  sets  of parameters are required, firstly the item to be
     set, and secondly what it is to be set to.










                                     - 7 -










       The question mark (?) can be used  to  give  useful  information  on
     commands,  if  entered  as  a  command  all the legal commands will be
     displayed, and if entered as a parameter the type of parameter will be
     displayed.

       send ?                                           <- You enter.
       SEND "Source filename" <"Destination filespec">  <- Kermit replies.
      Where '<' and '>' denote an optional item.

      If the required parameter is an item from a list the alternatives are
     all displayed, also note that list items can  be  abbreviated  in  the
     same way as commands.

       set flow ?                                       <- You enter.
       FLOW-CONTROL - NONE, XON/XOFF, DTR/RTS           <- Kermit replies.


      3.3 HP86 KERMIT COMMANDS
      ------------------------

        The following is a list of valid commands for the HP86 with a brief
     description of each, they will be explained in more detail  in  latter
     chapters.

       Command  Parameters  Description

       CONNECT               Sets the  HP86  to act as a  terminal to allow
                             communication with the remote host.

       SEND     "source filename" <"dest filespec">
                             Send  the  specified file  to the remote,  the
                             file name that is  used by the remote can also
                             be specified, if required to be different from
                             the source file name.

       RECEIVE  <"dest filename">
                             Receive  a file,  or group of files,  from the
                             remote, changing filename if required.

       SET      List option  Parameter
                             Set specified option  to a new value,  used to
                             change communication settings, timeouts, retry
                             limit etc. Requires extra parameter(s) after
                             the option.

       SHOW     List option  Displays  current  setting  of  the  requested
                             option,  if  no  option  is specified  all the
                             settable parameters will be displayed.

       EXIT                  Both these commands will cause the HP86 Kermit
       QUIT                  to stop,  and return the  HP86  to the command
                             state.


                                     - 8 -











       CAT                   This command will  produce a  catalogue of the
                             current disk.

         As  well as the above commands it is also possible to use the HP86
     filing system commands in the following way:

       <PAUSE>                       <- Press the PAUSE key.
       Warning 101 at line 0 : XFR   <- The HP86  gives  a warning  that an
                                        input transfer  from the  RS232  is
                                        still in progress.

       Any of the HP86 filing system  commands  can  now  be  entered,  for
     example:

       PURGE "GARBAGE"               <- Erase the file called "GARBAGE"

         Once  finished  entering  commands  to the HP86 the Kermit program
     should be restarted:

       <CONT>                        <- Press the continue key
       ?                             <- The  HP86  replies  with this,  the
                                        next  Kermit command  should now be
                                        entered under this prompt.


      3.4 USING KERMIT
      ----------------

       To use Kermit to transfer data you will need a  Kermit  program  for
     both  the HP86 and the other computer, the actual procedure to be used
     depends on whether the other computer is a microcomputer with its  own
     keyboard,  or  a  minicomputer  or  mainframe that needs a terminal to
     communicate with it.

       For HP86 to microcomputer transfer the method is very simple,  after
     making  any  connections  load  and  run  the  Kermit programs in both
     computers, then using the SET command the RS232 interfaces  should  be
     set  to  appropriate values (see chapter 4). Once all the settings are
     correct transfer can begin, enter the RECEIVE command on the  computer
     to  which  the  data is to be sent, then enter the SEND command on the
     sending computer, the transfer will now take place.

       For HP86 to minicomputer or mainframe transfer a slightly  different
     approach  is  needed,  after  physically  connecting  the  HP86 to the
     computer the HP86 Kermit is run and any communication  settings  made.
     The  HP86  should  now  be  put  into terminal emulator mode using the
     CONNECT command, then using the HP86 as a terminal you should  log  on
     to the computer and run its Kermit program. To transfer data you enter
     the  required  command  on  the  remote,  either SEND or RECEIVE, then
     escape back to the HP86 Kermit (using k1 - see chapter 4),  and  issue
     the complimentary command.


                                     - 9 -










         After  the transfer is completed connect back to the remote, if no
     more transfers are required exit from the  Kermit  program,  log  off,
     escape back to the HP86 and exit from its Kermit program.

         Both  these  methods will be discussed in more detail in chapter 5
     'Transferring files by Kermit'.


      3.5 FINISHING KERMIT
      --------------------

       Once you have finished using Kermit  for  your  file  transfers  you
     should  exit  from  the  program  by using either the EXIT or the QUIT
     command, either of these  will  halt  any  RS232  transfers  that  are
     active,  close  any  open files and leave the HP86 in a suitable state
     for further use.  If you wish to enter a new program via the  keyboard
     you  should use the SCRATCH command to clear the memory, as the Kermit
     program is still present.




































                                     - 10 -










      4. COMMUNICATING WITH ANOTHER COMPUTER
      ======================================

       This section describes how to set up the HP86 Kermit so that it  can
     communicate  with  another  computer,  the  remote  host. it will also
     outline how to use the terminal emulation facility when the remote  is
     a mainframe computer.

      4.1 SETTING THE RS232
      ---------------------

         Once  the  HP86  is physically connected to the remote (if you are
     unsure of how to do this contact your system support  personnel),  you
     should  now set up the RS232 interface so that it can communicate with
     the remote host. There are four separate settings that may have to  be
     changed  these  are  Baud  rate,  parity,  duplex  and flow control or
     handshake (depending on duplex setting).  All  the  changes  are  made
     using  the  SET  command  and  the existing settings can be determined
     using the SHOW command.

     BAUD RATE     110, 300                           Default 300
       This is the rate that the data is transmitted along the RS232  link,
     at present only two rates are allowed 110 or 300 baud.

     PARITY        NONE, ODD, EVEN, MARK, SPACE       Default MARK
         This  is the parity that will be used by the RS232 interface, this
     can be none, odd, even, mark or space, if none is chosen all 8 bits of
     a byte will be sent, otherwise only the bottom 7 are used.

     DUPLEX        FULL, HALF                         Default HALF
       This defines whether the remotes communication equipment can receive
     at the same time as it is transmitting, full duplex operation, or  can
     only  receive  whilst not transmitting, half duplex. Setting this will
     also change the local echo setting, if set to full duplex  local  echo
     will  be  switched  off, is set to half duplex it will be switched on,
     this can be changed with SET LOCAL-ECHO.

     FLOW-CONTROL  NONE, XON/XOFF, DTR/RTS            Default NONE
       Defines the method the remote uses to stop the HP86 transmitting any
     more data, to stop its buffers overflowing. The possible settings  are
     none, XON/XOFF for software flow control using control codes 17 and 19
     (XON,XOFF),  and  DTR/RTS  for hardware flow control using the DTR and
     RTS control lines. Setting this to any setting other  than  none  will
     set handshake to none.










                                     - 11 -










     HANDSHAKE     NONE, BELL, LF, CR, XON, XOFF      Default XON
         Defines the character to be used as a handshake character for half
     duplex  communications,  the  handshake  character  is  used  by  both
     computers  to  indicate  that they have finished transmitting and that
     the other  can  now  transmit,  this  is  sometimes  called  the  line
     turnaround  character.   The possible option are none, bell (ASCII 7),
     linefeed (ASCII 10), carriage return (ASCII 13), XON  (ASCII  17)  and
     XOFF (ASCII 19).

       To change any of these settings use the SET command in the following
     manner:

       KERMIT-HP86 > Enter command ?  <- Underneath the prompt  type in set
       set flow-control xon/xoff         followed by the options.
       FLOW-CONTROL - XON/XOFF        <- Kermit  will respond with  the new
                                         setting if it is accepted.
         Note  that  the options can be abbreviated for ease of typing, for
     instance the above could have been entered as set flow xon.

       The settings can be determined using the SHOW command, if no  option
     is  specified  the  screen  will  display  the settings of all the set
     options, otherwise specify the particular option:

       KERMIT-HP86 > Enter command ?
       show parity                    <- Enter command
       PARITY - MARK                  <- Kermit responds  with  the current
                                         setting.

       The actual settings needed will depend on the machine that you  wish
     to communicate with, you will need to know what its settings are.

       If you are linking to another microcomputer you will need to set the
     RS232  options to the same on both machines. The simplest method is to
     set the options on one machine to the default settings of  the  other,
     depending  if  this can be done, for instance if the other micro has a
     default Baud rate of 1200, which can not be set on  the  HP,  set  its
     Baud rate to 300. An alternative approach is to set each option to the
     'best'  that  can  be  set on both machines, ie the highest Baud rate,
     full duplex, hardware flow control, and no parity (to allow 8 bit data
     communication with no encoding).

       When connecting to a mainframe computer you will be limited  to  the
     standard operating on that computer, the default settings are designed
     to  operate  with an IBM 4341 on a 300 baud line, your Systems Support
     staff should be able to tell you what settings  are  needed  for  your
     installation.








                                     - 12 -










      4.2 USING THE HP86 AS A TERMINAL
      --------------------------------

         As mentioned before when transferring files between the HP86 and a
     minicomputer or mainframe you will need to communicate with the remote
     by using the HP86 as a terminal, to achieve this you  should  use  the
     CONNECT command.

      4.2.1 THE CONNECT COMMAND
      -------------------------

         The  CONNECT command needs no parameters and can be abbreviated to
     'C', once entered the HP86 will  clear  the  screen  and  display  the
     following information:

       HP86 Kermit - Terminal emulation mode
       Function key   Escape character   Action
       --------------------------------------------------
          k1                 C           Return to Kermit
          k7                 B           Transmit break
          k14                            Enable transmit

       The above display indicates the action of various function keys, and
     the  corresponding  escape key sequences (Ctrl-] + character).  At the
     bottom of the screen a cursor will be displayed,  this  is  where  any
     keyboard input will appear.

         The HP86 will now act like a 'glass' teletype, characters typed on
     the keyboard will be  sent  directly  to  the  remote  via  the  RS232
     interface, and characters received from the RS232 will be displayed on
     the screen.

      4.2.2 DIFFERENCES BETWEEN COMMAND MODE AND TERMINAL MODE
      --------------------------------------------------------

         There are important differences in the way the keyboard and screen
     are handled in the terminal mode compared to  the  normal  HP86  entry
     mode, these are as follows.

         All of the special keys, cursor keys and screen control keys cease
     to have any effect, except for the  ENTER  key,  RESET  key,  and  the
     defined function keys.  Pressing the ENTER key sends a carriage return
     (Control M)  to  the  remote,  in addition if a handshake character is
     specified it will also be sent and the transmitter will  be  disabled.
     The  RESET key performs its normal function of halting the program and
     resetting interfaces.








                                     - 13 -










       The delete key may not have any  effect,  depending  on  the  remote
     system, even if accepted the action on the screen will differ, instead
     of  the  last  character typed being removed from the screen, a delete
     character will be displayed  after  it.    Some  remotes  will  use  a
     different  key  for  this  purpose, for instance the IBM uses '_' as a
     delete character, you  will  be  able  to  find  this  from  the  user
     documention on using terminals.

         If  there is any handshake or flow control specified there will be
     times when the keyboard does not respond due to the transmitter  being
     disabled,  with  half duplex systems this will occur immediately after
     pressing the enter key and  will  remain  until  the  remote  finishes
     transmitting  data  and sends the handshake character. If the keyboard
     is not responding and the remote is  not  transmitting,  or  about  to
     transmit,  the  transmitter can be re-enabled by pressing function key
     14.

      4.2.3 SENDING A BREAK
      ---------------------

       Many mainframe computers may need to be sent a  'Break'  signal  for
     certain  reasons,  usually to interrupt the current program and return
     to the command state. You can send a break from the HP86 Kermit either
     by pressing function key 7, or by typing control ] followed by B.

      4.2.4 RETURNING TO THE HP86 KERMIT
      ----------------------------------

       When you have finished issuing the required commands to  the  remote
     Kermit  or you have finished your session on the remote, you will need
     to return to the HP86 Kermit's command mode, this  is  achieved  using
     function key 1, or control ] plus 'C'. On returning the screen will be
     cleared  and the standard Kermit prompt will be displayed.  If you are
     unsure what mode  you  are  in  examine  the  prompt,  if  it  is  not
     'KERMIT-HP86 > Enter command ?' then you are in terminal mode.



















                                     - 14 -










      5 TRANFERRING FILES USING KERMIT
      ================================

         The  main  purpose  of  the HP86 Kermit is to enable file transfer
     between the HP86 and another computer,  the  remote  host.  The  basic
     method  will not vary from one system to another as this is defined in
     the Kermit  protocol,  however  certain  details  will  be  different.
     Before  attempting any file transfer you should consult the user guide
     for the remote system to familiarise yourself  with  any  differences.
     This  section  describes  in  detail how to transfer files between the
     HP86 and the remote computer.


      5.1 THE BASIC METHOD
      --------------------

       To transfer files using Kermit you will need another Kermit  program
     running in the remote host, and you will need to issue commands to it.
     For  HP86 to microcomputer transfers this can be done simply by typing
     the required commands on the respective keyboards, however for HP86 to
     mainframes or minicomputers a more complex approach is needed.

      1. Load and run the HP86 Kermit, change any RS232 settings to  enable
         the  HP86  to  communicate  with  the  remote,  and  set any other
         parameters needed for the transfer.

      2. The HP86 is put into terminal mode using the CONNECT command.  Now
         with the HP86 acting as a terminal the user should log on  to  the
         mainframe in the normal manner.

      3. The  Kermit  program  on the remote should now be run, and any SET
         commands entered.

      4. To transfer files the relevant  command  should  now  be  entered,
         RECEIVE  for  HP86  to  remote,  SEND  for  remote  to HP86. After
         entering the command return to HP86 Kermit command mode  using  k1
         and  enter  the  complimentary  Kermit  command,  SEND for HP86 to
         remote, RECEIVE for remote to HP86.

      5. After the transfer is complete re-enter terminal mode to  set  the
         remote's  Kermit for any further transfer, or if you have finished
         all your transfers you should log out from the remote.

       The above description is only a guide to the sequence of actions  to
     be  taken,  you may not need to set any parameters, or you may wish to
     run some other program on the remote using data transferred by Kermit.








                                     - 15 -










      5.2 FILE TYPES
      --------------

       Before any discussion of file transfer it is  necessary  to  outline
     the   types  of  files  that  can  successfully  be  transferred  with
     HP86 Kermit version 1.00.  Due  to  version 1.00  being   written   in
     HP86 BASIC  the  ideal  of  being  able to transfer any file cannot be
     implemented.  The restrictions imposed by HP86 BASIC are quite  severe
     and  can only be overcome by various forms of file conversion. Because
     of the limitations it is advisable to  thoroughly  read  this  section
     before attempting any file transfer.

      5.2.1 THE FILE TYPE PROBLEM
      ---------------------------

        When a file is created by the HP86 it is assigned a particular type
     depending on its use and method of generation, these are as follows:-

       PROG - BASIC program created using the STORE command.
       BPGM - Binary program.
       DATA - Data file.
       GRAF - Screen dump.
       **** - Extended file.

      Of these only those of type DATA can be sent using  version  1.00  of
     Kermit,  this  being the only type that can be accessed by HP86 BASIC.
     Fortunately a utility program 'GETSAVE' exists on the HP86  demo  disk
     which  will  save  BASIC  programs from memory as DATA files, and load
     DATA files as BASIC programs (or sections of programs).

       The file type can be discovered using the CAT command either  before
     running Kermit or whilst in the command mode.

          KERMIT-HP86 > ?
          cat                             <- Enter catalogue command
                                          .. HP replies with
          Name        Type  Bytes   Recs
          ------------------------------
          MYFILE      DATA    256      4
          PROGRAM     PROG    256      9
          UTILITY     BPGM    256      7

         If  the  type  displayed  is  not  DATA  then  the  file cannot be
     transferred  using  HP86 Kermit version 1.00,  if  this  is  attempted
     Kermit will return with an error.









                                     - 16 -










      5.2.2 THE DATA TYPE PROBLEM
      ---------------------------

       As  previously mentioned only files of type DATA can be sent via the
     present implementation of Kermit, however there  is  a  second  factor
     that can affect the success of any transfer, that of data types.
       The  HP86 like many other microcomputers stores data on its disks in
     two different formats depending on the variable type,  either  numeric
     or  string  data.  This  causes problems when sending data to a remote
     kermit for the following reasons:

       All data to be transferred via Kermit has to be either  ASCII  data,
     or binary data that can be converted to ASCII by 8-bit prefixing.

         HP86  BASIC  is unable to access data on disk as bytes, it must be
     read either as a string variable or as a numeric variable.

       Therefore if data in the numeric format is encountered it has to  be
     converted into ASCII before it can be sent. There is a mechanism to do
     this   in  the  HP86  Kermit  program,  however  this  method  is  not
     satisfactory for most transfers for the following reasons:

       The numeric variable will be converted to a  string  of  characters,
     the  number  of which depends only on the number of significant digits
     in the variable (for instance '1 ','10 ' and '10.04 '). The  resulting
     file will therefore have a irregular format that will make its use, by
     other computer systems or languages, very difficult.

         There  is  no method in the Kermit program of converting this data
     back  into  numeric  variables,  therefore  a  file  sent  using  this
     conversion  and  then  received back will be of a different format and
     almost definitely unusable.

      For these reasons it is advisable to convert any files to be sent  by
     kermit  so  that  any  numeric  variables  are stored as, or in, ASCII
     strings.  You should attempt to do this so the numbers are stored in a
     fixed format based on their range, this will enable  the  data  to  be
     reconverted  easily,  and  allow  it  to  be used as input to programs
     written in other languages, or on different computers.

      For example if the data was a list of temperatures between 0 and  200
     measured  with  and accuracy of 2 decimal places, a sensible choice of
     format would be XDDD.DD (where D is a digit  or  space  if  a  leading
     zero,  X  is a space), 10 of these numbers could then be placed in one
     string, producing records with the following format:

       12.15  54.72 112.39  23.54 178.01 107.10  93.42 121.34 154.81 133.04

       This would produce a file that could be  used  by  many  high  level
     languages,  for  instance  it could be read by a FORTRAN program using
     the following format statement - FORMAT (10(1X,F6.2)).



                                     - 17 -










       For a simple method of storing numeric data as formatted strings see
     appendix C.
       Please note that there is no way that you can  determine  whether  a
     file  contains  data of the correct type until you actually attempt to
     transfer it. The default condition for the HP86 Kermit  is  to  do  no
     conversion  of numeric data, if a numeric variable is encountered then
     the transfer will be halted and an error message displayed. To use the
     inbuilt conversion facility issue the following command:

         SET SEND-CONVERT ON

     It  must  be  emphasized  again  that  using  this   method   produces
     unpredictable  results,  also  in some circumstances an type error can
     still be produced.  For these reasons it is suggested that  it  should
     be  used  vary rarely, for files containing only a small proportion of
     non crucial numeric data.


      5.3 HP86 TO REMOTE FILE TRANSFER - THE SEND COMMAND
      ---------------------------------------------------

       To send a file from the HP86 to the remote Kermit you use  the  SEND
     command,  however  before  you  issue  this command you should set the
     remote in to receiving state. To set the remote up to receive  a  file
     you  use the RECEIVE command, the manner in which this is done depends
     on the type of remote.

      If the remote is a  microcomputer  simply  enter  RECEIVE  using  its
     keyboard then enter the SEND command using the HP86's keyboard.

       For  a mainframe or minicomputer remote host you will have needed to
     have logged on and started Kermit using terminal mode. While still  in
     terminal  mode issue the RECEIVE command. You should now return to the
     HP86 Kermit command mode  by  using  function  key  1  and  enter  the
     HP86 Kermit SEND command.

        Once the remote is in a state to receive files you should enter the
     SEND command, this has the following format:

       SEND "source filename" <"dest filespec">

       Where:

       "source filename"  Is the name  of the file to be  sent in  standard
                          HP86 format.

       "dest filespec"    Is the name  that you wish the file  to be stored
                          as on the remote computer.

       If only the source filename is specified the HP86 Kermit  will  send
     this name converted into a 'legal' Kermit format.



                                     - 18 -










        The HP86 will now start to send the named file to the remote Kermit
     the following screen display will be seen:

          ----------------------------------------------------------------
          I HP86 Kermit sending file                                     I
          I ------------------------                                     I
          I                                                              I
          I Sending 'myfile dat' as 'MYFILE.DAT'                         I
          I                                                              I
          I Current action : Sending initialise      Retries : 0         I
          I Packets sent     : 0               NAKs received : 0         I
          I Bytes sent       : 0k              Timeouts      : 0         I
          I                                    Bad packets   : 0         I
          I                                                              I

       The file will now be sent packet by packet  to  the  remote  Kermit.
     The  progress  of  the transfer will be displayed on the screen.  When
     completed the message 'Transfer successful' will be displayed and  you
     will be returned to command mode.


      5.4 REMOTE TO HP86 TRANSFER - THE RECEIVE COMMAND
      -------------------------------------------------

        Before discussing the method used to transfer files from the remote
     to the HP86 a serious problem needs to  be  highlighted.  Unlike  most
     filing systems the HP86 BASIC filing system is incapable of creating a
     file  without  knowing its size. Unfortunately there is no way for the
     HP86 Kermit to know the size of the file it is receiving. Due to  this
     problem  it  is necessary to inform the HP86 Kermit of the size of the
     file that it is to receive, to do this use the SET FILE-SIZE command.

       SET FILE-SIZE size

        Where size is the desired  file  size  in  kilobytes,  the  default
     setting is 10.

     If  FILE-SIZE  is  not  set  correctly  one of two problems can arise.
     Firstly if FILE-SIZE is set far larger than the actual size  you  will
     be  wasting  disk space.   Secondly and more seriously if FILE-SIZE is
     smaller than the actual size then the transfer will  be  aborted  when
     the file on the HP86's disk becomes full.

       To  avoid  both problems before receiving files find the actual file
     size by using the relevant command on the remote system, you can  find
     this  from the user documentation.  You may have to calculate the size
     in kilobytes from the record size and number of  records,  round  this
     figure  up  to  the nearest kilobyte.  Setting FILE-SIZE to this value
     will usually be sufficient.  Occasionally though this can be less than
     actually needed as the HP86 requires  an  extra  3  bytes  per  record
     stored, so for added safety when transferring large files increase the
     file size by 1.


                                     - 19 -











         As  you would expect, to receive files from the remote you use the
     RECEIVE command on the HP86 Kermit and the SEND command on the remote.
     The order the two commands are entered will depend again on  the  type
     of remote.

       For microcomputer to HP86 transfer: Issue the RECEIVE command on the
     HP86, then the SEND command on the remote.

         For  transfer from mainframe or minicomputer: First issue the SEND
     command to the remote whilst in terminal mode,  then  return  to  HP86
     command mode, and enter RECEIVE.

       The RECEIVE command has the following format:

         RECEIVE  <"dest filename">

         Where "dest filename" is the file name that the received file will
     be stored as, if not supplied the name sent by the remote Kermit  will
     be converted to a legal HP86 name.

         Once  entered the HP86 screen will clear and the following will be
     displayed:

          ----------------------------------------------------------------
          I HP86 Kermit receiving file                                   I
          I --------------------------                                   I
          I                                                              I
        * I                                                              I
          I                                                              I
          I Current action : Wait for initialise     Retries : 0         I
          I Packets received : 0               NAKs sent     : 0         I
          I Bytes received   : 0k              Timeouts      : 0         I
          I                                    Bad packets   : 0         I
          I                                                              I

       * Note the name of the file being received  will  not  be  displayed
     until that information has been received from the remote.

         When  the  HP86 Kermit receives the file header it will attempt to
     create a file with either the name supplied after the RECEIVE command,
     or with the name contained in the header (converted to HP86 form).  If
     the file already exists on the disk then Kermit will rename  the  file
     and attempt to store it again, the new name will be displayed.

       Receiving 'MYFILE.DATA' as 'MYFI00 DAT'

         The actual way the file is renamed depends on whether the name was
     supplied as a parameter to the RECEIVE command, or  contained  in  the
     file header, see the section on file name conversion for more details.




                                     - 20 -










      5.5 TRANSFER PROBLEMS
      ---------------------

         After  the transfer has completed the HP86 Kermit will display the
     'Transfer successful' message, however if an error has occured and the
     transfer has been halted a suitable message will be displayed.

     Timeout           -  Time limit exceeded   on sending or  receiving  a
                          packet, increase timeout and re-run.
     NAK received      -  A  negative  acknowledge packet was received from
                          the remote that caused  the  retry  limit  to  be
                          exceeded.
     Checksum error    -  A  garbled  packet  was received from the remote.
                          Check   communication   settings   and   physical
                          connections.
     Incorrect  packet  -  The remote Kermit has sent a packet which is not
                          the type that the HP86 expects.  This should only
                          happen if both Kermits  have  been  set  to  SEND
                          files,  try  again  being  careful  to  enter the
                          correct commands.
     Error message from remote
                       -  The remote Kermit has sent an  error  packet  the
                          contents of which will be displayed.
     Transfer aborted  -  Function key 1 was pressed during transfer.
     Other messages    -  The rest of the messages generated by Kermit will
                          be  errors  produced  by  the  filing  system for
                          instance 'File does not exist', these are  mostly
                          self   explanatory,   however  the  error  no  is
                          displayed so users can check the HP86 manual  for
                          more detailed descriptions (see also Appendix B).

         Sometimes on connecting back to remote, especially after an error,
     garbage is printed on the  screen.  This  indicates  that  the  remote
     Kermit  is  still  in receive or send mode, having missed the relevant
     error or break packet. To rectify this situation press the  enter  key
     until the remotes prompt reappears.


      5.6 FILE NAME CONVERSION
      ------------------------

         The Kermit protocol specifies that the file name of the file being
     sent should be transmitted in the file header packet, to  provide  the
     receiving Kermit with a name to store the file under. However the file
     name  has  first  to  be  converted  to  a  standard  format, although
     different from the HP86 format it is very similar  to  many  mainframe
     file specifications being of the following form:

        filename.filetype

           where filename and filetype can be of any length but can only be
     composed of digits or uppercase letters.


                                     - 21 -










     HP86 file specifications are of the form "XXXXXXXXXX",
                                           or "XXXXXXXXXX.volume",
                                           or "XXXXXXXXXX:msus", where

     XXXXXXXXXX      is a filename of up to 10 characters.

     volume          is the volume label of the disk containing XXXXXXXXXX.

     msus            is the device specifier of the disk drive containing
                     XXXXXXXXX (E.G. D700).

       HP86 file names may contain upper or  lower  case  letters,  digits,
     special  characters,  excluding period and colon, and imbedded spaces.
     Upper and lower case letters are not equivalent.

       Due the differences in the format of filenames it  is  necessary  to
     convert  names  used on the HP86 if they are to be sent to the remote,
     and likewise convert names received from the remote if they are to  be
     used on the HP86.

      5.6.1 HP86 to standard conversion
      ---------------------------------

         When  sending a file to the remote and a destination file name has
     not been specified the HP86 Kermit will convert  the  source  filename
     into a 'legal' Kermit name.
         The  way this conversion takes place is as follows:  All lowercase
     characters are converted to uppercase.  If the name  contains  one  or
     more  spaces  then  the  first space will be converted to '.', else if
     name contains one or more '_' characters then the first  '_'  will  be
     changed to '.'.  The name is now scanned for legal characters (0-9,A-Z
     & first '.') if any illegal character is found it will be removed from
     the  name.  If the resulting name contains no '.' the filetype '.DATA'
     will be added to the end.

       For example

         Statistics  would be converted to  STATISTICS.DATA
         TEST FILE     ''  ''    ''     ''  TEST.FILE
         Tst File 1    ''  ''    ''     ''  TST.FILE1
         TEST#1-00     ''  ''    ''     ''  TEST100.DATA

       The name that Kermit sends to the remote will be  displayed  on  the
     screen along with the source file name.










                                     - 22 -










      5.6.2 Standard to HP86 conversion
      ---------------------------------

       When receiving files without specifying a destination file name then
     a  reverse  conversion  occurs.  First the name is scanned for the '.'
     marker, if this does not exist then the name is used as it  is.    The
     HP86  name  is  then  constructed  using the first 6 characters of the
     filename, a space and then the first 3  characters  of  the  filetype.
     Thus:

         STATISTICS.DATA  would be converted to  STATIS DAT
         TEST.FILE          ''  ''    ''     ''  TEST FIL

         Note that a filename converted to Kermit format and then converted
     back will not necessarily be the same.

       5.6.3 File renaming
       -------------------

       When receiving files from the remote the situation  can  arise  that
     the  file  name  supplied,  or the converted file name from the remote
     will clash with a file already on the disk drive. To avoid losing data
     by overwriting the existing  file  the  HP86 Kermit  will  attempt  to
     rename  the  file. The method used for renaming depends on whether the
     name was supplied as a parameter for the RECEIVE command, or converted
     from the file header sent by the remote.

       For a supplied name the method is to add a two digit number  to  the
     end,  keeping  the  total  length  to  10 characters, this may involve
     writing over the last two characters.  The numbering will  start  from
     00  and  will  continue  until 99 after which an error message will be
     generated.

       For example:-
         MYFILE      would be renamed  MYFILE00
         STATISTICS    ''  ''   ''     STATISTI00
       If MYFILE & MYFILE00 existed then
         MYFILE      would be renamed  MYFILE01

       If the file name is one that has been received  and  converted  from
     the  file header packet then the renumbering is done at the end of the
     part that was the filename, keeping it to 6 characters or less.

       For example
         MYFILE.DATA is converted to MYFILE DAT and renamed MYFI00 DAT
         TEST.BASIC  ''    ''     '' TEST BAS    ''   ''    TEST00 BAS

       The result of either of these  methods  will  be  displayed  on  the
     screen, however the results should not be too radically different from
     the original to enable correct identification.




                                     - 23 -










      6. CHANGING KERMIT ATTRIBUTES
      =============================

        At various points throughout this manual it has been mentioned that
     certain attributes have needed to be changed, the specific cases being
     described. This chapter gives  a  more  detailed  description  of  the
     command used to change these attributes, the SET command.


      6.1 THE SET COMMAND
      -------------------

       The SET command has the following format:

         SET option parameter(s)

       Where
        option        The attribute that you wish to change.
        parameter(s)  The value(s) to set the option to.

        The parameter types will depend on the option specified, and can be
     a character, a numeric value, or an item from a list. The option  name
     can be abbreviated, as can the parameter if it is a list item.  Kermit
     will  respond  with  the  new  setting  or with an error message if an
     illegal value is entered.

       SET RETRY 7        <- Enter set command
       RETRY - 7          <- Kermit replies

       SET RETRY #        <- Set command with incorrect value.
       Illegal value - #  <- Kermit replies.

       If a question mark is entered instead of the parameter  then  Kermit
     will display either the expected parameter type, numeric or character,
     or display the list from which the parameter should be chosen.

       SET RETRY ?                             <- Set command query.
       Numeric value                           <- Kermit replies

       SET FLOW ?                              <- Set command query.
       FLOW-CONTROL - NONE, XON/XOFF, DTR/RTS  <- Kermit replies.













                                     - 24 -










      6.2 THE SHOW COMMAND
      --------------------

         This  command  is  used  to  display  the  current settings of the
     attributes, if entered with no option  then  all  settable  attributes
     will  be  displayed,  otherwise the setting of the specified option is
     shown.

       SHOW DEBUG   <- You enter.
       DEBUG - OFF  <- Kermit responds.


      6.3 SETTABLE ATTRIBUTES
      -----------------------

       There now follows a list of the  attributes  that  can  be  set  and
     displayed using the SET and SHOW commands.

     OPTION         PARAMETER TYPE      DEFAULT

     TIMEOUT        Numeric value       Default - 10 secs
                    The  length  of  time  the  HP86 Kermit will wait for a
                    packet from the remote before causing a timeout.

     RETRIES        Numeric value       Default - 10 retries
                    The number of times the HP86 Kermit will try to  resend
                    a packet.

     SEND-CONVERT   OFF, ON             Default - OFF
                    Defines  whether  numeric variables are to be converted
                    and sent as string data, if off numeric variables  will
                    cause the transfer to abort.

     DEBUG          OFF, ON             Default - OFF
                    If  set  to  on  then packets sent and received will be
                    displayed on the screen.

     PREFIX         Character           Default - #
                    Defines the character to be used for prefix encoding.

     END-OF-LINE    Numeric value       Default - 13
                    The ASCII value of  the  end  of  line  character  that
                    should be sent after each packet.

     RECORD-END     Numeric value(s)    Default - 13 10
                    Defines   the   sequence  of  control  characters  that
                    indicate the end of a record. This  will  be  added  to
                    strings  when  sending  files, searched for and removed
                    when receiving files.

     FILE-SIZE      Numeric value       Default - 10



                                     - 25 -










                    The size of the file (kilobytes) that will  be  created
                    when receiving files.

     RECORD-LENGTH  Numeric value       Default - 256
                    The  record  length  that will be used by the HP86 when
                    creating files, if matching record  lengths  on  remote
                    systems  add  3 bytes, the HP86 needs these extra bytes
                    when storing strings.

     NO-OF-RECORDS  Numeric value       Default - 40
                    The number of  records  of  the  file  created  by  the
                    RECEIVE   command,   setting  this  will  override  the
                    file-size, the resulting size being the  record  length
                    times  the no of records, setting file-size will change
                    this value.

     DUPLEX         FULL, HALF          Default - HALF
                    The duplex setting of the remote,  setting  this  value
                    alters  the setting of the local echo, FULL - OFF, HALF
                    - ON.

     LOCAL-ECHO     OFF, ON             Default - ON
                    Defines whether characters typed on the  keyboard  will
                    be  displayed  on the screen (ON), this only applies to
                    terminal mode.

     FLOW-CONTROL   NONE, XON/XOFF, DTR/RTS        Default - NONE
                    Specifies the  flow  control  method  to  be  employed,
                    setting   this  to  any  value  other  than  NONE  sets
                    HANDSHAKE to NONE.

     HANDSHAKE      NONE, BELL, LF, CR, XON, XOFF  Default - XON
                    Defines the handshake character to  be  used  for  line
                    turnaround,  setting  this to anything except NONE will
                    set FLOW-CONTROL to NONE.

     PARITY         NONE, ODD, EVEN, MARK, SPACE   Default - MARK
                    The parity to be used by the RS232 interface.
















                                     - 26 -










      Appendix A : HP86 KERMIT Capabilities
      =====================================


       The following is a list of Kermit capabilities, with information  as
     to whether they are supported by HP86 Kermit version 1.00.

       Local operation:                   Yes
       Remote operation:                  No
       Transfers text files:              Yes
       Transfers binary files:            No
       Wildcard send:                     No
       ^X/^Z interruption:                Yes
       Filename collision avoidance:      Yes
       Can time out:                      Yes
       8th-bit prefixing:                 No
       Repeat count prefixing:            No
       Alternate block checks:            No
       Terminal emulation:                Yes
       Communication settings:            Yes; duplex,  parity,  handshake,
                                               flow control
       Transmit BREAK:                    Yes
       IBM communication:                 Yes; default settings
       Transaction logging:               No
       Session logging (raw download):    No
       Raw upload:                        No
       Act as server:                     No
       Talk to server:                    No
       Advanced commands for servers:     No
       Local file management:             Yes; CAT
       Handle file attributes:            No
       Command/init files:                No
       Printer control:                   No





















                                     - 27 -










      Appendix B : HP86 error messages
      ================================


         The following is a list of error messages that Kermit version 1.00
     will give if a transfer is aborted.

     Timeout receiving   The HP86 has timed out whilst waiting for a packet
                         from the remote.

     NAK received        The remote has sent a NAK causing the retry  limit
                         to be exceeded.

     Checksum error      The last packet received was garbled.

     Incorrect packet    The  wrong  packet type has been received from the
                         remote.

     Timeout sending     The HP86 has timed out whilst  trying  to  send  a
                         packet.

     Cannot rename file  The  file  being  received has the same name as an
                         existing file, but it cannot  be  renamed  as  the
                         number suffix is past 99.

     Disc write protected
                         The  disk  has a write protect label attached, the
                         file cannot be stored.

     File does not exist The file cannot be found on the disk.

     Incorrect file type The file cannot be sent as the file  type  is  not
                         DATA.

     Read error          There has been a read error on the disk.

     Record does not exist
                         The  file  has become full before all the data has
                         been received.

     No M.S. device      No mass storage device has been specified.

     Directory full      No more files can be stored on  the  disk  as  the
                         directory has become full.

     Volume not found    The specified volume name can not be found.

     MSUS not found      The specified mass storage device (disk drive) can
                         not be found.

     Read verify error   The data written to disk has been corrupted.



                                     - 28 -










     Disc full           The  disk  has  become  full,  or does not contain
                         enough space to create a new file.

     Medium damaged      The disk is faulty.

     Disc drive fault    The disc drive is not functioning  correctly,  can
                         be  caused  by leaving the latch on the disc drive
                         up.

     Data type error     The variable just read was a numeric variable  and
                         the data conversion facility is off.

     Transfer aborted    Function key 7 was pressed aborting the transfer.









































                                     - 29 -










      Appendix C : Converting numeric variables
      =========================================


         As  mentioned  in  the  section on file transfer numeric variables
     cannot be sent to the remote without conversion. Although a very basic
     conversion method is included  as  part  of  the  HP86 Kermit,  it  is
     advisable  not to use it but to convert the whole file into one usable
     by Kermit and the remote.

       To convert the file you will need to know the manner  in  which  the
     data  is  arranged  in the source file, and decide on a format for the
     converted file. The structure  of  the  source  file  can  usually  be
     determined  by  examining  the  program  that  created it, with a well
     documented program this task should be fairly  easy.  However  if  the
     creating  program  is not available, and the structure is unknown, use
     the HP86 BASIC TYP command.

       Once you have determined the structure  of  the  file(s),  and  have
     decided on a logical format to convert them to, you will need to write
     a  short  program  to  achieve this. The easiest way of converting the
     numbers into a useful format is to use  a  facility  provided  by  the
     HP86 I/O ROM.  The method involves defining a dummy I/O buffer, output
     the  numeric  variable  to this buffer using the formatting facilities
     (USING), and reading it back in as a string with the ENTER command.

       For example

         10 DIM dummy$"88"    <- Dimension  variable to  8 bytes  more than
                                 required size.
         20 IOBUFFER dummy$   <- Set it up as an I/O buffer
         .
         .
         .
         500 OUTPUT dummy$ USING "X,M4D.DD"; N  <- Output number  using the
                                                   specified format.
         510 ENTER dummy$ USING "K" ; N$       <- Read it in as a string.

















                                     - 30 -










       After converting the number to a string  it  can  either  be  stored
     separately,  or placed into another string along with others to form a
     record. The OUTPUT  command  can  be  used  to  construct  records  by
     outputting  more  than  one variable at once, or by outputting without
     end of line.

         500 OUTPUT dummy$ USING "XM4D.DD" ; N1,N2,N3,N4

       or
         500 FOR I=1 TO 10
         510 OUTPUT dummy$ USING "#,X,M4D.DD" ; N(I)  <- Output without EOL
         520 NEXT I
         .
         .   As there is now no  EOL sequence  at the end of the buffer the
         .   following statement would be needed to read this back.
         .
         530 ENTER dummy$ USING "#,#K" ; R$           <- Enter without EOL

       The complete record string can now be written to the disk file.

       As can be seen this is a very simple method of  producing  formatted
     files which can be sent using the HP86 Kermit. Also with a bit of care
     these  files  could  be  used  as  input  to programs written in other
     languages than BASIC. The reverse conversion is also easy  to  perform
     using the ENTER command:

         500 OUTPUT dummy$ ; R$  <- Output the string to the dummy buffer
         510 FOR I=1 T0 10
         520 ENTER dummy$ USING "#,X,M4D.DD" ; N(I) <- Get number
         530 NEXT I

         All  the  above conversion techniques can of course be included in
     other programs, if it is invisaged that the data files produced by the
     program will be transferred to another system using Kermit.  Including
     an option to produce files in 'Kermit' format is more  efficient  than
     having separate conversion programs.

         The  above  discussion  does  not  include  any  details  of image
     specifiers and other related matters, if you wish to use  this  method
     of  data  conversion  you  are strongly advised to read the section on
     Formatted I/O operations in the HP86 I/O Programming guide.













                                     - 31 -